| Input contribution Use case |
| --- |
| Use Case Title:* | Use cases for taxi advertisement |
| Group Name:* | WG1 |
| Source:* | CMCC |
| Contact: | Yawen Niu (niuyawen@chinamobile.com) |
| Date:* | 2014-09-23 |
| Abstract:* | Propose to add the use case for taxi advertisement of TR 0001. For taxi advertisement device, it is required to limited network access based on time. |
| Agenda Item:* |  |
| Work item(s): | WI 0015 - oneM2M Use Case Continuation |
| Document(s) Impacted* | Technical Specification TR 0001 - oneM2M Use Case Technical Report |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval of the Use Case |

oneM2M IPR STATEMENT

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## Title

### Use cases for taxi advertisement.

## Description

## For the taxi advertisement device, it does NOT need to access to the network during the day when the network is busy (e.g. from 8:00 to 23:00), but need to access the network at night when the network is idle (e.g. from 23:00 to 8:00) to download a large number of advertisement data.

## Source

### CMCC

## Actors

### Taxi advertisement device, which can download advertisement data from advertisement data server through M2M service platform and show to passengers.

### The M2M service platform, which can control the taxi advertisement device and its access to the network

### Advertisement data server, which can provide advertisement data for the  advertisement device to download

## Pre-conditions

### The taxi advertisement device and the advertisement data server registered to the M2M service platform.

## Triggers

### The taxi advertisement device accesses to the advertisement data server though M2M platform to download data.

## Normal Flow

## The taxi advertisement device accesses to the advertisement data server through M2M platform.

## The M2M service platform checks the time policy. If current time is permitted, it allows the device to access the advertisement data server. Otherwise, it denies access and instructs the taxi advertisement device not to access the advertisement data server until the time when access is permitted.

## When access is permitted the taxi advertisement device downloads data from advertisement data server.

## Post-conditions (if any)

### NONE.

## High Level Illustration (as applicable)

## Potential requirements (as applicable)

- The M2M service platform shall be able to support the time-based policies to access the Underlying network.