| Input contribution Use case |
| --- |
| Use Case Title:* | Use Case on Vehicle Data Services |
| Group Name:* | WG1 |
| Source:* | Toyota InfoTechnology Center, KDDI, Fujitsu |
| Contact: | Ryokichi Onishi, Toyota InfoTechnology Center, onishi@jp.toyota-itc.com Nick Yamasaki, KDDI, nr-yamasaki@kddi.com Shingo Fujimoto, Fujitsu, shingo_fujimoto@jp.fujitsu.com Joerg Swetina, NEC, Joerg.Swetina@neclab.eu |
| Date:* | <2014-10-30> |
| Abstract:* | This use case introduces several services based on various data collected and published by sensor devices via smart vehicle as M2M Gateway. |
| Agenda Item:* |  |
| Work item(s): | WI 0015 - oneM2M Use Case Continuation |
| Document(s) Impacted* | TR-0001 - oneM2M Use Case Collection |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Accept this use case. |

oneM2M Notice

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## Title

### Use Case on Vehicle Data Service

## Description

### This use case introduces several services based on various data collected by sensor devices via smart vehicle (vehicle with on-board communication system) which is regarded as M2M gateway.

### The sensor devices may be located in the vehicle but may also be located outside the vehicle, e.g. on the road side. Some sensor devices are equipped with M2M area network module and measure individual data. The smart vehicle connects to the sensor devices and collects data from sensor devices by using the M2M area network technology such as Wireless LAN, ZigBee, Bluetooth, etc., and sends the data to application server in infrastructure domain via mobile network.

### Management server and Application Server in the M2M infrastructure domain connect to the smart vehicle via a mobile network in order to control its configurations updating software and exchanging M2M data (e.g. updating a map).

### It is important to observe that the smart vehicle as M2M gateway has mobility. For instance, there are possibilities for a mobile device to simultaneously connect to many sensor devices, and to newly connect to sensor devices which have never been connected before.

### This use case illustrates potential requirements from the use case of services utilizing mobile device.

## Source

### Toyota InfoTechnology Center, KDDI, Fusjitsu, NEC (TTC)

## Actors

### M2M Device: In-vehicle sensor device and outdoor sensor device. In-vehicle sensor includes on-board(built-in) sensor used for monitoring of machine health and also sensor on user carry-on device, such as smart phone and wearable device like Fitbit™, Nike Fuelband™, Sony SmartBand™ for example. In-vehicle sensor may monitor status of machine health(diagnosis), mobility, passenger’s health and environment. Outdoor sensor device may be located outdoor and monitor roadway infrastructure, agriculture, property (surveillance) and utility (telemetering), for example. It may be equipped with several kind of communication protocol.

### M2M Area Network: Area network which connects M2M Device with M2M Gateway and also provides connectivity among M2M Gateways. It may include Wireless LAN, Bluetooth, ZigBee and Ethernet.

### M2M Gateway: On-board communication system equipped on the smart vehicle, which communicates with M2M Devices and other M2M Gateways via M2M Area Network and also communicates with Application Servers and Management Servers via Mobile Network.

### Mobile Network: Network which has functions to transfer data and control messages between M2M Gateway and M2M Application Server/Management Server. It may include cellular base station.

### M2M Management Server: Server which manages M2M applications in M2M Gateway and M2M Device by installing, uninstalling and updating them.

### M2M Application Server: Server which maintains database and  provides the data access services such as accepting data publication from and issuing data subscription to M2M Gateway/Device. This server also manages non-M2M applications such as navigation system as well as contents such as map data in M2M Geteway and M2M Device by installing, uninstalling and updating them.

## Pre-conditions

### It is possible to establish a connection among M2M Application Server, M2M Management Server and Smart Vehicle via Mobile Network.

### It is possible to establish a connection between Smart Vehicle and M2M Device and among Smart Vehicles via M2M Area Network.

### The M2M Gateway has been configured by the M2M Management Server.

### The has not yet been configured by the M2M Management Server.

## Triggers

### Subject to capabilities of the M2M Area Network, the M2M Device detects a M2M Gateway that can be associated, or vice versa. The association  may require explicit operation (permission) for that association by users (e.g. owners of Gateway and/or Device) or administrator (a manufacturer of Gateway and/or Device and/or Management Server). Examples are below:

### Sensors are built into the smart vehicle at the factory (Permanent Association, no triggering is needed).

### Sensors are equipped to the smart vehicle after market, e.g. at auto dealers or auto parts stores. Triggering occurs when the smart vehicle is being equipped with the new sensor

### Users bring sensors with user carry-on devices into the smart vehicle.

### The smart vehicle detects nearby outdoor sensors.

### The smart vehicle detects other smart vehicles nearby.

## Normal Flow

### M2M Configuration step: Management Server configures M2M Device

### Upon triggering, i.e. when the M2M Device detects a M2M Gateway that can be associated or the M2M Gateway detects a M2M Device that can be associated the following sequence is initiated:

### M2M Gateway establishes a connection to M2M Device (or the M2M Device establishes the connection to the M2M Gateway) via the M2M Area Network.

### M2M Device sends its attribute information (e.g. type of device, service certificates of the device, required application software, etc.) to the M2M Gateway.

### M2M Gateway establishes a connection to the M2M Management Server via Mobile Network.

### M2M Gateway relays the attribute information to Management Server.

### M2M Management Server provides M2M Gateway with the appropriate software and configuration data for the M2M Device.

### M2M Gateway relays the software and configuration data to M2M Device.

### M2M Device configures itself according to the software and configuration data.

### Transmission of data between M2M Device and M2M Application Server

### Data Publication of M2M Device

### M2M Gateway (re-)establishes a connection to M2M Device via M2M Area Network.

### M2M Device publishes measured data to M2M Gateway.

### M2M Gateway establishes a connection to M2M Application Server via Mobile Network.

### M2M Gateway relays the data to M2M Application Server.

### M2M Application Server receives the data.

### Data Subscription from M2M Application Server

### M2M Gateway establishes a connection to M2M Application Server via Mobile Network.

### M2M Application Server sends M2M Gateway attribute information of data in need.

### M2M Gateway (re-)establishes a connection to M2M Device via M2M Area Network.

### M2M Gateway relays the attribute information to M2M Device.

### M2M Device publishes measured data that meets the attribute information to M2M Gateway.

### M2M Gateway relays the data to Application Server.

### Application Server receives the data.

### Update of non-M2M Application 1: M2M Application Server and M2M Gateway

### M2M Gateway establishes a connection to M2M Application Server via Mobile Network.

### M2M Gateway sends its attribute information to M2M Application Server.

### M2M Application Server provides M2M Gateway with the appropriate software, its configuration data and contents such as map.

### M2M Gateway configures itself according to the software, configuration data, etc.

### Update of non-M2M Application 2: M2M Application Server and M2M Device

### M2M Device establishes a connection to M2M Gateway via M2M Area Network.

### M2M Device sends its attribute information to M2M Gateway.

### M2M Gateway establishes a connection to M2M Application  Server via Mobile Network.

### M2M Gateway relays the attribute information to M2M Application Server.

### M2M Application Server provides M2M Gateway with the appropriate software and configuration data.

### M2M Gateway relays the configuration software and data to M2M Device.

### M2M Device configures itself according to the software and configuration data.

### Alternative flow 1

### This alternative flow may occur in the case where the M2M Gateway only occasionally connects to devices and servers – e.g. via M2M Area networks that can only occasionally be used.

### M2M Gateway Opportunistic Communication (Store and Forward)

### M2M Gateway may store data that are destined to M2M Device, M2M Management Server and M2M Application Server.

### M2M Gateway may send the stored data to other M2M Gateway.

### Both, the originator and the other M2M Gateway may deliver the stored data to the destination when connected.

### M2M Gateway may erase the stored data that has been already sent to the destination.

### Alternative flow 2

### This variant flow may occur in the case where the M2M Gateway processes the data flow between M2M Gateway and M2M Application Server.

### M2M Gateway Data Processing

### M2M Gateway may aggregate, statistically summarize (e.g. average) and/or erase data based on criteria that are indicated in the data subscription or the configuration data from M2M Application Server.

### Alternative flow 3

### This variant flow may occur in cases where the M2M Gateway broadcasts its interest to subscribe to specific data to all M2M Devices in its vicinity.

### M2M Gateway Cross Layer Optimization

### M2M Gateway may indicate a full or part of data subscription (attribute information of data in need) in wireless pre-association information such as beacon.

### Smart Vehicle and Wi-Fi Hotspot may periodically broadcast beacon that contains the subscription in order to prevent sensor devices from establishing unnecessary connection and wasting radio resources as well as battery power.

## Post-conditions

### M2M Application Server stores data and provides data access service via API for user applications.

### M2M Devices and M2M Gateways are well maintained by M2M Management Server and M2M Application Server.

## High Level Illustration (as applicable)

### Potential requirements (as applicable)

### The M2M System shall enable discovery of M2M Application Servers, M2M Management Servers and M2M Devices available to a M2M Gateway for data exchange.

### The M2M System shall enable discovery of M2M Gateway available to a M2M Management Server and a M2M Device for data exchange.

### The M2M System shall be able to support the capabilities for data repository (i.e. to collect/store) and for data transfer from one or more M2M Devices or M2M Gateways, for delivery to one or more M2M Gateways via M2M Area Network without any assistance or instruction of M2M Management Servers and M2M Application Servers.

### M2M Gateway shall be able to statistically summarize (e.g. average) M2M data upon the request from M2M Application Server.

### M2M Gateway shall be able to erase M2M data and statistically summarized data upon the request from M2M Application Server.

### M2M Gateway and/or M2M Device shall be able to establish a connection to each other if M2M Device wants to publish data to M2M Gateway.

# Comments

NEC added

NEC added

Not limited to the same server.

I propose to remove the “non-M2M” section completely since it is not different to the “M2M” section.

I keep the “non-M2M” section since the M2M application server based management (non-M2M application/content/configuration update) is different from the one by the M2M management server. We assume the application server is different from the management server.

Not needed anymore since it is now already contained in the beginning of the flow.

OK

Averaging process and not limited to that

This needs to be more detailed. It is not clear what " statistically summarize " means

These ones

Which kind of data ?