| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG1 Requirements |
| Title:* | A use case for industry: On-demand data collection for factories |
| Source:* | Hitachi |
| Contact: | Yuichi Nakamura <yuichi.nakamura.fe@hitachi-solutions.com> |
| Date:* | 2014-10-31 |
| Abstract:* | This use case introduces data collection from production lines in factories where only necessary data are collected and the condition of data collection can be changed |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0012 |
| Document(s) Impacted* | oneM2M-TR-0001-Use Case Collection |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Title

### A use case for industry: on-demand data collection for factories

## Description

## In factories, a lot of data are created from PLCs every second and data are utilised to monitor production lines. In order to monitor remotely, data are gathered to M2M service platform. However, it is difficult to gather all data to M2M service platform because sometimes more than 1M bit data are created per second. In such cases, only necessary data are gathered depending on situations.

## Source

### Hitachi

## Actors

### PLC (Programmable logic controller):  It controls sensors and devices in a production line according to embedded programs. It also has interface to Real-time Ethernet. It broadcasts data related to the production line to Real-time Ethernet.

### Gateway: It bridges Real-time Ethernet and the Internet. It collects necessary data from Real-time Ethernet according to the configuration called data catalogue, and send collected data to M2M service platform.

### M2M service platform: It stores data gathered from gateway(s), and provide data to applications. It also manages data catalogue in gateway(s).

### Application: It monitors production lines by using collected data in M2M service platform, and send change request of data catalogue depending on situations.

### Real-time Ethernet: A technology standardized in IEC TC65. Ethernet is used at physical layer, but upper protocol is designed for industry purpose. In this use case, broad cast protocol is assumed. On top of Ethernet cable, data are broadcasted with ID. Address configuration is not necessary here.

### Internet connection: M2M service platform and gateway(s) are connected by the Internet physically.

## Pre-conditions

### PLCs and gateway are connected to Real-time Ethernet. PLCs broadcast data to Real-time Ethernet. Gateway is configured to pick up necessary data from Real-time Ethernet.

### On top of the internet, VPN connection is established between M2M service platform and gateway(s).

### The data catalogue is managed by M2M service platform

## Triggers

## Data catalogue is configured for gateway to pick up data in the Real-time Ethernet

## Normal Flow

## Gateway picks up broadcasted data. It picks up only data that matches condition described in the data catalogue. If data does not match the condition, gateway neglects the data.

## Gateway send collected data to M2M service platform.

## M2M service platform receives data and store.

## Application utilise the data. For example, it monitors the status of production line.

## If application user finds some trouble in a production line, he/she changes the data catalogue in M2M service platform to collect all data related to the production line, and sends the data catalogue to the target gateway.

## Post-conditions (if any)

### None

## High Level Illustration (as applicable)

## Potential requirements (as applicable)

- The gateway shall be able to collect data from field area network according to data collection policy stored in the gateway.

- The data collection policy shall be managed by M2M service platform