| CHANGE REQUEST |
| --- |
| Group Name:* | WG1 |
| Source:* | LG Electronics |
| Format:* | REQ#14 |
| Date:* | 2014-10-31 |
| Contact:* | Heedong Choi (heedong.choi@lge.com) |
| Reason for Change/s:* | Add Use Case of Message Profile |
| CR against: Release* | 1 |
| CR against: TS/TR* | TR-0013-V-0.1.1 |
| Clauses/Sub Clauses* | 6.2.x |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution is to introduce a use case for the message profile in the home domain envirionment.

## -----------------------Start of change 1-------------------------------------------

## 6.x	Use Case for Message Profile

### 6.x.1	Overview

#### 6.x.1.1	Description

To support a variety of smart home services, smart appliances as well as corresponding applications are installed in advance. The application is generally comprised of manufacturer-specific messages (e.g., on/off, brightness, volumn, strength, etc.) based on the appliance type (e.g., smart bulb, air conditioner, refrigerator, TV, etc.) and/or the model of the appliance type. Because the message description may necessarily different according to the manufacturer, the designated appliance is only controlled to by the application.

In the standardization, a “profile” is utilizied to enforce one interpretation. By using a profile, engineers can design or procure to ensure interoperability. Especially, one unified application based on the message profile can control all appliances by making rules of the message description. In this use case, the intruder detection in the home domain environment is introduced based on the message profile.

#### 6.x.1.2	Source

- LG Electronics

#### 6.x.1.3	Actors

- Home Appliance and Sensor

This is a M2M device which is controlled by the smart device.

- Home Server

This is an M2M platform that interacts with M2M gateway and smart device.

- Smart Device

This is a M2M devices such as smartphone and tablet device that controls the smart bulb.

#### 6.x.1.4	Pre-condition

- Message profile for the home domain is pre-defined.

(The following figure shows an example of the message profile for the home domain. The ‘Common Characteristic Sets’ specifies pre-defined characteristics and their properties such as power, brightness, color, etc. Each characteristic has an unique ID, type, format,value, etc. Also, ‘Applicable Device Sets’ specifies pre-defined services such as bulb, lock management, thermostat, etc. Each applicable device is comprised of characteristic(s).)

Figure 6.2-1 Example of Message Profile

- Two smart bulbs and the motion sensor are registered with a home server. Here, each smart bulb is produced by a different manufacturer.

- The smart device discovers the registered smart bulb and the motion sensor from the home server.

#### 6.x.1.5	Triggers

- None

#### 6.x.1.6	Normal Flow

A variety of home appliance and devices are utilized for the intruder detection service in the home domain environment. According to the service scenario, the generated information is collected to the home server. Then, the countermeasure is provided based on the collected information.

In this scenario, the service configuration includes the message profile for the home domain. It means that one unified application for applicable devices can simultaneously control without additional application installation.

Based on the configuration information, the motion sensor detcts a movement and it reports the home server due to the subscription. Later, the home server notifies the changed status to the smart device and a waning service is provided by using smart bulbs.

#### 6.x.1.7	Post-conditions

- None

#### 6.x.1.8	High Level Illustration

Figure 6.2-2 High Level Illustration - Message Profile

### 6.x.2	High Level Analysis

#### 6.x.2.1	Functional Impacts

Figure 6.2-3 High Level Illustration of Functional Impact - Message Profile

- In oneM2M configurations, the smart bulb and the motion sensor can be interpreted as ADN-AE. The home gateway and server can be interpreted as MN-CSE and IN-CSE, respectively. Also, smart device can be interpreted as ADN-AE.

#### 6.x.2.2	High Level Information Flows

Figure 6.2-4 High Level Information Flows - Message Profile

- 000:In this information flow, assume that the message profile for the home domain is pre-defined. Therfore, the smart bulb (ADN-AE1 and ADN-AE2) and the motion sensor (ADN-AE3) send the information as sets of pre-defined message. The below steps are operated by using the pre-defined message.

- 001: The smart device (ADN-AE4) subscribes to changes of information about the motion sensor (ADN-AE3) for the intruder detection service.

- 002: Since the motion sensor (ADN-AE3) detects a movement, it reports the changed status as pre-defined message to the home server (IN-CSE) via the home gateway (MN-CSE).

- 003: The home server (IN-CSE) notifies the changed status to the smart device (ADN-AE4).

- 004: To give a warning, the smart device (ADN-AE4) turns on smart bulbs (ADN-AE1 and AND-AE2). (Although two smart bulbs are produced differenct manufacturer, they are simultaneously controlled.)

- 005: Nevertheless, the motion sensor (ADN-AE3) continuously detects a movement, it reports the changed status as pre-defined message to the home server (IN-CSE).

- 006: The home server (IN-CSE) notifies the changed status to the smart device (ADN-AE4).

- 007: To give a stronger warning, the smart device (ADN-AE4) changes to smart bulbs (ADN-AE1 and ADN-AE2).

### 6.x.3	Potential Requirements

- The oneM2M System shall support a message profile for one interpretation of the message description in the home domain environment.

## -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?