| Input contribution Use case |
| --- |
| Use Case Title:* | Use case for automatically switching between remote access and local access |
| Group Name:* | WG1 |
| Source:* | Haier |
| Contact: | Jun Zhang, Haier, zhangjun@haierubic.com Yali Guo, Haier, guoyali@haierubic.com |
| Date:* | 2015-01-12 |
| Abstract:* | Propose to include the use case for Home Domain Enablement TR. |
| Agenda Item:* | TBD |
| Work item(s): | WI 0017 – Home Domain Enablement |
| Document(s) Impacted* | Technical Specification TR 0013 – Home Domain Enablement TR |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval of the Use case for the Home Domain Enablement TR |

oneM2M IPR STATEMENT

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## 6.x	Use case for automatically switching between remote access and local access

### 6.x.1 Overview

#### 6.x.1.1 Description

### In smart home system, it is very common that the mobile devices such as smart phones play the role of home controller to access and control home appliances operating in the local home network. It is very likely that the home controller moves in and out of the home network as the user moves, e.g., when the user stays at home, the home controller is connected to the same local network as the home appliances, or when the user takes a walk in the park, the home controller disconnects from the local home network. However, it is necessary to guarantee that home appliances can be controlled by the home controller regardless of where the home controller is.

### In the gateway-centric smart home system, the smart home gateway can be configured as the smart home centre which manages local access of home appliances through home gateway and also enables remote access of home appliances through the cloud server.

### When the home controller is out of the local home network, it communicates with the home appliances through the cloud server. But when the home controller returns to the local home network, normally the smart home user prefers to control home appliances directly through the home gateway.

### The user experience would be bad if this feature is supported based on the user’s manual switch. To meet the user’s requirement of automatically switching between local access and remote access, in this use case, the user preference can be configured as enabling local access when the home controller is connected to the local home network and enabling remote access when the home controller disconnects from the local home network. So when the user is at home, the home controller performs local access mode to control home appliances through the home gateway. When the user goes out, the home controller automatically switches to the remote access mode to control home appliances through the cloud server and when the user get home, the home controller automatically switches to the local access mode again.

### This use case provides an easy way for the user wherever he is to  control home appliances according to the user preference.

#### 6.x.1.2 Source

### Haier (CCSA)

#### 6.x.1.3 Actors

### Home appliances

### are networked home appliances such as smart air conditioner, smart refrigerator, smart washing machine, smart plug, smart lighting, etc.

### Home gateway

### is an oneM2M enabled smart home centre in the home domain, used to manage home appliances registered with the home gateway.

### Home Controller

### is an oneM2M device that manipulates home appliances regardless of whether it is in or out of the local home network.

#### 6.x.1.4 Pre-condition

### The home gateway registers with the cloud server. The home appliances registers with the home gateway. The local access of home appliance is configured as the user preference when the home controller is in the local home network.

#### 6.x.1.5 Triggers

### None

#### 6.x.1.6 Normal Flow

### The smart home user goes out. The user wants to control home appliances remotely. The home controller accesses to the remote cloud server and the home controller remotely controls home appliances through the cloud server.

### The user returns home. The home controller detects and joins the local home network.

### The oneM2M service layer of the home controller get the information of the underlying network and determines the underlying network is its local home network.

### As the user has pre-configured the user preference that enables local access of home appliances when the home controller is in the local home network, the home controller automatically switches from the remote access mode to the local access mode, i.e., the home controller accesses and controls home appliances through the home gateway instead of through the cloud server.

#### 6.x.1.7 Post-conditions

### The home controller controls the home appliance directly through the home gateway.

#### 6.x.1.8 High Level Illustration

### The following figure illustrates, at the time of t1, the home controller registers with the cloud server as it is out of the local home network. At the time of t2, the home controller deregisters with the cloud server and registers with home gateway as it is in the local home network.

### 6.x.2 High Level Analysis

#### 6.x.2.1 Functional Impacts

### In oneM2M configurations, home appliances such as the refrigerator, the washing machine can be interpreted as the ADN (Application Dedicated Node). The home gateway can be interpreted as the MN (Middle Node) and the home controller can be interpreted as the ASN (Application Service Node). The cloud server can be interpreted as the IN (Infrastructure Node).

### To enable this service, the home appliance operating in the local home network needs to register its information to the home gateway. The home controller needs to register its information to cloud server or the home gateway. (Registration)

### The home controller can detect the home gateway in the local home network. The home controller connects with the home gateway through which it can access home appliances locally. (Detection)

### The home controller switches its access mode of the home appliance from remote access to local access.

#### 6.x.2.2 High Level Information Flows

### 001. ADN1 and ADN2 register its information with the MN. The MN and the ASN register its information with the IN.

### 002. At the time of T1, if the ASN needs to manipulate ADN2, it issues the request to the MN through the IN and then the MN transfers the request to ADN2.

### 003. The ASN detects its local home network and connects to the MN through which it can locally access home appliances.

### 004. The ASN registers its information with the MN and automatically switch the access model from remote access to local access.

### 005. At the time of T2, the ASN issues the request to the MN for manipulating ADN2, and then the MN transfers the request to ADN2.

### 6.x.3 Potential Requirements

### The oneM2M system shall provide the capability of detecting the field domain through which the M2M device can perform registration locally.

### The oneM2M system shall support automatically switching between remote access and local access.

# Text boxes

Time = t2

Time = t1

Washing Machine

Refrigerator

Cloud Server

Home Controller

Home Gateway

ADN

ADN

MN

ASN

IN

Time = t2

Time = t1

Washing Machine

Refrigerator

Cloud Server

Home Controller

Home Gateway