| Input contribution Use case |
| --- |
| Use Case Title:* | Integrity of Data Collection Monitoring |
| Group Name:* | WG1 Requirements |
| Source:* | Hitachi Huawei Technologies ,CO.,LTD |
| Contact: | Toshiko Matsumoto , toshiko.matsumoto.jz@hitachi-solutions.com Qi Yu, yuqi@huawei.com |
| Date:* | 2014-3-16 |
| Abstract:* | This use case introduces how to monitor the integrity of the data collected from production lines in factories. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0028 |
| Document(s) Impacted* | oneM2M-TR-0001-Use Case Collection and TR-0018-Industrial-Domain-Enablement |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Title

Integrity of Data Collection Monitoring

### Description

In factories, a lot of data are created from Programmable logic controllers (PLCs) every second and data are utilised to monitor production lines. These data are available via industrial bus systems, e.g. Real-time Ethernet.

This type of data is called time series data which is a sequence of data points, typically consisting of successive measurements made over a time interval.

In order to monitor remotely, data are gathered by the M2M service platform that needs to interface with such industrial bus systems via M2M gateways.

However, when some of data are lost due to some reasons, such as, damage of product line, temporal network delay, continuous network capacity overload and so on, some actions will be required immediately for safety. Furthermore, some considerations may be necessary, for example, switching to a new network service with more capacity, changing to the backup network, or adjusting data collecting policy for addressing an original reason of data loss. Other considerations may be effective when remote monitoring application inquires the M2M platform about condition of network traffic, e.g. temporal delay, continuous capacity overflow, or connection failure.

Similarly, from remote monitoring application, M2M gateway in each factory receives analysis result or some kinds of commands,   which can be lost due to some reasons, such as, failure in analysis process, temporal network delay, or continuous network capacity overflow. M2M gateway can detect the loss when the analysis result or the commands in form of time series data, or it can detect potential loss with the help of monitoring condition of network  traffic. When temporal network delay or continuous network capacity overflow occur, analysis result or commands may be lost. This loss will also require immediate decision and addressing a root cause.

This use case proposes that the oneM2M System shall be able to provide capability to collect, store time series data as well as monitor the integrity of data.

Moreover, the oneM2M System shall be able to provide the capability to monitor condition of network traffic.

### Source

### Actors

- PLC (Programmable logic controller):  It controls sensors and devices in a production line according to embedded programs. It also has interface to Real-time Ethernet. It broadcasts data related to the production line to Real-time Ethernet.

- M2M Gateway: It provides an interface from the Real-time Ethernet to the M2M System. The gateway collects and stores time series data from Real-time Ethernet then sends them to M2M service platform. It also receives analysis results or commands from M2M service platform. Furthermore, the gateway monitors the integrity of received analysis result or command by monitoring condition of network. It can detect the loss when the analysis result or the commands in form of time series data, or it can detect potential loss with the help of monitoring condition of network traffic when temporal network delay or continuous network capacity overflow occur.

- M2M service platform: It stores data gathered from gateway(s), and provide data to applications.

- Application: An M2M Application in the Infrastructure Domain monitors production lines by using collected data in M2M service platform and sends analysis results or commands depending on situations.

- Real-time Ethernet: A technology standardized in IEC TC65. Ethernet is used at physical layer. However the upper protocol is designed for industry purpose. In this use case, broadcast protocol is assumed.

- Internet connection: M2M service platform and gateway(s) are connected by the Internet physically.

### Pre-conditions

- PLCs and gateway are connected to Real-time Ethernet. PLCs broadcast data to Real-time Ethernet. Gateway is configured to pick up necessary data from Real-time Ethernet.

- On top of the internet, VPN connection is established between M2M service platform and gateway(s).

### Triggers

- The gateway starts to receive time series data.

### Normal Flow

Gateway picks up time series data which is broadcasted at Real-time Ethernet. The gateway sends collected data to M2M service platform.

M2M service platform receives, stores and sends data to application.

The application monitors the integrity of time series data which is sent from gateway. If data loss occurs, application user will decide to send a command for some control action immediately. Then the application user will check the condition of network traffic to determine which means are used to solve the data loss.

### Alternative flow

None

### Post-conditions

None

### High Level Illustration

### Potential requirements

- The oneM2M System shall be able to collect, store time series data as well as monitor the integrity of these data.

- The oneM2M System shall be able to provide the capability to monitor condition of network traffic.