| Input contribution Use case |
| --- |
| Use Case Title:* | Event Priority Management Use Case |
| Group Name:* | WG1 |
| Source:* | Catalina Mladin, InterDigital |
| Contact: | Catalina.Mladin@InterDigital.com |
| Date:* | 2015-03-23 |
| Abstract:* | Use case for gateway-based event priority management |
| Agenda Item:* | N/A |
| Work item(s): | WI-15 |
| Document(s) Impacted* | TR-0001 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Event Priority Management

### Description

Home Assistance systems on oneM2M-based platforms may integrate a variety of devices which are integrated on a home gateway based system. The gateway is registered to an infrastructure node provided by a Service Provider which enables all the services available on the platform. Senior Care Service are provided by a medical services provider using a specialized application

Several services are integrated based gateway-based platform including but not limited to the ones described as follows:

A home management assistive service complements any restrictions in mobility of the home owner/patient by controlling devices using gestures. It uses the cameras distributed around the home to identify the gestures, but these are turned on/off selectively based on occupancy/presence.

Another service provides security by video-monitoring the surrounding of the house, with several feeds for doors and windows, garage, gates, surrounding gardens

Direct access to medical and emergency services is provided based on call button activation, e.g. after a fall.

### Source

REQ-2015-xxxx

### Actors

- Home owner/user: Person using the services included in this use case, might also be the administrator/manager of the home gateway-based platform

- Smart sensors/ devices/ appliances: Devices integrated in the home gateway based platform, providing measurements or services to the owner.

- Home M2M gateway: home based device which can receive wellness data from wellness smart devices and communicate with application servers.

- M2M Service Platform: provides common functionalities for the M2M services, such as collecting the data, status and configuration information for devices via the M2M gateway.

- M2M Service Providers: Companies providing their own M2M services for the user through the M2M Service Platform and via specialized infrastructure nodes. For example a medical/senior care monitoring provider uses specialized platform applications enabled by the home sensors and devices to monitor vitas as well as respond to emergency calls.

### Pre-conditions

Each device registers its information with the home gateway, which in turn is registered with a home server.

### Triggers

N/A

### Normal Flow

The home security monitoring service is set-up with a large amount of memory allowed for video recording. It ends up taking most of the resources available at the gateway, although all applications registered continue functioning.

When a fall of the home owner/patient occurs, the platform resources should be allocated to attend to the critical situation. However the monitoring application is not aware of the emergency call button activation and continues using a large portion of resources.

During an emergency situation such as the fall, priority management provided by the home gateway may enable event arbitration based on either general platform settings or user input.

### Alternative flow

N/A

### Post-conditions

N/A

### High Level Illustration

TBD

### Potential requirements

- The oneM2M system shall support gateway-based capabilities for event management, e.g. capability for arbitration of the resulting processing.