| CHANGE REQUEST |
| --- |
| Meeting:* | REQ 17.0 Face-to-face meeting in Sapporo |
| Source:* | Nicolas Damour, Sierra Wireless, ndamour@sierrawireless.com |
| Date:* | 2015-05-11 |
| Contact:* | Nicolas Damour, Sierra Wireless, ndamour@sierrawireless.com |
| Reason for Change/s:* | Inclusion of requirements from GSMA Connection Efficiency project |
| CR against: Release* | Release 2 |
| CR against: WI* | Active - WI-0026 Efficient Communications MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0002 V2.0.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The Communication Management and Delivery Handling Common Service Function of oneM2M has been defined and developed in the release 1, with the intent of allowing the oneM2M service layer to better control the establishment and usage of communication channels over the Underlying Networks available to a given CSE.

In parallel, the GSM Association has over the course of 2014 developed a set of guidelines, called the “IoT Device Connection Efficiency Guidelines”, to help IoT solution developers deploy solutions that make an efficient usage of the cellular networks. Liaison Statements exchanged between oneM2M and the GSMA (see TP-2014-0507R02 and TP-2014-0540) show that these guidelines could result in further requirements applicable to the oneM2M service layer, and to extensions of the oneM2M functionality, in particular (but not limited to) in its CMDH CSF.

The present document takes as a basis the GSMA IoT Connection Efficiency Guidelines, and tries to derive generic requirements for the oneM2M system.

## Main Reference – GSMA IoT Connection Efficiency Guidelines

As stated above, the main reference document to be considered in conjunction with the present oneM2M input contribution is the GSMA Connection Efficiency Guidelines document.

This document has been initially published by GSMA in October 2014 under version 1.0

It has since been updated twice. The latest version, version 1.2, has been approved by the relevant GSMA project (the IoT Connection Efficiency project of the Connected Living Program) but is currently being published.

The version currently publicly available is the version 1.1, available on the GSMA website at the time this document is written, here: http://www.gsma.com/connectedliving/iot-device-connection-efficiency-guidelines/

Any mentions in the present oneM2M document to these GSMA Connection Efficiency Guidelines, unless otherwise specified, will refer to this version 1.1 of the guidelines.

## Architectural considerations

The GSMA Connection Efficiency Guidelines consider the following generalized IoT Service architecture.

The version 1.2 of the Guidelines also acknowledges the evolution of monolithic applications (both on the device and server side) into the following model.

Considering this diagram, it becomes clear that it is nicely in line with the oneM2M model of a split between an Application Layer, where the AEs (Application Entities) reside, and a Common Service Layer, where the CSEs (Common Services Entities) reside.

This convergence between oneM2M and GSMA will prove very helpful in deriving guidelines and requirements expressed by GSMA to requirements on the oneM2M Service Layer.

## Requirements related to communication management

Before introducing new requirements, the present document proposes to reorganize communication management – related requirements into a single section.

### -----------------------Start of change 1-------------------------------------------

## 6.7	Communication Management Requirements

Table 12: Communication Management Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| CMR-001 | The oneM2M System shall provide to M2M Applications a communication service which provides buffering of messages to/from M2M Gateway / Device / Infrastructure Domain. | Implemented in Rel-1 |
| CMR-002 | The oneM2M System shall be able to support forwarding buffered messages depending on communication policies and based on service preference associated with the buffered messages. | Implemented in Rel-1 |
| CMR-003 | The oneM2M System shall enable an M2M Application to send a communication request with the following service preference: QoS parameters, including delay tolerance, for initiating the delivery of data; categorizing communication requests into different levels of priority or QoS classes. | Implemented in Rel-1 |
| CMR-004 | The oneM2M System shall be able to support concurrent processing of messages within M2M Gateways and/or M2M Devices from different sources with awareness for the service preference associated with the messages while observing the provisioned communication policies. | Implemented in Rel-1 |
| CMR-005 | The oneM2M System shall be able to maintain context associated with M2M sessions (e.g. security context or network connectivity context during the interruption of the session). | Partially implemented in Rel-1 (see note 1) |
| NOTE 1: Long lived security context and registration is covered, M2M Sessions are not covered. |

### -----------------------End of change 1---------------------------------------------

## Requirements related to communication management

Here are some of the new requirements that may be introduced to oneM2M based on the GSMA IoT Connection Efficiency Guidelines document.

Parameters stored locally in a secure manner (eg. in a secure element and/or UICC) and remotely manageable, either by OTA SIM management (RTC7), or via DM protocols (DM1to4), or via usual oneM2M protocols

DAR1 – use and manage an always-on connection

DAR2 – minimize the number of connections and perform aggregation

DAR3+27 + MCR1– randomized access patterns (from device to cloud and the other way around too)

DAR6 and DAR7 – maintain keep alive connection by detecting timeout on the network, or use 29 minutes as default value instead

DAR10 – oneM2M system should be able to request information about quality of service provided by the network (eg. speed, latency, etc.)

DAR11 –handling connection failures – shall monitor the connection failures and should count them per interval of time

DAR12+13 – count the number of failures over periods of time, and the volume of communication over periods of time

DAR12+13 – shall be able to stop communication attempts if too many attempts or too much data

DAR16 – should be able to use the network preferably during certain periods (off-peaks hours)

DAR18 – establish classes of communication

DAR26 – avoid ping pong between communication channels

MCR2 – if the subscription is disabled, the oneM2M service layer should prevent communication attempts (exponential backoff)

CER3+BTR1-2-3-4+BTI1to12 – backoff timers for IMSI attach, GPRS attach, PDP Context activation and SMS MO

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?