| CHANGE REQUEST |
| --- |
| Meeting:* | REQ#17 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2015-05-21 |
| Contact:* | As above |
| Reason for Change/s:* | Application End-to-End security requirements |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0002 v1.0.1 |
| Clauses/Sub Clauses* | 6.4 “Security” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

The motivation for these requirements is provided in SEC-2015-0513R01 “Application End-to-End Security”

R01: splits the requirements into one addressing confidentiality and one for integrity and data origin verification, as discuss in SEC Ad Hoc 2015-05-19 1130-1300

### -------------Start of change 1: insert at appropriate place in table 5----------------

## 6.4	Security Requirements

Table 5: Security Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| SEC-0xx | The oneM2M System shall allow security protocol end-points to protect portions of individual application-generated data so that intermediate entities (whether trusted or untrusted) can forward the data (between the security protocol end-points) without accessing the protected portions of the data in clear text. | Targeted for Release 2 |
| SEC-0xx | The oneM2M System shall allow security protocol end-points to protect portions of individual application-generated data so that security protocol end-points can detect modification of the protected portions of data by intermediate service layer entities (whether trusted or untrusted) forwarding the data (between the security protocol end-points). | Targeted for Release 2 |

### -----------------------End of change 1---------------------------------------------