| CHANGE REQUEST |
| --- |
| Meeting:* | REQ 17.1 |
| Source:* | Darold Hemphill, iconectiv, dhemphill@iconectiv.com |
| Date:* | 2015-06-11 |
| Contact:* | Darold Hemphill, iconectiv, dhemphill@iconectiv.com |
| Reason for Change/s:* | New requirements to support App-ID |
| CR against: Release* | Release 2 |
| CR against: WI* | Active WI-0029 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0002 |
| Clauses/Sub Clauses* | Propose new operational and security requirements |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

# App-ID Requirements

Work Item WI-0029 proposes additional work to clarify the App-ID and its use within TS-0001, TS-0003 and TS-0004. This document proposes new requirements to support clarify App-ID in Release 2.

# Terminology

The following terminology is used in this Change Request.

App-ID is defined in section 7.1.3 of TS-0001 Functional Architecture-V1.8.0 as:

An Application Identifier (App-ID) uniquely identifies an M2M Application in a given context.

App-ID is further defined as a string of characters that constitutes an identifier for an M2M application.

A M2M application will warrant a unique App-ID for any of the following cases:

- The M2M application code (either source code or binary code) is different

- The M2M application code changes ownership i.e., software developer has a name change or buyout

- The M2M application name changes

- Two M2M applications which are functionally 100% equivalent (accept the same inputs, produce the same outputs and are produced by the same software developer) but are realized as different pieces of software would be identified by different App-ID codes.

- A single M2M application provided to two different customers where the only difference between the customers is the software configuration i.e., white-label solution would require different App-IDs

# New Requirements

### We propose the following new requirements for Registered App-IDs to TS-0002. We are looking for input on the requirements listed below.

### -----------------------Start of change 1-------------------------------------------

| Requirement ID | Description | Release |
| --- | --- | --- |
| OPR-a | The format for registered App-IDs shall be able to support use by people and systems to readily determine whether the App-ID is registered and the Registration Authority which issued the App-ID, App Developer and App Name. | 2 |
| OPR-b | The oneM2M System Registration Authorities shall be able to collect and maintain supporting required information when assigning an App-ID. | 2 |
| SEC-c | The oneM2M System shall be able to verify the App-ID to support the detection of impersonation or to support revocation. | 2 |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?