| CHANGE REQUEST |
| --- |
| Meeting:* | REQ#18 |
| Source:* | Vinod Choyi, Vinod.Choyi@InterDigital.com Catalina Mladin, Catalina.Mladin@InterDigital.com |
| Date:* | 2015-07-12 |
| Contact:* | As above |
| Reason for Change/s:* | End-to-End security requirements R01 addresses offline comments R02 addressess comments during SEC session and provides consolidated end-to-end requirements for data security |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0002 v1.0.1 |
| Clauses/Sub Clauses* | 6.4 “Security” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

The motivation for these requirements is provided in SEC contributions introducing the use cases for providing End-to-End data integrity and confidentiality.

### -------------Start of change 1: insert at appropriate place in table 5----------------

## 6.4	Security Requirements

Table 5: Security Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| SEC-0x1 | M2M system shall support the ability to provide and verify end-to-end data integrity and authenticity at-rest. | 2 |
| SEC-0x2 | M2M system shall support end-to-end data confidentiality at rest | 2 |
| SEC-0x3 | M2M system shall ensure that the end-to-end data credentials are protected for confidentiality, integrity and against tampering. | 2 |
| SEC-0x4 | M2M system shall ensure that the end-to-end data credentials are protected for confidentiality, integrity and against tampering | 2 |

### -----------------------End of change 1---------------------------------------------