| Input Contribution |
| --- |
| Meeting ID* | TP#18 |
| Title:* | CR on TS-0001 and TS-0011 regarding Application ID and related issues |
| ID: | TP-2015-0751-AppID_CR REQ-2015-0615-AppID_CR ARC-2015-0616-AppID_CR |
| Source:* | David Crowe, IFAST, David.Crowe@ifast.org, +1-403-289-6609 Mihai Voicu, Telit, Mihai.Voicu@telit.com, +1-561-214-4559 |
| Uploaded Date:* | 2015-07-20 |
| Document(s) Impacted* | TS-0001, TS-0011 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Based on ballot comments from IFAST, endorsed by other members of TIA TR-50, changes to TS-0001 and TS-0011 related to Application ID are recommended. Proposed changes are indicated by marked up text. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# TS-0001: Application ID Format

Proposed change to the definition of “M2M Application”.

# 3	Definitions

…

The inclusion of the registration authority ID makes identifier portability more difficult. It implies that queries for Application ID must go to a specific registrar, but this is not necessary even if there are multiple registrars (all registrars could synchronize their data, for example). It is therefore recommended to remove the Authority ID from the format.

Table 7.2-1: Identifiers formats and use

| Identifier Name | Absolute & Format-Designator or Relative & Format-Designator & Context | Format | Rule of use |
| --- | --- | --- | --- |
| … |
| APP-ID | App-ID | Either: "R [registered-App-ID]" or "N[non-registered-App-ID]" If the first letter is "R", then registered-App-ID is assigned and managed by the registration authority. If the first letter is "N", then the non-registered-App-ID is not registered by a registration authority. | AE Registration Procedure described in clause 10.1.1.2.2. |

…

Reason for change: The M2M Application Key is mentioned in only one place, in TS0001. Without any details it is unclear what kind of key this is and whether it is unique for the application, or for each instance of the application. It implies that this is obtained from the application registry, but it is not clear how the “M2M application key” will be derived with the assistance of the registry. Nor is it clear how a key can be used to “grant specific authorization to access an approved list of M2M services”. The section should therefore be deleted.

…

Reason for change: If it is possible to query a registry for an App-ID, at least the minimal information that will be returned should be defined. This is not in any specification, but was proposed in an ATIS/iConectiv contribution to the App ID ad hoc group. Since the contribution was not accepted, it is not discussed here. Organizations that can obtain the information should also be defined, but this is probably more appropriate by industry assignment guidelines rather than in a specification.

Annex J (informative):
Application Identifier (App-ID) Registry Information

Any Application Identifier registry shall contain at least the following information fo each App-ID that is currently assigned:

- App-ID

- Assignee (name of organization to which the identifier is assigned)

- Application Description (a simple English language description of the application)

- Registrar (name of organization from which the identifier was assigned)

- Date of assignment

- Current status (e.g. Pending assignment; Assignbed; Being withdrawn; Withdrawn). The specific states may vary between registries.

# TS-0011: M2M Application

Proposed change to the definition of “M2M Application”.

# 3	Definitions

…

## 3.2	A

…

M2M application: applications that run the service logic in a single entity within the field domain and use M2M Common Services accessible via a set of oneM2M specified open interfaces.

…