| CHANGE REQUEST |
| --- |
| Meeting:* | REQ#18 |
| Source:* | BT Group |
| Date:* | 23rd July 2015 |
| Contact:* | Colin Blanchard colin.blanchard@bt.com |
| Reason for Change/s:* | Add Potential requirements from REQ-2015-0619R02-Terms_And_Conditions_Markup_Language_for_Privacy_Policy_Manager |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0002 v1.0.1 |
| Clauses/Sub Clauses* | 6.4 “Security” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

The motivation for these requirements is provided in

| REQ-2015-0619R02 | Terms And Conditions Markup Language for Privacy Policy Manager |
| --- | --- |

### -------------Start of change 1: insert at appropriate place in table 5----------------

## 6.4	Security Requirements

Table 5: Security Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| SEC-0xx1 | The oneM2M system shall store and process privacy preferences in an interoperable manner. | 2 |
| SEC-0xx2 | The oneM2M system shall support privacy profiles at various levels to care for conditions of legal requirements, manufacturers, and data subjects. | 2 |
| SEC-0xx3 | The oneM2M system shall be able to prioritise privacy profiles where there is a conflict between profiles (legal profile takes priority over data subject profile, for example). | 2 |

### -----------------------End of change 1---------------------------------------------