| Input Contribution |
| --- |
| Meeting ID* | REQ 19 |
| Title:* | TR-0018- Industrial Domain Enablement_Clause_8_High_Level_Architecture |
| Source:* | Yanping Jiang, Huawei, jiangyanping@huawei.com Qi Yu, Huawei, yuqi@huawei.com Mitch Tseng, mitch@T-infoserv.com Miao Jiang, Hitachi, miaojiang@hitachi.cn |
| Uploaded Date:* | 2015-8-31 |
| Document(s) Impacted* | WI 0028 oneM2M-TR-0018- Industrial Domain Enablement -V0_3_0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TR-0018. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This document is the detailed description of Clause 8 “High Level Architecture” in TR-0018.

R01: update based on the  comments on meeting.

R02: update the figure8.2 and add a reference at section 2,2

# 2	References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## 2.1	Normative references

Not applicable.

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules

[i.2]		oneM2M TS0011, “Definitions and Acronyms”

[i,x]	oneM2M TS-0001 "Functional Architecture"

# 8. High Level Architecture

The seven use cases in the industrial domain discussed in this document are listed in Table 8-1.

Table 8-1: Use cases in the industrial domain

| Use case No. | Title | Description |
| --- | --- | --- |
| 1 | An industrial use case for on-demand data collection for factories | See clause 6.1 |
| 2 | Integrity of data collection monitoring | See clause 6.2 |
| 3 | Data process for inter-factory manufacturing | See clause 6.3 |
| 4 | Aircraft construction and maintenance | See clause 6.4 |
| 5 | Real Time Data Collection | See clause 6.5 |
| 6 | Data encryption in industrial domain | See clause 6.6 |
| 7 | QoS/QoI monitoring in industrial domain | See clause 6.7 |

The deployments which support these use cases require the use of M2M Devices which use broadcasting mode through the PLC or DCS.The following sections  provide the high level oneM2M architecture mapping for these deployments  .

## 8.1 Deployment Mapping Using IPE

Table 8.1-1 lists the mapping relationship between actors in industrial domain and nodes in oneM2M domain. Those devices under the M2M Gateway are non-oneM2M devices which can be mapped into the M2M Area Network. In this case ,the M2M Gateway which is mapped to the MN shall implement the Inter-working Proxy Application Entity (IPE).

Table 8.1-1: Mapping relationship 1

| Use case No. | Actors in the use case | oneM2M Node |
| --- | --- | --- |
| 1, 2, 3, 4, 5, 6, 7 | Application and M2M service platform | IN |
| 1, 2, 3, 5, 6, 7 | M2M Gateway | MN |
|  | M2M Devices (PLC/DCS, sensors) and Intra-factory network | Non-oneM2M Device in M2M Area Network |
| 4 | WiFi gateway | MN |
|  | Power tools and underlying network (WiFi) | Non-oneM2M Device in M2M Area Network |

## Figure 8.1-1 illustrates Deployment Mapping Using  IPE.

Figure 8.1-1 Deployment Mapping Using IPE

## 8.2 Deployment Mapping Using Peer-to-Peer Communication

Table 8.2-1 lists the mapping relationship between actors in industrial domain  and nodes in oneM2M domain. In this case, all of the actors are assumed to be oneM2M compliant nodes.

Table 8.2-1: Mapping relationship 2

| Use case No. | Actors in the use case | oneM2M Node |
| --- | --- | --- |
| 1, 2, 3, 4, 5, 6, 7 | Application and M2M service platform | IN |
| 1, 2, 3, 5, 6, 7 | M2M Gateway | MN |
|  | M2M Devices (PLC/DCS, sensors) | ADN/ASN |
| 4 | WiFi gateway | MN |
|  | Power tools | ADN/ASN |

Figure 8.2-1 illustrates Deployment Mapping for Peer-to-Peer Communication. In the existing factory production line, M2M Devices with PLC/DCS will support peer-to-peer communication, which means data can be exchanged among nodes directly. Note that  peer-to-peer communication between CSEs of different ASNs is currently not supported by oneM2M architecture deployment (see 6.1 [i.x]) .

Figure 8.2-1 Deployment Mapping Using Peer-to-Peer Communication

8.2 Conclusion

Since M2M Devices with PLC/DCS need to support peer-to-peer communication,  the existing reference enhancement  between CSEs of different ASNs shall be considered in the future oneM2M releases.