| CHANGE REQUEST |
| --- |
| Meeting ID:* | REQ 28 |
| Source:* | Jairo Lopez, Hitachi, jairo.lopez.uh@hitachi.com |
| Date:* | 2017-03-24 |
| Reason for Change/s:* | Improvement of Chapter 10 Potential Solutions for the Key Issues |
| CR against: Release* | N/A |
| CR against: WI* | Active <WI-0046 > MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0026-V-0.6.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This change improves the Potential Solutions for the Key Issues chapter in the Vehicular Domain Enablement technical report.

### -----------------------Start of change 1-------------------------------------------

# 10	 Potential Solutions for the Key Issues

Editor’s Note: This clause summarizes solutions for the Key Issues. Each solution is captured in a separate clause.

Due to the high mobility that a vehicular domain oneM2M system has to handle, the potential solutions to the key issues; location, AE contact maintenance, registration management and security, depend on the cooperation and interaction of the oneM2M system components. The behaviour of the components will change depending on the vehicular architecture deployed. This chapter describes potential solutions for the issues presented.

## 10.1 Solution A

### 10.1.1 Solution Description

Editor’s Note: This clause provides a description of the solution

Although the architectures for vehicle domain  that have been discussed differ slightly, the big differences arise from how much competing information the principal MN-CSE handling the MN-AE can obtain. It is also important to take into consideration that the location information can only be successfully propagated if key issue 2 and 3 are correctly being handled, Taking that into account, we can outline a very basic procedure below:

Step 1: The MN-AE receives a signal from MN-CSE that the current connection is weakening. The MN-AE begins de-association procedures.

Step2: With the MN-AE de-association complete, the MN-CSE disconnects from the current point of attachment

Step 3: The MN-CSE surveys the surrounding area for updated location information, be it from nearby MN-CSEs and their MN-AEs or from collected data obtained via non-oneM2M interfaces.

Step 4: The MN-CSE searches for a new IN-CSE. When a valid IN-CSE is found, the MN-CSE begins its re-association.

Step 5: With the MN-CSE re-associated, the MN-AE attempts re-registering into the whole system, asking to be validated by the IN-CSE. The previous URI used by the MN-AE is transmitted in the re-registry to the IN-CSE.

Step 6: The IN-CSE being used for registering allocates a new URI for the registering MN-AE.

Step 7: The IN-CSE being used for registering examines all services that contain the URI handed by the re-registering MN-AE. A  Notify request with the new URI information is transmitted to surrounding IN-CSEs and other MN-CSEs.

Step 8: Surrounding IN-CSE and MN-CSE will update URI information, ensuring that future requests are forwarded to the new URI.

### 10.1.2 Solution Applicability

Editor’s Note: This clause specifies which Key Issues are resolved using this solution

This solution applies to Key Issue 1, 2 and 3.

## 10.2 Solution B

### 10.2.1 Solution Description

In the communications between different types of MN-CSE and IN-CSE, with a heterogeneous assortment of computational resources, there is a need to be able to choose a suitable method to secure communication that balances security with resource usage.

In an oneM2M system, we believe that a mechanism to negotiate the encryption method would solve this issue. The basic procedure for this negotiation is shown below:

Step 1: An MN-CSE wishing to transmit to another MN-CSE or IN-CSE sends encryption methods available to use.

Step 2: The receiving MN-CSE or IN-CSE obtains the available encryption methods and chooses a particular encryption method suitable to its current situation and signals this information to the originating MN-CSE.

Step 3: The originating MN-CSE accepts the chosen encryption method or returns to step 1 with a reduced list of encryption methods available.

Step 4: If both entities agree on the encryption method, then the negotiation for the use of the encryption method begins. Once this negotiation finishes, secure communication between the entities can begin.

### 10.2.2 Solution Applicability

Editor’s Note: This clause specifies which Key Issues are resolved using this solution

This solution applies to Key Issue 4.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

4. Secure transmission establishment

3. Encryption method negotiation

2. Chosen encryption method

1. Desired encryption method

MN-CSE/IN-CSE

MN-CSE

7. URI change redirect

7. URI change redirect

6.URI allocation

5. Re-register

4. Re-association

3. Information

3. Information

3. Information poll

3. Information poll

2. Disconnection

1. De-association

MN-AE

MN-CSE

Non-oneM2M interfaces

MN-CSE

IN-CSE

IN-CSE

MN-AE