| CHANGE REQUEST |
| --- |
| Meeting ID:* | REQ 30 |
| Source:* | Catalina Mladin, Convida, Mladin.Catalina@convidawireless.com Kenichi Yamamoto, KDDI, kc-yamamoto@kddi.com |
| Date:* | 2017-07-10 |
| Reason for Change/s:* | TS002 new reqs from TR-0026, not implemented, to be clarified first |
| CR against: Release* | Release 4 |
| CR against: WI* | Active MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision) Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0002 V 2.10.3 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |

| Impacted other TS/TR(s) | TR-0026 |
| --- | --- |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This document proposes to move requirements pertaining to Vehicular Domain from TR-0026 clause 7 to TS-0002. The following requirements have been proposed to be postponed in order to clarify the wording.

Contributor proposals are contained in the initial version of this document, but further discussion and re-wording should ensue in REQ#30.

### -----------------------Start of Change 1 -------------------------------------------

| OSR-yy3 | Provisioning, installation, configuration and registration method of terminal system. Especially for the case of overlapping two different system for DTG management system (owns and manages the device) and the application system using DTG data (utilising the data from the device). | Rel-3/ future releases? |
| --- | --- | --- |
| OSR-yy4 | DTG/FMS data storing method and delivery protocol. There is no dominant standard specifying data formats and protocols for vehicle related applications. | Rel-3/ future releases? |
| OSR-yy8 | The registration shall be able to include information that identify the peer entity, and other information such as its management privilege, subscription etc., that are necessary for the conduct of the respective peer relationships. | Rel-3/ future releases? |
| OSR-yy9 | It shall be possible for some registrations to hold the complete set of information context about the peer entity. This is referred to as "full registration". | Rel-3/ future releases? |
| OSR-y10 | It shall be possible for some registrations to hold only a subset of information context about the peer entity. This is referred to as "lightweight registration". | Rel-3/ future releases? |
| OSR-y11 | It shall be possible for "lightweight registration" at different entities that pertain to a common peer entity, to hold different sets of information, if needed, about the common peer entity. | Rel-3/ future releases? |
| OSR-y12 | It shall be possible to correlate the "full registration" and the "lightweight registration" that pertain to a common peer entity. | Rel-3/ future releases? |
| OSR-y13 | It shall be possible to distinguish the "full registrations" and the "lightweight registrations" that pertain to a common peer entity. | Rel-3/ future releases? |

### -----------------------End of Change 1 ---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause?