| Input Contribution |
| --- |
| Meeting ID* | <e.g. TP#1> |
| Title:* | <title of input contribution> |
| Source:* | <name>, <company>, <email address> |
| Date:* | 2017-mm-dd |
| Input related to* | <A list of the Work Item(s), Technical Report(s), Technical Specification(s) or other documents that are related to this contribution> |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes a result of study for the disaster alert system use cases and potential requirements.

### -----------------------Start of input 1-------------------------------------------

# 6. Use cases and potential requirements

## 6.1	Disaster Alerting Services

### 6.1.1	Description

Background

- 한국, 미국, 유럽 및 일본을 비롯한 몇몇 나라들은 재난 상황을 국민들에게 빠르고 정확하게 전달하고, 재난 상황을 managing하기 위한 방법으로 재난경보시스템을 구축하고 이를 운영하고 있다. 재난경보 서비스에 있어서 사물인터넷은 기존의 전달 매체보다 상당히 나은 솔루션을 제공할 수있을것으로 기대되고 있으며, 이는 독립적으로 동작하기 보다는 기존의 재난경보시스템과의 interworking을 통해 시스템의 정보전달 체널 확장의 형태로 구축되는 것이 합리적이다.

Description

- This is the use case of a M2M Service that interworks between integrated public warning system(IPWS) and M2M service platform(MSP) to transmits disaster information to the User Devices(UDs) and Public Devices(PDs) located in devastated area.

- In peace time, UDs and PDs do it’s programed tasks, for example play audio, lock and unlock the door, bright streets, display advertisements, etc. These UDs and PDs could be transformed to disaster safety assistive devices under a disaster situation.

- Authorities triggers IPWS for delivering warning messages to citizen through standardized open API. IPWS distributes warning message through multiple channels include MSP. The warning message will be propagated to UDs and PDs as a high priority message immediately.

### 6.1.2	Source

- void -

### 6.1.3	Actors

- Authorities: 재난 상황이 발생했을 때 이를 국민들에게 경보해야 할 책임을 가진 공공 기관.

- Integrated Public Warning System(IPWS): 재난 경보를 위해 하나 이상의  authorities들이 공동으로 운영하는 통합된 경보 시시템이다.

- IPWS-M2M Interworking Proxy (IMIP): IPWS로부터 disaster  message를 수신하여 M2M message로 변환 및 M2M Service Platform을 통해 디바이스로 전송하는 기능을 수행하는 Proxy entity.

- M2M Service Platform(MSP): M2M service provider에 의해 운영되는 M2M service platform

- User Device(UD): individual user가 소유한 M2M connected device. 일부 User Device들은 재난 상황에서 사용자의 피해를 줄이기 위한 disaster safety assistive feature를 가질 수 있다.

- Public Device(PD): 하나의 공공시설로서 개인이 아닌 공공기관이 소유한 M2M connected device. 일부 PublicDevice들은 재난 상황에서 사용자의 피해를 줄이기 위한 disaster safety assistive feature를 가질 수 있다.

### 6.1.4	Pre-conditions

- Authority와 IPWS, IPWS와 M2M Service Platform은 표준화된 프로토콜로 구현된 openAPI로 통신한다.  표준화된 프로토콜은 CAP 1.2(OASIS Common Alerting Protocol version 1.2) 가 많이 사용되고 있다.

- IMIP는 IPWS로부터 수신된 human understandable warming message를 machine readable M2M message으로 변환하여 UD 또는 PD에 전달한다.

- IPWS로부터 수신된 warning message는 devastated area에 대한 geolocational information을 포함할 수 있다

### 6.1.5	Triggers

재난상황 발생

### 6.1.6	Normal Flow

Figure 6.1.6-1 Usecase Scenario Service Flow

- 재난 상황이 발생하면, Authority는 IPWS를 통해 다양한 통신 channel로 재난 상황을 국민들에게 전파한다.

- IPWS가 전파하는 human understandable warning message는 UD/PD에 직접 전달할 수 있는 형태가 아니기 때문에 IMIP의 message translation을 통하여 machine readable한 형태로 변환하는 과정을 거친다.

- M2M Warning message를 수신한 UD와 PD는 자신의 동작 모드를 disaster 모드로 변환하여 disaster safety assistive task를 수행한다.

### 6.1.7	Alternative Flow

None

### 6.1.8	Post-conditions

None

### 6.1.9	High Level Illustration

Figure 6.1.9-1 High level system view

### 6.1.10	Potetial Requirements

This scenario is fulfilled by below already defined requirements. There is no needs to define new requirements for this use case.

Table 6-1 Related current requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| OSR-094 See REQ-2015- 0631R02 | The oneM2M System shall provide Information Model(s) to support interoperability among different devices/applications. | Implemented in Rel-2 |
| OSR-095 See REQ-2015-0631R02 | The oneM2M System should provide mappings between different Information Models from non-oneM2M System(s). | Not implemented |
| OSR-096 See REQ-2015- 0631R02 | The oneM2M System should be able to interwork with non-oneM2M System(s). | Implemented in Rel-2 |
| OSR-037 | The oneM2M System shall enable an M2M Application to request to send data, in a manner independent of the Underlying Network, to the M2M Applications of a group of M2M Devices and M2M Gateways in geographic areas that are specified by the M2M Application. | Not implemented |

### -----------------------End of input 1---------------------------------------------