| Input Contribution |
| --- |
| Meeting ID* | REQ#33 |
| Title:* | Use case for authentication to non-oneM2M devices |
| Source:* | Maciej Goluch, ORANGE, maciej.goluch@orange.com Saïd Gharout, ORANGE, said.gharout@orange.com Paweł Strzemecki, ORANGE, pawel.strzemecki2@orange.com |
| Date:* | 2018-01-12 |
| Input related to* | TR-0001 Use Case Collection |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TR-0001 V.3.1.0 |
| Decision requested or recommendation:* |  |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Support for authentication non-oneM2M devices

### Description

This use case is to provide support for authentication of oneM2M user applications (AE) on non-oneM2M  vendor’s specific platforms. The objective  is to ease developers to integrate with devices which their applications require to be authenticated to specific platforms.  For example, it can be a camera with vendor specific cloud server which must authenticate Application Entity

Let assume there are 3 communication channels between Application Entity and vendor specific platform which is non-oneM2M node:

- communication channel for authentication,

- communication channel for platform and stream configuration/controll ,

- communication channel for data streaming.

Those are introduced to simplify authentication and configuration/controll  of non-oneM2M platform provided by independent vendors. Communication channel for data streaming is out of oneM2M scope and is separated from configuration/controll  and authentication channels. oneM2M System is used only to authentication and configuration/controll  process.

This use case addresses needs of applications that require to  register on non-oneM2M vendor specific platforms. Please note that the example of camera and video streaming is only an example. Streamed data could be also photos, music, files, etc.

### Source

REQ-2018-0001-TR-0001 use case for authentication to non-oneM2M devices

### Actors

Vendor specific platform (non-oneM2M node), AE (user application)

### Pre-conditions

none

### Triggers

- User Application wants to authenticate to non-oneM2M specific vendor platform (authentication  communication channel).

- User Application wants to change configuration  of non-oneM2M specific vendor platform or data streaming provided by this platform (configuration/control communication channel).

- User Application wants non-oneM2M platform to start streaming data (configuration/control communication channel).

- User Application wants non-oneM2M platform to stop streaming data (configuration/control communication channel).

### Normal Flow

- Application entity wants to authenticate to non-oneM2M platform. To do so AE sends the authentication request through MN/IN-CSE and Proxy-API using authentication communication channel. Proxy-API translates given request and forwards it to non-oneM2M platform. Then it responds using the same dataflow channel. This process is depicted on Figure 1.

- Application entity wants to change configuration of non-oneM2M platfrom or data stream. To do so AE sends the configuration change request through MN/IN-CSE and Proxy-API using configuration/controll  communication channel. Proxy-API translates given request and forwards it to non-oneM2M platform. Then it responds using the same communication channel. This process is depicted on Figure 2.

- Application entity wants to controll data streaming provided by  non-oneM2M platform. To do so AE sends the control request through MN/IN-CSE and Proxy-API using configuration/controll  communication channel. Proxy-API translates given request and forwards it to non-oneM2M platform. If it is needed it  responds using the same communication channel. This process is also depicted on Figure 2.

Figure 0-1Call Flow for authentication

Figure 0-2Call flaw for camera configuration/controll

### Alternative Flow

None

### Post-conditions

None

### High Level Illustration

Following figure depicts high level illustration of describing use case. Data streaming communication channel is out of one-M2M scope and is separated from authentication and camera configuration/controll  communication channels.

### Potential Requirements

- The oneM2M System shall be able to distinguish between the raw dataflow and the configuration/control flow.

- The oneM2M System shall be able to provide an authentication framework of  user application to the non-oneM2M vendor’s specific platform.