| Input Contribution |
| --- |
| Meeting ID* | REQ#33 |
| Title:* | Use case for authentication to non-oneM2M devices |
| Source:* | Maciej Goluch, ORANGE, maciej.goluch@orange.com Saïd Gharout, ORANGE, said.gharout@orange.com Paweł Strzemecki, ORANGE, pawel.strzemecki2@orange.com |
| Date:* | 2018-01-12 |
| Input related to* | TR-0001 Use Case Collection |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TR-0001 V.3.1.0 |
| Decision requested or recommendation:* |  |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Support for configuration of and authentication to non-oneM2M devices

### Description

This use case is to provide support for authentication of oneM2M user applications on non-oneM2M  vendor’s specific application (server, or IoT application). The authentication is required to configure the non-oneM2M application through the user application. The objective  is to ease IoT services developers to integrate with devices which their applications require to be authenticated to specific platforms.  For example, it can be a camera with vendor specific cloud server which must authenticate the application which configure the camera. This is important to avoid that an attacker or a non autorised person control or configure the camera.

Let assume there are 3 communication channels between user application and vendor specific platform which is non-oneM2M node:

- communication channel for authentication,

- communication channel for node and stream configuration/controll ,

- communication channel for data streaming. This is the classic stream used ton transport.

Those are introduced to simplify authentication and configuration of non-oneM2M platform provided by a vendor using an authentication method (standardized or proprietary). Communication channel for data streaming is out of oneM2M scope and is separated from configuration  and authentication channels. The M2M System is used only for the authentication and configuration  process.

This use case addresses needs of applications that require to  register on non-oneM2M vendor specific applications or platforms. Please note that the camera and video streaming is given only as an example. Streamed data could be also photos, music, files, etc. Other data flows could be considered. The use cas aims to highlight the need to configure and authentication to non-oneM2M entities.

### Source

REQ-2018-0001-TR-0001 use case for authentication to non-oneM2M devices.

### Actors

Vendor specific application or platform (non-oneM2M node), AE (user application).

### Pre-conditions

None.

### Triggers

- User Application wants to authenticate to non-oneM2M specific vendor node (authentication  communication channel).

- User Application wants to change configuration  of non-oneM2M specific vendor node or data streaming provided by this node (configuration/control communication channel).

- User Application wants non-oneM2M node to start streaming data (configuration/control communication channel).

- User Application wants non-oneM2M platform to stop streaming data (configuration/control communication channel).

### Normal Flow

- Application entity wants to authenticate to non-oneM2M platform. To do so the user application  (AE) sends the authentication request through the IoT Server (MN/IN-CSE) and Proxy-API using authentication communication channel. Proxy-API translates given request and forwards it to non-oneM2M platform. Then it responds using the same dataflow channel. This process is depicted on steps 1 of Figure X.

- Application entity wants to change configuration of non-oneM2M node or data stream. To do so AE sends the configuration change request through IoT Server (MN/IN-CSE) and Proxy-API using configuration  communication channel. Proxy-API translates given request and forwards it to non-oneM2M node (device or platform). Then it responds using the same communication channel. This process is depicted on steps 2 of Figure X.

- Application entity wants to control data streaming provided by  non-oneM2M node (device or platform). To do so AE sends the control request through IoT Server (MN/IN-CSE) and Proxy-API using configuration/controll  communication channel. Proxy-API translates given request and forwards it to non-oneM2M platform. If it is needed it  responds using the same communication channel. This process is also depicted on steps 2 of Figure 2 (same flow with configuration flow).

### Alternative Flow

None

### Post-conditions

None

### High Level Illustration

figure X depicts high level illustration of describing use case. Data streaming communication channel is out of one-M2M scope and is separated from authentication and non-oneM2M node configuration/control  communication channels. According to Figure X, it’s possible that the Data streaming to be received by another user application(s).

Figure X Call flaw for configuration and authentication

### Potential Requirements

- The M2M System shall be able to distinguish between the raw dataflow and the configuration/control flow for the purpose of authentication.

- The M2M System shall be able to provide an authentication framework of  user application to the non-M2M vendor’s specific node.