| Input Contribution |
| --- |
| Meeting ID* | TP-34 |
| Title:* | Use case: Automated Valet Parking (AVP) |
| Source:* | M. Djurica, TNO, Miodrag.djurica@tno.nl M. Bauer, NEC Europe Ltd., martin.bauer@neclab.eu M. ben Alaya, Sensinov, benalaya@sensinov.com Bei Xu, Huawei, Echo.xubei@huawei.com Yongjing Zhang, Huawei, Zhangyongjing@huawei.com G. Romano, Telecom Italia, giovanni.romano@telecomitalia.it |
| Date:* | 2017-03-05 |
| Input related to* | TR-0026, adding new use cases focused on autonomous driving |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* | Add Automated Valet Parking use case to TR-0026. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

## 1 Use Case on Automated Parking

## 1.1 Description

- The concept of Valet Parking is widely used all over the world; for example, the more  luxurious hotels and restaurants, stores and other businesses.

- Once a customer arrives with his/her vehicle at the hotel, he/she gets out of the vehicle and hands over the car-keys to the hotel personnel, which will then drive the vehicle to its parking spot, relieving the customer from that task. In the meantime, the owner of the vehicle can e.g. check-in or attend a meeting. Likewise, the vehicle is returned by the hotel personnel upon the request of the relevant customer. Utilising the technology evolution of self-driving vehicles, it logical next step to also automate the valet parking concept, further referred to as Autonomous Parking, or AP.

- In AP (see Figure 1), the autonomous vehicle will park itself after the driver has left the car (step 1) at a drop-off point, which may be located near the entrance of a parking lot. The autonomous vehicle will find an available parking spot (step 2) and drive and park itself (step 3). When the driver wants to leave the site, he/she will simply request from the autonomous vehicle to return by itself (step 4) to the collect point, using (for example) a smartphone app.

- ?

- Figure 1: Automated Parking Sequence.

To navigate safely around the parking lot to its destination, the Automated Driving (AD) vehicle uses information about the environment around the vehicle. The vehicle can use its own functions and sensors to observe immediate environment, but it can also benefit from gathering additional data going beyond what its sensor can observe – like accessing IoT platforms which can provide data and functions based on IoT enabled sensors like parking cameras, as well as position info from other vehicles driving (or being parked) at parking. Furthermore, IoT platforms may provide information to support services for booking a parking place and arranging (automated) payment.

## 1.2 Source

REQ-2018-0012-Use_case_on_Automated_Valet_Parking.

## Actors

# Vehicle owner

Profits from the AP service by decreasing the required time to park the vehicle (shorter drive), or by choosing cheaper parking garage, or by increasing the probability of finding a free slot in the parking area and decreasing the probability of vehicle accidents in the parking area.

# IoT platform provider

It operates an IoT platform which is collecting data from vehicles, parking spots, roads, other participants in traffic present, and from surrounding associated infrastructure (traffic lights, cameras, etc.).

# Autonomous Parking application provider

Party that is providing Automated Parking Service (APS). It collects dat from different sources relvant for parking of the vehicle (from parking garage, or smart city on available parking spots in the street). It processes data and gives destination to AD vehicle where to park itself.

# Communication Network provider

Provides connectivity between vehicles, roads, parkings and associated infrastructure.

## 1.4 Pre-conditions

The vehicle supports autonomous driving - meaning it is capable of autonomously driving.

## 1.5 Triggers

AP function (sending vehicle to park itself, as well as calling it back to pick up point) is activated by vehicle driver.

## 1.6 Normal Flow

- The APS continuously collects data from vehicles, parking garages, smart city (on available parking spots), VRU’s, smart city camera’s,…

- When receiving request from end-user for finding a parking spot for particular vehicle, APS will determine which parking spots fulfils criteria as given or being end-user’s profile. For example that can be ‘find closes garage’, ‘park on street’, ‘park on restaurant’s plot’,…

- ASP publishes, and subscribed vehicle get from oneM2M location of parking spot.

## 1.6.1 Example of data published by APS

Here we present example of data (name-type-value) that can be used.

| Parking location | Description |
| --- | --- |
| + messageID: uint8 | Unique message ID, as defined in ETSI EN 302 637 |
| + stationID: uint32 | Unique station (vehicle) ID as defined in ETSI EN 302 637 |
| + generationTimestampUTC: uint64 | The elapsed time since midnight January 1st 1970 UTC in miliseconds. (with leap seconds) |
| + latitude: WGS84 double | Coordinate for parking space defined in ETSI EN 302 637 |
| + longitude: WGS84 double | Coordinate for parking space defined in ETSI EN 302 637 |
| + altitude: WGS84 double | Coordinate for parking space defined in ETSI EN 302 637 |

## 1.7 Alternative Flow

None.

## 1.8 Post-conditions

Vehicle stays in AP mode until it is removed from it by end-user, typically after picking up end-user.

## 1.9 High Level Illustration

# Figure 1: Example of IoT data streams and corresponding communication networks

## 1.10 Potential Requirements

- The M2M system shall support the the AP related data (for example available parking places and their location) exchange between the vehicle and the platform.

- M2M system shall support a standardized information model for AP including model for parking places – both in garage and in streets.

- OneM2M should support a profile for valet parking with a consistent information model Based On existing information models (e.g. ETSI ITS, DATEX and Sensoris).

# Text boxes

Mobile network

APS