| Input Contribution |
| --- |
| Meeting ID* | REQ 34 |
| Title:* | Service Subscriber Users TR Limitation |
| Source:* | Dale Seed, Convida, Seed.Dale@convidawireless.com Catalina Mladin, Convida, Mladin.Catalina@convidawireless.com |
| Date:* | 2018-03-02 |
| Input related to* | WI-0083 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* | Agree definition |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This is a proposal to ammend and clarify the definitionof M2M Service Users.

R01 contains changes agreed at REQ#34

### -----------------------Start of change 1-------------------------------------------

## 3.20	S

Secure [i.12]: not vulnerable to most attacks, are able to tolerate many of the attacks that they are vulnerable to, and that can recover quickly with a minimum of damage from the few attacks that successfully exploit their vulnerabilities

Security [i.5]: system condition that results from the establishment and maintenance of measures to protect the system

Security Association: set of shared security attributes necessary to perform secure communication between two entities (CSEs and/or AEs) which have performed Mutual Authentication.

NOTE:	The security attributes include a description of the algorithms to be applied, and derived keys which are applied for the lifetime of the security association.

Security Association Establishment: procedure for establishing a Security Association between two entities (CSEs and/or AEs)

Security Pre-Provisioning: process of providing a credential into a secure environment of the Node prior to device deployment, e.g. during manufacturing

Security Provisioning: process of configuring a credential into a secure environment of a Node to enable access to a service provided by a target entity, such as communication services or M2M Services

NOTE:	This involves putting in the device and target entity the security Credentials that will be used for Mutual Authentication.

Sensing and Actuation (S&A) Equipment: equipment that provides functionality for sensing and/or influencing the physical environment by interacting with one or more M2M Application Services

NOTE:	Sensing and Actuation Equipment can interact with the oneM2M System, however does not host an M2M Application. The specification of S&A Equipment is not considered in the current oneM2M specifications. S&A Equipment may, but does not need to, be co-located with an M2M Device.

Sensitive Data: classification of stakeholder's data that is likely to cause its owner some adverse impact if either:

- It becomes known to others when not intended.

- It is modified without consent of the affected stakeholder.

M2M Service: consists of one or more M2M Application Services and one or more M2M Common Services

M2M Service Administrative State of a M2M Device: indicates whether the M2M Service is enabled by the M2M Service Provider to be run for this device

M2M Service Infrastructure: physical equipment (e.g. a set of physical servers) that provides management of data and coordination capabilities for the M2M Service Provider and communicates with M2M Devices

NOTE:	An M2M Service Infrastructure may communicate with other M2M Service Infrastructures. An M2M Service Infrastructure contains a CSE. It can also contain M2M applications.

M2M Service Operational Status of a M2M Device: indicates whether the M2M Service is currently running for this device

M2M Service Provider: entity (e.g. a company) that provides M2M Common Services to a M2M Service Subscriber

M2M Service Subscriber: M2M Stakeholder that subscribes to a M2M Service Provider to consume its M2M Service(s)

M2M Service Subscription: agreement between a M2M Service Provider and a M2M Service Subscriber for consumption of M2M Services for a period of time

NOTE:	An M2M Service Subscription is typically a commercial agreement.

M2M Service User: an entity authorized by a M2M Service Subscriber to use M2M Services. M2M Session: service layer communication relationship between endpoints managed via M2M Common Services consisting of session authentication, connection establishment/termination, transmission of information and establishment/termination of Underlying Network services

M2M Solution: set of deployed systems satisfying all of the following criteria:

- it satisfies the end-to-end M2M communication requirements of particular entities; and

- some part of the M2M Solution is realized by including services compliant to oneM2M specifications.

M2M Stakeholder: entities who facilitate and/or participate in the legitimate operation of the oneM2M system

NOTE:	Examples of stakeholders, in alphabetical order, are:

- M2M Application Service Provider;

- Manufacturer of M2M Devices and/or M2M Gateways;

- Manufacturer of oneM2M system and its components;

- M2M Device/Gateway Management entities;

- M2M Service Provider; Network Operator;

- M2M Service Subscribers;

- M2M Service Users;

- etc.

Static Device/Gateway Context: static metrics, which may impact the M2M operations of M2M Devices/Gateways

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 3.22	U

Underlying Network: functions, networks, busses and other technology assisting in data transportconnectivity services

### -----------------------End of change 2-------------------------------------------