| Input Contribution |
| --- |
| Meeting ID* | TP-34 |
| Title:* | Data model for use case: Platooning |
| Source:* | M. Djurica, TNO, Miodrag.djurica@tno.nl H.J.D. van der Sluis, Jacco.vandersluis@tno.nl |
| Date:* | 2017-03-05 |
| Input related to* | TR-0026, data model to be used for use cases for vehicular domain |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* | Informative data model to be used for Platooning use case. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

## 1 Introduction of data model for Platooning

This is informative document presenting data model that is used for use case platooning, as it is implemented in EU LSP (large Scel; Pilot) Autopilot (http://www.autopilot-project.eu).

Data model is based on elements of already existing models like Sensoris, DATEX II, CAM,… And the definition which data is needed for particuloar use case is coming from Autopilot project, and responsible implementation teams.

Data model contains Name and Type.

## 1.1 Data sent from Vehicle / Platoon – IoT CAM

This is data object that vehicle sends to other participants in traffic informaing them on (own) location, state and time.

| IoT_CAM | Description |
| --- | --- |
| + messageID: uint8 | as defined in ETSI EN 302 637_2 v010302 |
| + stationID: uint32 | as defined in ETSI EN 302 637_2 v010302 |
| + generationDeltaTime: uint16 | generationDeltaTime = timestampIts mod 65 536, ETSI EN 302 637_2 v010302 |
| + generationTimestampTAI: uint64 (ms since 2004) | TAI time value in milliseconds since 00:00:00.000 hours of 01 January 2004 UTC |
| + generationTimestampUTC: uint64 | The elapsed time since midnight January 1st 1970 UTC in miliseconds. (with leap seconds) |
| + stationType: (1..225) int | defined in ETSI EN 302 637_2 v010302, |
| + latitude: WGS84 double | defined in ETSI EN 302 637_2 v010302 |
| + longitude: WGS84 double | defined in ETSI EN 302 637_2 v010302 |
| + heading: WGS84 (0..360) | defined in ETSI EN 302 637_2 v010302 |
| + speed: (0..163) m/s | defined in ETSI EN 302 637_2 v010302 |

## 1.2 Data on shared world model

Currently not implemented in Autopilot, reserved for future use. This would typically include information of other (detected by the vehicle sensors) relevant vehicles (targets)  and/or information of the road segment it is currently driving.

| SharedWorldModel | Description |
| --- | --- |
| + stationID: uint32 | as defined in ETSI EN 302 637_2 v010302 |
| + targetID: double | as defined in ETSI EN 302 637_2 v010302 |
| + generationTimestampUTC: uint64 | The elapsed time since midnight January 1st 1970 UTC in miliseconds. (with leap seconds) |
| + targetPosition: Location | defined in ETSI EN 302 637_2 v010302 |
| + targetGeometry: string |  |
| + roadSegmentInfo: string |  |

## 1.3 Data for platoon formation advice

This is data that is sent from roadside platooning service to vehicle that wants to join an already existing platoon in its vicinity.

| FormationAdvice | Description |
| --- | --- |
| + messageID: uint8 | as defined in ETSI EN 302 637_2 v010302 |
| + stationID: uint32 | as defined in ETSI EN 302 637_2 v010302 |
| + platoonID: uint32 | TBD, will use same format as stationID |
| + generationTimestampUTC: uint64 | The elapsed time since midnight January 1st 1970 UTC in miliseconds. (with leap seconds) |
| + speedAdviceValue: array float32 | Last known latitude of the engaging vehicle in put in here by and updated only by the PlatoonService. |
| + speedAdviceStartTime: array uint64 | Last known longitude of the engaging vehicle in put in here by and updated only by the PlatoonService. |
| + speedAdviceStopTime: array uint64 | The elapsed time since midnight January 1st 1970 UTC in miliseconds. |

## 1.4 Data on platoon status

This is data that leading vehicle of the platoon sends to roadside (platooning service in whcihc it informs it about state of the platoon. Same dat can be sent laso by any other vehicle in the platoon.

| PlatoonStatus | Description |
| --- | --- |
| + messageID: uint8 | as defined in ETSI EN 302 637_2 v010302 |
| + stationID: uint32 | defined in ETSI EN 302 637_2 v010302 |
| + platoonID: uint32 | TBD, will use same format as stationID |
| + generationTimestampUTC: uint64 | The elapsed time since midnight January 1st 1970 UTC in miliseconds. (with leap seconds) |
| + platoonState: uint8 (enum) | None(0), Standalone(1), VehicleEngaging/Assembling(2), Platooning(3), VehicleDisengaging(4), DisengagingAll(5) |
| + platoonDestination: string | Global platoon desitnation eg (cities); Eindhoven..Helmond |
| + vehicleRole: uint8 (enum) | None(0), Standalone/Ready-for-leading(1), Trailing(2), Following(3), Leading(4), Ready-for-leading(5) |
| + vehicleMode: uint8 (enum) | None(0), Standalone(1), Engaging(2), Platooning(3), Disengaging(4), Searching(5), Forming(6) |
| + platoonSize: uint8 | Number of vehicles in platoon |

## 1.5 Data for platoon navigation

This is sent by roadside service to leading vehicle of the platoon. It is end destination of the platoon, with optional waypoints in between.

| PathToPointOnMap |  |
| --- | --- |
| + stationID: uint32 | defined in ETSI EN 302 637_2 v010302 |
| + generationTimestampUTC: uint64 | The elapsed time since midnight January 1st 1970 UTC in miliseconds. (with leap seconds) |
| + destinationLatitude: WGS84 double | defined in ETSI EN 302 637_2 v010302 |
| + destinationLongitude: WGS84 double | defined in ETSI EN 302 637_2 v010302 |
| + path: | TBD (it is collection of waypoints) |

## 1.6 Platoon driving advice

This is set of data representing advice (from roadside) to platoon with info on speed advice etc.

| PlatoonAdvice | Description |
| --- | --- |
| + messageID: uint8 | as defined in ETSI EN 302 637_2 v010302 |
| + stationID: uint32 | defined in ETSI EN 302 637_2 v010302 |
| + platoonID: uint32 | TBD, will use same format as stationID |
| +generationTimestampUTC: uint64 | The elapsed time since midnight January 1st 1970 UTC in miliseconds. (with leap seconds) |
| + trafficIntensity: string | tbd |
| + speedAdviceValue: array float32 | The array can be of variable length number of elements. [12.5, 13.0, 14] |
| + speedAdviceStartTime: array uint64 | The array can be of variable length number of elements. [1515493681, 1515493690, 1515493699] |
| + speedAdviceStopTime: array uint64 | The array can be of variable length number of elements. [1515493681, 1515493690, 1515493699] |
| + laneAdvice: string | lane number from left to right in the current road driving direction |

## 1.7 Traffic light information

This is information on traffic lights. When having few vehicles in the platoon, one would like to avoid splitting of the platoon. Traffic light info is combined with platoons statre (speed, location) to establish whener the platoon can go uninterrupted through traffic light.

| trafficLightInfo (IoT_SPAT) |  |
| --- | --- |
| + id: String | Traffic light ID, TBD |
| +timestampUTC | the mSec point in the current UTC minute that this message was constructed (see J2735_201603) |
| + stationID | as defined in ETSI TS 102 894-2 V1.2.1 (2014-09) |
| + intersectionID | Unique ID of Intersection, as defined in J2735_201603 |
| + moy | Optional: minute of the year, used only with messages to be archived as defined in J2735_201603 |
| signalGroupID | SignalgroupID is used to map to lists of lanes. as defined in J2735_201603 |
| state-time-speed: | Sequence with information on eventstate, timing and speeds as defined in J2735_201603 |
| + speeds | As part of the state-time-speed: sequence with information on type, speed advice, speed confidence and distance (zone length). |

## 1.8 Platoon formation – declaring intention to platoon

This is information sent by vehicle that declares own intention to join a platoon going in particular direction.

| PlatoonFormation (car wants to platoon) |  |
| --- | --- |
| + messageID: uint8 | as defined in ETSI EN 302 637_2 v010302 |
| + stationID: uint32 | defined in ETSI EN 302 637_2 v010302 |
| + platoonID: uint32 | TBD, will use same format as stationID |
| + generationTimestampUTC: uint64 | The elapsed time since midnight January 1st 1970 UTC in miliseconds. (with leap seconds) |
| + latitude: WGS84 double | defined in ETSI EN 302 637_2 v010302 |
| + longitude: WGS84 double | defined in ETSI EN 302 637_2 v010302 |
| + ETA(timestampUTC): uint64 | The elapsed time since midnight January 1st 1970 UTC in miliseconds. (with leap seconds) |
| + rendevouzPointLatitude: WGS84 double | defined in ETSI EN 302 637_2 v010302 |
| + rendevouzPointLongitude: WGS84 double | defined in ETSI EN 302 637_2 v010302 |
| + speedAdviceValue: array float32 |  |
| + speedAdviceStartTime: array uint64 | The elapsed time since midnight January 1st 1970 UTC in miliseconds. (with leap seconds) |
| + speedAdviceStopTime: array uint64 | The elapsed time since midnight January 1st 1970 UTC in miliseconds. (with leap seconds) |
| + handOverToPS: boolean | Handover to Platooning Service or not |

## 1.10 Used terminology:

CAM – Cooperative Awareness Message ETSI European Norm 302 637-2

WGS84 – World Geopdetic system (release from1984) is the standard U.S. Department of Defense definition of a global reference, see https://en.wikipedia.org/wiki/World_Geodetic_System