| Input Contribution |
| --- |
| Meeting ID* | REQ34 |
| Title:* | Resource Reservation for Public Services |
| Source:* | Catalina Mladin, Convida Wireless, Mladin.Catalina@convidawireless.com |
| Date:* | 2018-07-10 |
| Input related to* | WI-0015 Usecases Collection TR-0001 V 4.2.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) |  |
| Decision requested or recommendation:* | Agree for inclusion in TR-0001. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution provides a use case for Clause 8 of TR-0001.

### ---------------------- Start of change 1-------------------------------------------

## 8.x	Resource reservation for public services

### 8.x.1	Description

In a Smart City environment, a central management coordinator interacts with hundreds of devices and vehicles owned and operated by different stakeholders: public service managers and end-user applications, traffic and transportation apps from local companies, stakeholders and users, vehicles and sensors from municipality, universities, etc. Some devices, such as those for public services, allow the central coordinator access to specific resources hosted locally on the device, with access control managed at the device level. In an emergency or special event situation the coordinator needs uninterrupted access (albeit for short periods of time) to specific resources on all these devices, and for their state to be unchanged by other entities. For example, reservation 1 (see Figure 4) will be needed temporarily for shuttles and traffic lights in a specific area, in order to coordinate traffic when emergency public works are performed . Another reservation (2) is needed for resources on end-user’s mobile devices to allow for updates with critical event information while temporarily blocking changes, for example, from the bus system.

The usecase requires that entities (such as the management applications) can make reservations on their own behalf or others’, including groups of applications, etc. Such actions normally require changes in the ACPs resources in many devices, where the ACPs are distinct from each other. This requires individual RESTful operations to be performed for each change, with a large messaging overhead.

This usecase requires a more dynamic procedure. Pre-provisioned policies for reservation (for the security of the system) are used to enable reservations via simple/dynamic requests such as: “allow THIS specific Originator (which already has privileges in all these heterogeneous and distributed ACPs), to reserve the resource temporarily, with the existing privileges”.

### 8.x.2	Source

REQ-2018-00xx: Resource reservation for public services

### 8.x.3	Actors

Originator: It is the entity that requests a reservation of resources, either in its own behalf or on behalf of other entities, termed privileged entities (for the duration of the reservation).

Host: Entity hosting resources and providing services using reservation mechanisms.

Privileged Entity: Entity requesting access to reserved resources at the Host during a reservation on its behalf; the access is allowed subject to reservation policy and Access Control.

Non-Privileged Entity: Entity requesting access to reserved resources at the Host during a reservation on another entity’s behalf; the access not allowed subject to reservation policy and Access Control.

### 8.x.4	Pre-conditions

Reservation Policies are created along with Access Control Policies

### 8.x.5	Triggers

None.

### 8.x.6	Normal Flow

# Figure 8.x.6-1: Resource Reservation flow

The flow in Figure 8.x.6-1 distinguishes the following steps:

- Reservation setup :  During this step the target resource Host is enabled to provide services using (or based on) reservations by being provided with Reservation Policy information.

- Reservation request/triggering:   During this step a Reservation Instance is created or triggered.

There may be several types of reservation, depending on triggering methods:

  - Explicit: A reservation requester provides directly all the reservation information that allows the Host to enforce the reservation (on behalf of the requester or another privileged entity)

  - Request-based/ Implicit: A RESTful request is used to trigger a reservation, with reservation parameters (scope) provided implicitly, i.e. determined by the Host based on the local information.

  - Event-based/ Implicit: A specific event monitored by the Host triggers the reservation, with reservation parameters (scope) provided implicitly, i.e. determined by the Host based on the local information

- Reservation authorization and creation

This step is closely linked to the triggering procedure in that the reservation request received is authorized based on the information available at the Host from the setup phase (Reservation Policy). If authorized, it results in a new Reservation Instance being created. The parameters (scope) of the Reservation Instance are based on the Reservation Policy as well as information included in step 1.

- Management of external requests during reservations:

  - From privileged entities

  - From non-privileged entities

During the reservation the Host processes requests based on the reservation rules. The processing of Privileged Requests is different than the processing of Non-Privileged Requests.

- Reservation stop or release:

This step is also closely linked to the triggering procedure in that the method for reservation stop or release depends on the triggering method. Differential processing of incoming requests ceases.

### 8.x.7	Alternative Flow

None

### 8.x.8	Post-conditions

### 8.x.9	High Level Illustration

# Figure 8.x.9-1 Resource Reservation for Public Services

### 8.x.10	Potential requirements

- The oneM2M System shall provide capabilities to provide reservation of resources at resource hosts for limited time, based on pre-provisioned resource reservation policies and reservation request, and subject to access control.

### -----------------------End of Change 1 ---------------------------------------------

# Text boxes

Reservation 1

Reservation 2