| Input Contribution |
| --- |
| Meeting ID* | REQ-37 |
| Title:* | Use case on Vehicle Remote Control using Artificial Intelligence Platform |
| Source:* | Joonyoung Kim, Hyundai Motor, jkim@hyundai.com Minbyeong Lee, Hyundai Motors, minbyeong.lee@hyundai.com Youngjin Na, Hyundai Motors, yjra@hyundai.com |
| Date:* | 2018-09-10 |
| Input related to* | TR-0026, Adding new use case on Vehicle Remote Control |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0002 |
| Decision requested or recommendation:* | Add new use case on Vehicle Remote Control for artificial intelligence platform to TR-0026. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 6.XX Vehicle Remote Control using Artificial Intelligence Platform

## 6.XX.1    Description

Vehicle remote control is a function or service to access the vehicle for its control or necessary information. Vehicle remote control services are currently used with a wide range of functions from ignition to destination setting in navigation platform.

In general, a vehicle is equipped with a telematics unit which has a modem for the connection of telematics services. Protocols of telematics communications can be consisted of various different forms, such as TCP, HTTP, and SMS gateway. With respect to security and financial reasons, telematics communication tends to be highly secure and only remain short period of time. SMS gateway system is a prime example for that.

Figure 6.XX.1: Generic Diagram of Telematics System for Vehicle Remote Control with SMS Gateway

In figure 6.XX.1, external platform conducts vehicle remote control by accessing to telematics server to control vehicles. Note that external platform can be forms of application, server, or other vehicle platform.

In recent days, Artificial Intelligence (AI) platform is widely popular in information technology industry and various studies focus on in-depth about the integration of AI Platform to nodes including vehicles. AI platform has potentials for objects in a sophisticated manner. However, it has an issue with security.

For instance, if AI platform is granted to access vehicle ignition or auto-driving mode, AI platform may control ignition and drive on the highway under no driver presence without any intention of drivers. To prevent this case, the level of authorization must be established based on the security level of vehicle function.

In order to determine the level of authorization, vehicle functions have to be categorized by following items, i) Autonomous capability and notification requirement, ii) Visual activities and self-damage possibilities, iii) Vehicle component access (e.g. information, Engine, transmission, and accelerator).

Autonomous capability and notification requirement are to review the capabilities and seriousness of vehicle functions. If they are capable of operating on its own with risk-free, it can be in a pool of authorization granted. Visual activities and self-damage possibilities are looking in the aspects of whether or not the operation of vehicle functions is visible and harmful to surrounding environments.  Vehicle component access is the critical authorization part due to the fact that hacker or unexpected outsider can access and control vehicle for any damage and casualty.

Thus, based on three items, the authorization level can be categorized as follows.

- Required Authorization (Level 1)

  - No autonomous, required approvals in every step

  - Visual activities, Self-damage

  - Engine, transmission access(e.g. engine ignition, air-conditioning, Autonomous Parking)

- Partially Authorized (Level 2)

  - Partial autonomous, at least should be approved by users

  - Visual activities, No self-damage

  - No engine, transmission access (e.g. light, horn & light, door lock, Electricity charging)

- Fully Authorized (Level 3)

  - Fully autonomous, not require to notify users

  - No visual activities, No self-damage

  - Information access & transfer(e.g. fuel gauge, Navigation Location, Over-The-Air update)

Each component is granted to one of three levels and it can set their authorization level up to the granted level. For instance, if the navigation information is granted to level 3, it can set its authorization level 1, 2, or 3. However, if the electric charging is granted to level 2, it can only set its level 1 and 2, but not 3.

Figure 6.XX.2: Example of Vehicle Remote Control for AI Platform

Figure 6.xx.2 is an example of vehicle remote control that the driver checks fuel gauge of the vehicle using AI platform. In this scene, AI speaker is a form of voice interface between driver and AI platform. Assuming the fuel gauge information is with level 3, the vehicle and AI platform communicates each other to transfer fuel gauge information. At the end, the AI platform informs the driver with current fuel status of the vehicle.

## 6.XX.2    Source

REQ-2018-00XX- Use case- Vehicle Remote Control using Artificial Intelligence Platform

## 6.XX.3    Actors

# Vehicle

# Vehicle is a nomadic object monitored by oneM2M infrastructure node through telematics server. It is equipped with a telematics unit as a form of modem hardware. (E.g. 3G, LTE modem).

# External Platform

# TBD.

# Telematics Server

TBD.

# oneM2M Infrastructure

# In charge of providing common functionalities for the M2M services.

## 6.XX.4    Pre-conditions

- TBD

## 6.XX.5    Triggers

None.

## 6.XX.6    Normal Flow

# Figure 6.XX.3: Normal Flow - Car-to-Home based on Geo-Fence

- update.

## 6.XX.7    Alternative Flow

None.

## 6.XX.8    Post-conditions

None.

## 6.XX.9    High Level Illustration

# Figure 6.XX.5: High Level Illustration – Vehicle Remote Control for AI Platform

## 6.XX.10    Potential Requirements

- oneM2M system shall be able to set authority level based on security importance of vehicle function in case of vehicle remote control using artificial intelligence platform.