| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 |
| Title:* | Description of Levels of assurance for authentication |
| Source:* | Giesecke & Devrient |
| Contact: | Claus Dietze, claus.dietze@gi-de.com |
| Date:* | 2013-08-06 |
| Abstract:* | Adds a description of basic security concepts to section 6.3 of the security TR |
| Agenda Item:* |  |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | oneM2M-TR-0008-Security-V0_1_0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include section 6.3.x into oneM2M-TR-0008-Security-V0_1_0 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### 6.3	Security Concepts

### Implementing security features and countermeasures to threats requires mechanisms that provide security related operations with an appropriate level of confidence. Those generic mechanisms are described within this clause. They include:

### secure storage of sensitive data

### sensitive functions executing operations on sensitive data

### secure connection allowing the secure transmission of sensitive data

### 6.3.1	Secure Storage

### Sensitive data comprises key material / credentials, privacy related data such as identifiers and other data as identified by the M2M solution provider for the purpose of its use case. In order to prevent misuse of sensitive data, it requires protected and secure storage within the termination points of the system. Secure storage capability can be implemented by several means within the network infrastructure nodes and network applications by the M2M service provider. In addition it need to be ensured that secure storage capabilities are present in termination points residing at the consumer, i.e. in the M2M Device and/or the M2M Gateway, depending on the requirements of the use case. It is recommended that M2M Devices / Gateways support a secure / tamper resistant storage capability for sensitive data.

#### 6.3.2	Sensitive Functions

### All security features as described within the remainder of this document rely on the secure execution of certain sensitive functions. Sensitive functions operate on sensitive data that is securely stored such that sensitive data will never leak to any unauthorized entity. Sensitive functions are typically performed in termination points within the M2M system.

### Examples of sensitive functions include:

### cryptographic algorithms

### (session) key derivation functions

### hash functions

### Access to sensitive functions is subject to security policies and access control. Sensitive functions are accessible via a well defined interface.

## Security Requirements

Editor's Note: This clause is intended to capture the security requirements for solving key issues. The requirements are mapped to the relevant threats.

### …