| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 |
| Title:* | Security CSF Architecture |
| Source:* | Giesecke & Devrient |
| Contact: | Claus Dietze, claus.dietze@gi-de.com |
| Date:* | 2013-xx-yy |
| Abstract:* |  |
| Agenda Item:* |  |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | oneM2M-TS-0003-Security_Solutions-V0_0_0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include chapters below into oneM2M-TS-0003-Security_Solutions-V0_0_0 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction and topics for discussion:

Following proposed text is not completed yet. The intention is to discuss and agree on an approach and a high level architecture for the Security CSF.

Following topics were considered when creating this proposal:

- Security CSF is implemented as a CSF rather than an Enabler Function – once the concept of enabler function is clarified by ARC we may want to reconsider the approach.

- The architecture is modular and consists of components that can be configured according to the requirements and circumstances of the respective use case and physical device/gateway/node.

- The assumption is that e.g. depending on the device class the architecture will be implemented differently. It is further assumed that there may be alterations of the architecture depending on the real life situation however the API functions shall remain stable.

- There may be a need to elaborate further on requirements on the Security CSF depending on the node it resides in. There may be different requirements on a Security CSF within an infrastructure node compared to a Security CSF residing in an Application Service Node

- The resource structures need further elaboration and are not yet completed. For some security functions the RESTful approach may not be suitable (see above bullet on enabler function vs. CSF). Once the structure is clarified the tables will be filled in.

- Security CSF offers its functions over the X and Y reference points. In addition it also offers its service capabilities to other CSFs within the same CSE. This interface may need to be considered separately.

=================== Proposed addition to Security TS ====================

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[x]	Open Mobile API specification V2.0.2

[y]	GP TEE Client API….

## 2.2	Informative references

[i.1]	oneM2M-TR-0008-Security-Vx_y_z

[i.2]	3GPP TR 33.868 V0.13.0; Security aspects of Machine-Type and other Mobile Data Applications Communications Enhancements; (Release 12)

## 3.1	Definitions

Local CSF:  A CSF may provide services to another local CSF, i.e. a CSF that is present in the same CSE than the CSF providing the services.

# 5	Security CSF Architecture

## 5.1	Overview

The following figure provides an overview of the Security CSF architecture.

The architecture consists of following layers:

- Application layer

- Service layer

- Security Transport layer

Editor’s note: Blue components may be Enabler Functions rather than resources of a CSF.

Design principles:

- The architecture is split into several components and sub-components providing a modular design. With this design, mapping of the architecture to different nodes and entities is enabled

- The current architecture does not follow a strict RESTful approach. The Security CSF may need to be split into a pure CSF and certain Security Enabler Functions.

- Depending on the requirements of each entity, the Security CSF should consist of components relevant to fulfil the requirements of the respective node or entity and the intended use case

- The architecture may need to be adapted to be suitable for implementation in different entities. For example, the architecture can be mapped to different device classes.

- A plug-in concept for the security transport layer allows to extend the Security CSF depending on the available Secure Environment

- The security administration component shall enable administration of all sensitive resources (data and functions) within the Security CSF and shall also allow configuration and extension of the Security CSF itself

- The Secure Environment within the Security CSF is accessed via the Security Transport layer and shall hold all sensitive resources

## 5.2	Resource Structure

Following figure shows the resource structure of the Security CSF. Further elements may be added as needed. Those elements are described further in sections below.

Editor’s note: RESTful approach may only be suitable for a subset of the Security CSF functionality. Functions that are put into an enabler function (highlighted in blue in above figure) need to be considered. Alternatively, a new resource type <Function> may be needed. Security Transport not classified as resource and therefore not included in the tree.

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| Sensitive Data Handling |  | 1 | Indicates which Sensitive Functions and Secure Storage capabilities are available |
| Secure Environment |  | 1..n | Describes the number and types of Secure Environment available within the Security CSF |
| Tbd… |  |  |  |

| AttributeName | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| Access Rights | 1 | RO | Describes the access rights of the Security CSF itself |
| Security Level | 1 | RO | Indicates the security levels supported by the Security CSF |
| Attributes tbd |  |  |  |

## 5.3	Security CSF Layer

### 5.3.1	Service Layer

The service layer consists of following components:

- Access Management

  - Authorization

  - Authentication

  - Access Control

- Sensitive Data Handling

  - Sensitive Functions protection

  - Secure Storage

- Security Association Establishment

  - Secure Connection via secure session establishment

  - Secure Connection via object security

- Security Administration (including security bootstrapping)

- Identity Protection

Each of these components provide functions and resources on the Security Service and Administration API.

### 5.3.2	Security Transport Layer

The Security Transport Layer component provides access to the Secure Environment via a general Security Transport API. A Plug-in associated to the type of Secure Environment shall provide physical / logical connectivity to the secure environment. The Security Transport Layer shall also be accessible on the Service Layer.

## 5.4	Integration within overall oneM2M architecture

The Security CSF may reside in following architectural components and interacts on the different reference points as described below:

- CSE within an Application Service Node

  - Connected via the X-Reference Point to an Application Dedicated Node

  - Connected via the Y-Reference Point to a Middle Node

  - Connected via the Y-Reference Point to an Infrastructure Node

  - Connected via the Z-Reference Point to an Underlying Network Service Entity

- CSE within a Middle Node

  - Connected via the X-Reference Point to an Application Dedicated Node

  - Connected via the Y-Reference Point to an Application Service Node

  - Connected via the Y-Reference Point to a Middle Node

  - Connected via the Y-Reference Point to an Infrastructure Node

  - Connected via the Z-Reference Point to an Underlying Network Service Entity

- CSE within an Infrastructure Node

  - Connected via the X-Reference Point to an Application Dedicated Node

  - Connected via the Y-Reference Point to an Application Service Node

  - Connected via the Y-Reference Point to a Middle Node

  - Connected via the Y-Reference Point to an Infrastructure Node

  - Connected via the Y’-Reference Point to an Infrastructure Node

  - Connected via the Z-Reference Point to an Underlying Network Service Entity

In addition the Security CSF offers its functions to other Local CSFs.

## 5.5	Configuration

The Security CSF is modular and configurable according to the needs of the hosting node, its supported reference points and its purpose. Following table indicates which components within the Security CSF are mandatory or optional. Each sub-function may have different capabilities and technical implementation depending on the purpose and the node it resides in. Implementation of components may rely on functions provided by the underlying network over the Z reference point.

Note: Security capabilities residing within the Application Entity are out of scope, however their implementation can rely on functions and resources exposed through the API provided by the Security CSF.

| Resource / Component | Child resource | M/O |
| --- | --- | --- |
| Access Management | tbd | O Note: depending on use case |
| Security Transport | n/a | M |
| Sensitive Data Handling | Sensitive Function | O Note: depending on use case |
|  | Secure Storage | M |
| Security Administration | Tbd | M |
| Secure Association Establishment | Tbd | O Note: depending on use case |
| Identity Protection | Tbd | O Note: depending on use case |

Configuration of the Security CSF is either done via the Security Administration component or during production of the respective entity.

The architecture shall support a plug-in concept that allows adding further security functions and secure environments.

# 6	Security CSF Implementation

## 6.1	Interaction on Reference Points

### 6.1.1	X-Reference Point

The Security CSF offers Application Entities / Application Dedicated Nodes its API through the X-Reference point. Implementation of the Security CSF is dependent on the operating system of the physical device it resides in.

Editor’s note: Categories of physical devices are currently discussed in WI-0006. Depending on the outcome of this WID, definitions of Security CSF may have to be adapted.

### 6.1.2	Y-Reference Point

Editor’s note: This section covers topics related end-to-end secure channel establishment between CSEs

### 6.1.3	Y’-Reference Point

Editor’s note: This section covers topics end-to-end secure channel establishment in case they are different to Y-reference point. In addition there may be relation to topics such as M2M Subscription Management / Identifier handling.

### 6.1.4	Z-Reference Point

Editor’s note: This section covers topics such as GBA and Remote Subscription Management.

#### 6.1.4.1.	Interworking with 3GPP networks

Add reference to [i.2].

### 6.1.5	Security CSF – CSF Interface

Editor’s note: If this section is required is FFS.

Over this interface Security CSF functions are exposed to other Local CSFs. CSFs residing in external CSEs have access to the Security CSF via the Y or Y’ reference point.

## 6.2	Internal Components

### 6.2.1	Registry

Editor’s note: Further internal components such as a registry are FFS. This internal component may be needed to store management related information.

## 6.3	Service Layer Components

### 6.3.1	Access Management

#### 6.3.1.1	Access Control

The access control component controls access of Application Entities and CSEs to security resources within the Security CSF. Access Control is used by the service and Security Transport layer. Requesting entities access the security CSF functions via the X, Y or Y’ reference point. Based on the access policies stored within the secure environment, the access control function within the security CSF grants or rejects access of the requesting entity to the called Security CSF function, depending on the requested action and affected resources.

Access Control Flow:

Step 001:	The Originator AE or CSE calls a Security CSF function

Step 002:	The Security CSF shall forward the request to the Access Control resource together with the respective identifiers of the calling entity and related authentication material

Step 003: 	The access control component shall verify the access rights and grant access to the function requested by the Originator AE/CSE.

Step 004:	Access control provides a response on the access control verification to the Security CSF

Step 005:	Depending on the response of the access control component, the security CSF shall processes (or reject) the called function.

Step 006	Security CSF function provides result / response to the originating AE/CSE

#### 6.3.1.2	Authorization

The Authorization component provides other CSFs within the same or a distant CSE with functions to authorize access of AEs or CSEs to that particular CSF calling the Authorization component. As indicated in below figure, the requesting entity shall call functions of the CSF (located within the CSE) over the X, Y or Y’ reference point. The called CSF may want to verify the authorization status of the requesting entity and initiates an authorization request. In this case the called CSF and the security CSF reside within the same CSE. Access to the Security CSF is done via a CSE internal reference point that may be identical to the Y reference point.

Authorization Flow:

Step 001:	The originating AE or CSE requests certain functions of any CSF. In case a Security CSF function is requested the access control flow as described above shall apply.

Step 002:	The called CSF shall request to check authorization of the AE/CSE and verify if access to the called function is allowed. Therefore, the called CSF shall send an authorization request to the authorization function of the Security CSF.

Step 003: 	The Security CSF / Authorization function shall verify that the calling CSF is allowed to access the authorization function and therefore shall request an access control verification.

Step 004:	Access control shall process the verification request.

Step 005:	Depending on access control rights, the Access Control function shall send a response to the Authorization function..

Step 006	The authorization function shall process the request initiated by the originator based on the result retrieved by the access control function.

Step 007:	A response to the CSF shall be sent.

Step 008:	Based on the response, the CSF shall process the request of the initiating AE or CSE.

Step 009:	The result of the CSF processing of the request shall be sent back to the originator.

#### 6.3.1.3	Authentication

This component provides authentication services to the Application Layer.

### 6.3.2	Security Association Establishment

This component provides functions to establish a security association between different entities.

This component shall provide following functions:

- Secure Connection via secure session establishment

- Secure Connection via object security

- …

Editor’s note: to be completed.

For secure connection on 3GPP networks [i.2] applies.

### 6.3.3	Security Administration

The Security Administration component shall provide functions to manage the Security CSF including all its components, resources and attributes. This shall include management of resources provided via the secure environment. In addition it should provide functions to manage sensitive data such as identifiers and subscriptions on behalf of other CSFs.

Editor’s note: to be completed.

### 6.3.4	Identity Protection

This component provides Identity Protection services to the Application Layer.

### 6.3.5	Sensitive Data Handling

The Sensitive Data Handling component provides certain Sensitive Functions to the Application Layer.

Sensitive Functions shall include following functions:

- Secure Storage

In addition the component should support the following sensitive functions

- Cryptographic operations

- Methods for bootstrapping initial secrets (e.g. GBA)

Editor’s note: to be completed.

Resource Structure

Editor’s note: to be completed.

| Child Resource Name | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| Sensitive Functions |  | N |  |
| Secure Storage |  | 1..N |  |

| AttributeName | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| Attributes tbd |  |  |  |

#### 6.3.5.1	Sensitive Functions

This component shall provide AEs, CSEs, and CSFs with access to Sensitive Functions of the security CSF.

Resource Structure

Editor’s note: to be completed. Sensitive Functions may include cryptographic algorithms, …

| AttributeName | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| Sensitive Function ID | 1 | RO | Unique Identifier of the sensitive function |
| Version | 1 | RO | Version number of the sensitive function |
| Supported Security Level | 1 | RO | Indicates the Security Level provided by the sensitive function |

#### 6.3.5.2	Secure Storage

This component shall provide AEs, CSEs, and other Local CSFs with access to the secure storage capability of the Security CSF. Data securely stored by the AE, CSE or Local CSF shall only be accessible through the Security CSF and by authorized entities. Secure Storage should be managed by the Secure Environment. Stored data shall be associated with the entity owning the data, i.e. the AE, CSE or Local CSF that requested the data to be stored within the secure storage.

Resource Structure

Editor’s note: to be completed.

## 6.4	Security Transport Layer Components

### 6.4.1	Secure Environment

The Secure Environment component is a logical entity that provides Sensitive Functions operating on Sensitive Data, Secure Storage and other resources / functions.

There is no assumption made on the particular implementation of the Secure Environment. A SE may be implemented as an independent HW Security Element or as an integrated SW function. Each Secure Environment shall be associated with one certain Security Level depending on the particular implementation of the SE. Different Secure Environments may provide different Security Levels.

There shall be at least one Secure Environment within or accessible via the Security CSF API, however there may be multiple.

### 6.4.2	SE Plug-in

The SE Plug-in enables physical access to the respective Secure Environment. Depending on the type of Secure Environment, the SE Plug-in may be implemented differently for each Secure Environment.

NOTE: Specification of the SE Plug-in is out of scope of the present document.

### 6.4.3	Security Transport

This component shall enable entities accessing the Security Service API direct access to the Security Transport layer. For this purpose the generic Security Transport component shall expose functions provided by the Security Transport layer functions to the Application layer. The Security Transport layer is specific to the underlying secure environment. The Security Transport component provides a Transport layer agnostic interface to the Application layer. The Security Transport component provides the capability to extend the SECAPI depending on the use case with proprietary functions.

The Generic Security Transport component provides access to resources residing within the secure environment. Access to those functions shall be restricted to functions that are not addressable by the standardised SECAPI.

# 7	Security CSF API

## 7.1	API description

General description of the API…

## 7.2	Security Transport

The Security Transport API provides a communication framework to the secure environment.

The Security Transport API shall be implemented according to the Security Transport API as defined in [x].

Editor’s note: a more detailed description of the mapping of the architecture to the architectures defined in [x] and [y] may be added.

## 7.3	Authorization

Editor’s note: add API functions required to provide Authorization Service here.

## 7.4	Sensitive Data Handling

Editor’s note: add API functions required to provide Sensitive Data Handling here.

## 7.5	Security Association

Editor’s note: add API functions required to provide Security Association here.

## 7.6	Security Administration

Editor’s note: add API functions required to provide Security Administration here.

## 7.7	Identity Protection

Editor’s note: add API functions required to provide Identity Protection here.

## 7.8	Authentication

Editor’s note: add API functions required to provide Authentication Service here.