| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4(SEC) |
| Title:* | Description for Authorization functionality |
| Source:* | FUJITSU(TTC), GEMALTO (ETSI) ,Sierra Wireless(ETSI),Qualcomm(ATIS) |
| Contact: | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com Francois Ennesser, GEMALTO, francois.ennesser@gemalto.com Nicolas Damour, Sierra Wireless, ndamour@sierrawireless.com Philip Hawkes, Qualcomm,phawkes@qti.qualcomm.com |
| Date:* | 2013-10-17 |
| Abstract:* | This contribution proposed to add texts which explain authorization functionality on oneM2M platform system. R01: Renumbered in sequence diagram R02: Described OAuth as a solution for ‘token-based access controll’. |
| Agenda Item:* | Security-TR |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | TR-0008 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG4 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This follows up on the issue raised by the contribution oneM2M-PRO-2013-0027-AuthorizeDataAccess, as part of stage 3 work discussed in joint meeting with WG3 (PROTOCOL WG) in TP#6,

The issue was that an Authorization functionality should be provided in order to meet requirements regarding access control.

As the conclusion, both WG3 and WG4 members agreed on start work regarding providing an authorization functionality in oneM2M platform.

This contribution proposes adding some text which should be included as a part of TR-0008.

======[START of proposed text 1]=======

### 6.4.2	Authorization requirements

In many traditional client-server authorization models, clients can access  protected resources on the server by using the resource owner's credentials directly. This is typically done either by directly authenticating as the resource owner, or by using authorization credentials of the resource owner.

This approach, however, has the inherent limitation that the resource owner may want to grant restricted access to their resources (such as read-only, or limited in time), while they themselves retain the full access to the same resources.

When the owner of a resource wants to give such restricted permissions for using the resource to some third-party without sharing their full owner’s credentials which allows full access to said resource, there are several issues to be solved:

- The system SHOULD have a mechanism to allow a resource owner to configure the access authorization rules for restricted access by third-parties

- The system SHOULD have a capability to handle the access by third-parties which will use the resource on behalf of User.

- The system SHOULD allow the third-party to access the User’s resource even when the User is offline.

======[END of proposed text 1]=======

======[START of proposed text 2]=======

### 6.6.3	Authorization

### 6.6.3.1	Solutions for token based authorization

### Editor’s Note: description about further investigation for token based authorization, and adding more solutions are encouraged

### 6.6.3.1.1	SolutionX: OAuth

The user can use the OAuth framework to give a permission for restricted access to a third party entity in token based access controlled system. The OAuth system issues ‘access token’, which represents authorized use of the system as the proof of the user’s authorization. Note that the ‘access token’ is managed by server system associating with the ‘authorized use’,  which consists of specific scopes  and duration of access.

The third party entity can access necessary data and/or information without sharing credentials (such as user-id and password) which allows full access to the system.

In the oneM2M architecture, resource owners could be subscribers of the M2M Service, and third-party applications could be Web applications used by resource owner or by another user which is allowed to access the resource. This is of particular interest in Internet of Things scenarios, where the data streams produced by source devices owned by individual users could be made available to data consumer applications deployed by other parties.

[Status of Specification]

As described in the reference RFC6749, OAuth is an “authorization framework [that] enables a third-party application to obtain limited access to an HTTP service, either on behalf of a resource owner by orchestrating an approval interaction between the resource owner and the HTTP service, or by allowing the third-party application to obtain access on its own behalf”.

OAuth was standardized by the IETF, and there are two versions which are not compatible with each other. OAuth 1.0 is published as RFC5849, and OAuth 2.0 is published as RFC6749 to solve identified issued in OAuth 1.0.

### [Usage Scenario]

Following clause illustrates interactions to give an authorization for resource access by third-party application following OAuth 2.0. 
Note that once access-token was issued and passed  to the M2M Application, the M2M Application can get access to restricted resource providing access-token without requiring further interaction with resource owner.

Description for Use Case:

The subscriber user wants to authorize a M2M Application for accessing data

Pre-conditions:

- M2M Platform is ready to provide some data resource to be referred as URI

- The M2M Application is assigned an application-id for the M2M platform

- The condition of authorized access to the resource is pre-defined as system-wide Role.

Procedures:

- The user access to the web page to enable new service provided by M2M application using a web browser.

- The web page redirect to the authorization request page along with application-id and URI of the data. This web page can be dedicatedly prepared for allowing access from the M2M application.

- The authorization request page requests the user to enter username and password for authenticating user as owner of the resource.

- The user inputs username and password to be authenticated.

- The authorization request page show the web form page to confirm the user allowing access to the data from M2M Application which is identified by application-id.

- When user posts the form to confirm, it redirects again to the page of step2.

- The page show the message as authorization for the data access is granted, then redirect to the web page of application portal along with ‘access token’ data.

- When user opened the page, the ‘access token’ data will be sent to the Application portal.

- The Application portal page forwards the ‘access token’ to M2M Application to be used for future access to the data belongs to the user.

- M2M Application acknowledges necessary authorization is given by user.

- When the M2M Application is triggered as scheduled task, M2M Application requests to access to the user’s data on  M2M Platform along with access token for the user.

- M2M Platform checks the validity of the ‘access token’ given by M2M ApplicationIf the access token is determined as ‘valid’ the requested user data is provided to M2M Application

Post-conditions:

- M2M Application gets access-token to access to the data

- M2M Platform can determine M2M Application can access to the data

======[END of proposed text 2]=======