| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 TP#7 |
| Title:* | Network-based bootstrap for Security CSF |
| Source:* | Gemalto |
| Contact: | Mireille Pauliac, Gemalto, mireille.pauliac@gemalto.com |
| Date:* | 2013-10-3 |
| Abstract:* | This contribution aims at defining for the Security CSF a network-based credential provisioning relying on GBA. |
| Agenda Item:* | TBD |
| Work item(s): | WI-007 |
| Document(s) Impacted* | oneM2M-TS-003-Security v0.0.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To add in TS-003-Security the solution described in proposal below |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

OneM2M Architecture TS-0001 provides an overview of the Security CSF where credential provisioning is needed. This contribution aims at defining a network-based credential provisioning for Security CSF in case of presence of underlying network supporting GBA, e.g. 3GPP or 3GPP2.

2	Rationale

Security Administration

The Security Administration functionality of the Security (SEC) CSF shall enable the post-provisioning of a root credential protected by the security environment, as specified in the Architecture TS-0001 v0.1.2.

This contribution addresses the cases where the underlying network is a 3GPP or 3GPP2 network.

For scenarios where the M2M Service Provider and the operator of the underlying network have a trust relationship (including the case that they are actually the same entity) a solution for the post-provisioning consists in using GBA (Generic Bootstrapping Architecture) functionality as specified in 3GPP TS 33.220 [xx].

Leveraging on UICC-stored network credentials, GBA-based bootstrap enables to provision a root credential that is shared between a M2M Application Service/Middle Node and an Infrastructure Node. This solution avoids the pre-provisioning of root credentials by the M2M service layer or M2M application.

GBA capability could be exposed over Z interface.

This solution fulfils the security requirement SER-004 described in oneM2M TS-Requirements-v0.5.2:

“SER-004: In case where the M2M devices support USIM / UICC and the underlying networks support network layer security, the M2M system shall be able to leverage device’s USIM / UICC credentials and network’s security capability e.g. 3GPP GBA for establishing the M2M services and applications level security through interfaces to underlying network.”

Security Association Establishment

This functionality shall be able to establish security associations between corresponding M2M nodes, in order to provide specific security services (e.g. confidentiality, integrity, authentication, authorisation, or support for application level signature generation and verification) involving specified security algorithms and sensitive data. This involves key derivation based on provisioned root secrets.

In case of scenario where the M2M Service Provider and the operator of the underlying network have a trust relationship (including the case that they are actually the same entity), GBA procedure could be used, as specified in [xx], to share a key used to establish a security association between a M2M Application Service/Middle Node and Infrastructure Node.

Conclusion

The following section proposes to add GBA-based solutions within TS-0003. It does not refer to a specific section in order to add it in the most adequate section(s) that could be determined during TP#7 according to discussions and agreed documents.

Candidate sections already identified are:

- Section 6.3 of oneM2M-TS-0003-Security

- Section xxxx of contribution oneM2M-SEC-xxxx on “Security CSF” from Claus Dietze (Giesecke&Devrient).

3	Proposal

-----------------------Start of first change-------------------------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TR 0008 Security (draft)

[xx]	ETSI TS 133 220: "Digital cellular telecommunications system (Phase 2+); Universal Mobile Telecommunications System (UMTS); LTE; Generic Authentication Architecture (GAA); Generic Bootstrapping Architecture (GBA) (3GPP TS 33.220)".

-----------------------End of first change-------------------------------

-----------------------Start of second change-------------------------------

x	Security Administration of SEC CSF

x.1	Post-provisioning

x.1.1	Network-based bootstrap

For scenarios where the M2M Service Provider and the operator of an underlying network have a trust relationship (including the case that they are actually the same entity), GBA procedure specified in [xx] may be used for the post- provisioning of a root credential shared between an Application Service/Middle Node and an Infrastructure Node.

x.1.1.1	GBA-based bootstrap

For scenarios where the M2M Service Provider and the operator of an underlying network supporting GBA, such as 3GPP and 3GPP2, have a trust relationship (including the case that they are actually the same entity), the post-provisioning of root credential shared between a M2M Application Service/Middle Node and an Infrastructure Node shall rely on GBA procedure as specified in [xx].

y	Security Association Establishment of SEC CSF

In case of scenario where the M2M Service Provider and the operator of the underlying network have a trust relationship (including the case that they are actually the same entity), GBA procedure could be used, as specified in [xx], to share a key used to establish a security association between a M2M Application Service/Middle Node and Infrastructure Node.

y.1	GBA-based security association

For scenarios where the M2M Service Provider and the operator of an underlying network supporting GBA, such as 3GPP and 3GPP2, have a trust relationship (including the case that they are actually the same entity), the GBA procedure shall be applied as specified in [xx] to share a key used to establish a security association between a M2M Application Service/Middle Node and Infrastructure Node.

-----------------------End of second change-------------------------------