| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 |
| Title:* | Proposal for Completing Related Threats |
| Source:* | CATT (CCSA) |
| Contact: | Wei Zhou, zhouwei@catt.cn Hui Xu, xuhui@catt.cn |
| Date:* | 2013-07-29 |
| Abstract:* | In oneM2M-TR-0008-Security-V0.2.1 there are several countermeasures that do not have related threats. This contribution provides several proposals for completing these countermeasures’ related threats. |
| Agenda Item:* |  |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | oneM2M-TR-0008-Security-V0.2.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to use proposed threats for corresponding countermeasures in the TR (oneM2M-TR-0008) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

The proposed “Threat ID” is in yellow colour.

- Proposal

### 6.6.12	Keys can be derived from M2M Service-layer keys

| Related threats | 7;8;9;13(if it is not merged with other threats) Threat ID=7: General Eavesdropping on M2M Service-Layer Messaging between Entities Threat ID=8: Alteration of M2M Service-Layer Messaging between Entities Threat ID=9: Replay of M2M Service-Layer Messaging between Entities Threat ID=13: Eaves Dropping/Man in the Middle Attack |
| --- | --- |
| Countermeasure 11 | Communications whose security is anchored in M2M Service-layer keys use session keys, i.e. keys with a limited lifetime which can be set by security policy. Session keys can be derived from M2M Service-layer keys. |
| Applicable Security domain | Application domain security, Underlying Network security. |
| Advantages | Resists the attack. Limits exposure window if a session key is exposed or discovered. A well-established counter-measure. Allows shorter key lengths reduces cryptographic overheads. |
| Disadvantages | May place unsustainable loads on the endpoint device, for instance during cryptographic operations for authentication and re-key. May create unacceptable network and M2M Service backhaul loads during certain periods, such as re-key, or system-wide re-starts. |

Editor’s note: “Related Threats” to be completed.

### 6.6.13	Integrity Verification

| Related threats | 10 Threat ID=10: Unauthorized or corrupted Applications or Software in M2M Devices/Gateways |
| --- | --- |
| Countermeasure 12 | The integrity of executable functions and files in M2M Devices/Gateways can be verified. |
| Applicable Security domain | Application domain security. |
| Advantages | Detects the attack. High degree of assurance in the M2M application, supporting critical infrastructure functions and mitigating both logical and cascading kinetic impacts. |
| Disadvantages | Increases the cost and complexity of the M2M Device/Gateway, which may or may not be significant. May place unsustainable loads on the endpoint device, for instance during cryptographic operations for authentication or for encryption. May place inappropriate demands on the device for memory protection to protect credentials – or protections are insufficient to support assurance requirements. May create unacceptable network loads during certain periods, such as key expiry, or system-wide re-starts. |

Editor’s note: “Related Threats” to be completed.

### 6.6.14	Policy based Actions

| Related threats | 10 Threat ID=10: Unauthorized or corrupted Applications or Software in M2M Devices/Gateways |
| --- | --- |
| Countermeasure 13 | Policy-based action can be taken to prevent the use of functions or of M2M Devices/Gateways which fail the integrity verification test. |
| Applicable Security domain | Application domain security |
| Advantages | Prevents corrupted or unauthorised functions from being used. Resists the attack, without necessarily having to disable the whole M2M Device/Gateway. Allows the possibility of remote remediation of faults by download of new or patched functionality. |
| Disadvantages | Increases the cost and complexity of the M2M Device/Gateway, and possibly the M2M Core, which may or may not be significant. Policy decisions made in the M2M Core may require a standardised abstraction of Device/Gateway functionality. May place unsustainable loads on the endpoint device and reduce performance, for instance during integrity checking (hashing) operations of system files. |

Editor’s note: “Related Threats” to be completed.