| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 TP#7 |
| Title:* | Post-Provisioning Phases |
| Source:* | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com |
| Contact: | As above |
| Date:* | 2013-10-16 |
| Abstract:* | This contribution provides a high-level description of some common phases for Post-Provisioning. This is to provide a suitable framework for oneM2M-SEC-2013-0044 “Network-Based Post Provisioning” and oneM2M-SEC-2013-0050 “PKI-Based Post Provisioning”. |
| Agenda Item:* | TBD |
| Work item(s): | WI-007 |
| Document(s) Impacted* | oneM2M-TS-003-Security v0.0.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Add the proposed text to oneM2M-TS-003-Security |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

[1]		oneM2M-SEC-2013-0044 “Network-Based Post Provisioning”

[2]		oneM2M-SEC-2013-0050 “PKI-Based Post Provisioning”

2	Rationale

This contribution provides a high-level description of some common phases for Post-provisioning. This is to provide a suitable framework for the methods described in [1] and [2].

3	Proposal

-----------------------Start of first change-------------------------------

x	Security Administration of SEC CSF

x.1	Post-provisioning

x.1.1	Post-Provisioning Phases

[Editor’s note: This section describes the high-level sequence of events common to post-provisioning scenarios]

This clause defines a sequence of phases for post-provisioning where the input and outcome of each phase is consistent, but a variety of options for each phase are supported and can be (for the most part) selected independently of the options in other phases.

Post-provisioning is partitioned into three phases: Phases 1 (Triggering) and 3 (Bootstrap) occur during every post-provisioning, while Phase 2 (Discovery) is conditional on the outcome of Phase 1.

- Post-Provisioning Triggering (Section x.1.2): The Field entity is triggered to attempt a series of one or more instructions. Each instruction has the option (independent of the other instructions) of being one of the following:

  - A Post-Provisioning Bootstrap instruction, identifying a Post-Provisioning Bootstrap method  to be applied and  a target with which to establish the root credential,

  - The Field entity skips directly to Phase 3 “Post-Provisioning Bootstrap” to perform a Post-Provisioning Bootstrap instruction.

  - A Post-Provisioning Discovery instruction Identifying a Post-Provisioning Discovery method and a Post-Provisioning Discovery resource that can provide a set of Post-Provisioning Bootstrap instructions.

  - The Field entity skips directly to Phase 2 “Post-Provisioning Discovery” to perform a Post-Provisioning Discovery instruction.

The Field entity performs these instructions in sequence, until one of the instructions results in successful post-provisioning or all instructions fail to result in successful post-provisioning.

- Post-Provisioning Discovery Phase (Section x.1.3): The input to this phase is a Post-Provisioning Discovery instruction. The Field entity performs the identified Post-Provisioning Discovery method with the identified Post-Provisioning Discovery resource – which (if successful) results in the Field entity being provided with a series of one or more Post-Provisioning Bootstrap instructions. The Field entity performs these Post-Provisioning Bootstrap instructions in sequence, until one of these instructions results in successful post-provisioning or all these instructions fail to result in successful post-provisioning.

- Post-Provisioning Bootstrap (Section x.1.4): The input to this phase is a Post-Provisioning Bootstrap instruction. The Field Node performs the indicated Post-Provisioning Bootstrap method with the identified target. If successful, a shared root credential is established between the Field Node and the identified target.

x.1.2	Post-Provisioning Triggering Methods

[Editor’s note: This section would include methods used to initiate post-provisioning. Examples may include manual input of Infrastructure Node FQDN into Field Node, or a trigger initiated during boot-up, etc.]

x.1.3	Post-Provisioning Discovery Methods

[Editor’s note: This section would include methods for Post-Provisioning Discovery. Examples include retrieving Post-Provisioning Bootstrap instructions from an online server, or reading Post-Provisioning Bootstrap instructions from a pre-configured file. There could be some methods that are informative: for example a method for reading instructions from a file will not require standardization beyond the format of the Post-Provisioning Discovery instruction]

x.1.4	Post-Provisioning Bootstrap Methods

[Editor’s note: This section would include the descriptions for the Post-Provisioning Bootstrap methods, such as Network-based bootstrap and the PKI-Based Bootstrap]

-----------------------End of first change-------------------------------