| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC8.0 (WG4 at TP#8) |
| Title:* | GBA framework for Security CSF |
| Source:* | Gemalto (ETSI) |
| Contact: | Mireille Pauliac, Gemalto, mireille.pauliac@gemalto.com Francois Ennesser, Gemalto, francois.ennesser@gemalto.com |
| Date:* | 2013-12-02 |
| Abstract:* | This contribution aims to further describe the GBA procedures used for Security Association Establishment and Security Administration components of SEC CSF specified in oneM2M TS-0003. |
| Agenda Item:* | TBD |
| Work item(s): | WI-007 |
| Document(s) Impacted* | oneM2M-TS-003-Security v0.1.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To add in TS-003-Security the text provided in this contribution |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to further describe GBA procedure.

2	Rationale

This contribution further describes the GBA procedure used for Security Association Establishment and Security Administration components of SEC CSF specified in oneM2M TS-0003.

A new section dedicated to GBA framework is proposed to avoid the duplication of GBA description in several sub-sections of section 6 on “Security CSF implementation”.

3	Proposal

-----------------------Start of 1st   change-------------------------------

### 6.3.2	Security Association Establishment

This component provides functions to establish a security association between different entities.

This component shall provide following functions:

- Secure Connection via secure session establishment

- Secure Connection via object security

- …

Editor’s note: to be completed.

### For secure connection on 3GPP networks [1] applies.

#### 6.3.2.1	Network-based security association

In case of scenario where the M2M Service Provider and the operator of the underlying network have an agreement to use the underlying network credentials as the basis for establishing a secure connection between a M2M Application Service/Middle Node and Infrastructure Node (including the case that the M2M Service Provider and the operator of an underlying network are actually the same entity), GBA procedure could be used, as specified in [4].

It is important that this feature is used only within the scope of an appropriate agreement between the M2M Service Provider and the operator of the underlying network. The normative text in Section y.1 implicitly assumes that such an agreement is already in place. Since the present document is a technical specification, it does not address the details of such an agreement.

##### 6.3.2.1.1	GBA-based security association

The GBA procedure shall be applied as specified in [4] for scenarios where the operator of an underlying network supports GBA, e.g. 3GPP or 3GPP2, and the underlying network credentials are to be used as the basis for establishing a secure connection between a M2M Application Service/Middle Node and Infrastructure Node.

The Secure Connection relies on a symmetric shared key called “M2M Connection Key”( Kmc) used to establish a secure session between a M2M Application Service/Middle Node and Infrastructure Node.

The section 8.2.3 specifies how the key Kmc is obtained thanks to GBA framework.

-----------------------End of 1st change-------------------------------

-----------------------Start of 2nd change-------------------------------

#### 6.3.3.2	Post-provisioning

#### 6.3.3.2.1	Network-based bootstrap

For scenarios where the M2M Service Provider and the operator of an underlying network have an agreement to use the underlying network credentials as the basis for the post- provisioning of a root credential shared between an Application Service/Middle Node and an Infrastructure Node (including the case that the M2M Service Provider and the operator of an underlying network  are actually the same entity), GBA procedure specified in [4] may be used.

It is important that this feature is used only within the scope of an appropriate agreement between the M2M Service Provider and the operator of the underlying network. The normative text in Section x.1.1.1 implicitly assumes that such an agreement is already in place. Since the present document is a technical specification, it does not address the details of such an agreement.

###### 6.3.3.2.1.1	GBA-based bootstrap

The GBA procedure as specified in [4] shall be used for scenarios where the operator of an underlying network supports GBA infrastructure, e.g. 3GPP or 3GPP2, and the underlying network credentials are to be used as the basis for the post-provisioning of root credential shared between an Application Service/Middle Node and an Infrastructure Node.

The root credential shared between an Application Service/Middle Node and an Infrastructure Node is a symmetric shared key called “M2M Root Key” (Kmr).

The section 8.2.2 specifies how the key Kmr is obtained thanks to GBA framework.

-----------------------End of 2nd change-------------------------------

-----------------------Start of 3rd change-------------------------------

# 8	GBA (Generic Bootstrapping Architecture) framework

## 8.1	GBA overview

GBA framework relies on a BSF, HSS, SLF and NAF as specified in [4].  The User Equipment corresponds in oneM2M to a M2M Application Service Node or a M2M Middle Node.

## There are two modes of GBA: ME-based (GBA_ME) and UICC-based (GBA_U). The latter requires that the UICC is GBA aware. The BSF shall decide which mode to run based on the UICC capabilities indicated in the GBA user security setting (GUSS).

Figure 8.1	Simple Network Architecture for GBA

.

## 8.2	GBA framework for SEC CSF

### 8.2.1	General

After a successful GBA bootstrapping, the M2M Application Service/Middle Node and the BSF share a security association which consists of a bootstrapping transaction identifier (B-TID) and key material (GBA bootstrap Ks).

This security association may be used by the M2M Application Service/Middle Node to derive NAF keys (Ks_(ext/int)_NAF) shared between a M2M Application Service/Middle Node and a M2M Infrastructure Node.

Figure 8.2.1	GBA framework for SEC CSF

### 8.2.2 Security bootstrap

To share a M2M Root Key (Kmr) between an Application Service/Middle Node and an Infrastructure Node, the M2M Application Service/Middle Node shall perform a successful GBA bootstrapping and derive a NAF key (Ks_(ext/int)_NAF). This NAF key is the M2M Root Key (Kmr).

### 8.2.3 Security Association Establishment

To obtain a M2M Connection Key (Kmc) used for secure connection between a M2M Application Service/Middle Node and a M2M Infrastructure Node, the M2M Application Service/Middle Node shall perform a successful GBA bootstrapping and derive a NAF key (Ks_(ext/int)_NAF). This NAF key is the M2M Connection Key (Kmc).

-----------------------End of 3rd change-------------------------------