| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 |
| Title:* | Security CSF Architecture Figure |
| Source:* | Giesecke & Devrient, Oberthur Technologies |
| Contact: | Claus Dietze, claus.dietze@gi-de.com Dragan Vujcic, v.dragan@oberthur.com |
| Date:* | 2013-12-04 |
| Abstract:* |  |
| Agenda Item:* |  |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | oneM2M-TS-0003-Security_Solutions-V0_1_0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include figure into oneM2M-TS-0003-Security_Solutions-V0_1_0 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction and topics for discussion:

Following discussions at SEC7.0 and TP7.0 a new figure needs to be created taking into account the comments as listed in the Editor’s notes. Below figure is proposed to be included in the next revision of the security TS.

Editor’s note: Blue components may be Enabler Functions rather than resources of a CSF.

Editor’s note: Several changes to the figure required, incl.: internal interface for interaction CSF – CSF to be replaced/removed, there is only one API at CSE level (X,Y ending at CSE), removal of tbd interfaces, introduce Security CSF as a separate box. Plug-in boxes to be removed as they are not going to be standardized. Illustrate security framework. Find different name for “Security Transport” in order to reduce confusion (e.g. SE Transport)

Editor’s note: Merge Access Control with Authorization (into one box).

=================== Proposed change of Security TS ====================

# 5	Security CSF Architecture

## 5.1	Overview

The following figure provides an high level overview of the Security CSF architecture.

The architecture consists of following layers:

- Application layer

- Security Services Framework layer

- Secure Environment layer

Design principles:

- The architecture is split into several components and sub-components providing a modular design. With this design, mapping of the architecture to different nodes and entities is enabled

- Depending on the requirements of each entity, the Security CSF should consist of components relevant to fulfil the requirements of the respective node or entity and the intended use case

- The architecture may need to be adapted to be suitable for implementation in different entities. For example, the architecture can be mapped to different device classes.

- The security administration component shall enable administration of all sensitive resources (data and functions) within the Security CSF and shall also allow configuration and extension of the Security CSF itself

- The Secure Environment within the Security CSF is accessed via the Secure Environment Abstraction layer and shall hold all sensitive resources