| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 |
| Title:* | Security Architecture Diagram |
| Source:* | FUJITSU |
| Contact: | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2013-12-10 |
| Abstract:* | This contribution proposed diagram of ‘oneM2M Security Architecture ‘ . |
| Agenda Item:* | Security TS |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG4(SEC) member should agree on proposal. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

During discussions triggered by oneM2M-SEC-2013-0073 WG4 members realized a possibility to draw different picture to fit common understanding for Security CSF.

This contribution proposed new diagram for section 5.1.

=== START OF CHANGE ===

# 5. 	oneM2M Security Architecture

## 5.1	Overview

The following figure provides an overview of the oneM2M Security architecture.

The architecture consists of following layers:

- Application layer

- Security Service Framework

- Security Enforcement Functions

- Security Administration Functions

- Secure Environment Abstraction Layer

- Secure Environment

- CSFs

Editor’s note: Blue components may be Enabler Functions rather than resources of a CSF.

Editor’s note: Several changes to the figure required, incl.: internal interface for interaction CSF – CSF to be replaced/removed, there is only one API at CSE level (X,Y ending at CSE), removal of tbd interfaces, introduce Security CSF as a separate box. Plug-in boxes to be removed as they are not going to be standardized. Illustrate security framework. Find different name for “Security Transport” in order to reduce confusion (e.g. SE Transport)

Editor’s note: Merge Access Control with Authorization (into one box).

=== END OF CHANGE ===

# Comments

Since this section covers relationship with other CSF, it can be called ‘oneM2M Security Architecture’.