| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC8.0 (WG4 at TP#8) |
| Title:* | GBA description for Security TR |
| Source:* | Gemalto (ETSI) |
| Contact: | Mireille Pauliac, Gemalto, mireille.pauliac@gemalto.com Francois Ennesser, Gemalto, francois.ennesser@gemalto.com |
| Date:* | 2013-12-10 |
| Abstract:* | This contribution provides a description of GBA framework and its use in oneM2M. |
| Agenda Item:* | TBD |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | oneM2M-TR-0008-Security-V0.3.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To add in TR-0008-Security the text provided in this contribution |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to describe GBA procedure and its use in oneM2M.

3	Proposal

All proposed changes to the TR text appear in Revision Marks.

-----------------------Start of 1st   change-------------------------------

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M drafting rules (draft)

[i.2]	oneM2M-TR-0004-Definitions_and_Acronyms (draft)

[i.3]	oneM2M-TS-0002-Requirements (draft)

[i.4]	oneM2M-TS-0001-Functional Architecture (draft)

[i.5]	oneM2M-TR-0001-UseCase (draft)

[i.6]	ISO/IEC 29115	Information technology- Security Techniques – Entity authentication assurance framework

[i.7]	ETSI TS 102 221 V11.0.0 Smart Cards; UICC-Terminal interface; Physical and logical characteristics (Release 11)

[i.8]	ETSI TS 102 671 V9.1.0 Smart Cards; Machine to Machine UICC; Physical and logical characteristics (Release 9)

[i.9]	ISO/IEC 15408: "Information technology - Security techniques - Evaluation criteria for IT security".

[i.x]	 ETSI TS 133 220 "Digital cellular telecommunications system (Phase 2+); Universal Mobile Telecommunications System (UMTS); LTE; Generic Authentication Architecture (GAA); Generic Bootstrapping Architecture (GBA) (3GPP TS 33.220)".

-----------------------End of 1st change-------------------------------

-----------------------Start of 2nd change-------------------------------

# x	GBA (Generic Bootstrapping Architecture) framework

## x.1	GBA overview

GBA framework relies on a BSF, HSS, SLF and NAF as specified in [i.x].  GBA has two modes (GBA_U and GBA_ME) and one variant (GBA_Digest).

## GBA_U and GBA_ME rely on AKA credentials stored in the UICC application.

## GBA_ME is a ME-based solution with all GBA-specific functions carried out in the ME. The Boostrapping Key “Ks” and the NAF key “Ks_NAF” are stored on the ME.

## GBA_U is a UICC-based GBA with UICC-based enhancement proposing higher level of security with the storage of GBA keys in the UICC. The Bootstrapping Key “Ks” and the NAF key “Ks_int_NAF” are stored in the UICC while the NAF Key “Ks_ext_NAF” is stored in the ME.

## The BSF shall decide which mode to run based on the UICC capabilities indicated in the GBA user security setting (GUSS).

## GBA_Digest is a GBA variant that extends the usage of GBA to environments where the UICC is not available. GBA_Digest relies on SIP Digest credentials.

Figure 8.1-a	Simple Network Architecture for GBA in 3GPP [i.x]

Figure 8.1-b	Use of GBA in oneM2M

-----------------------End of 2nd  change-------------------------------