| CHANGE REQUEST |
| --- |
| Group Name:* | TP#15 |
| Source:* | Datang |
| Format:* | Plenary Face-to-face |
| Date:* | 2015-01-19 |
| Contact:* | Wei Zhou, Datang (zhouwei@catt.cn) Hui Xu, Datang (xuhui@catt.cn) |
| Reason for Change/s:* | TS-0003 Clause7 Cleanup |
| CR against: Release* | Rel. 1 |
| CR against: TS/TR* | TS-0003 V-0.9.0 |
| Clauses/Sub Clauses* | 7.1.1, 7.1.3, 7.1.4, 7.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes changes for cleanup of commonly used attribute: “accessControlPolicyIDs”. This common attribute is defined in TS-0001. However, in TS-0003, this common attribute is named as “accessControlPolicyID”, so these errors shall be corrected.

### -----------------------Start of change 1-------------------------------------------

### 7.1.1	General Description

The M2M authorization procedure controls access to resources and services hosted by CSEs and AEs. The authorization procedure requires that the originator of the resource access request message has been identified to the Authentication Function, and originator and receiver are mutually authenticated with each other.

The resource addressed in a request message has an associated  accessControlPolicyIDs attribute (either included explicitly as an attribute of the resource addressed in the request message, implied  from the parent of the resource, or set fixed by the system, see clause 9.6.1 of TS-0001 [1]).  The accessControlPolicyIDs attribute contains a list of identifiers of <accessControlPolicy> resources applicable to the resource addressed in the request message.

The overall structure of <accessControlPolicy> resources is described in clause 9.6.2 "Resource Type accessControlPolicy" of TS-0001 [1]).

Each of these <accessControlPolicy> resources include privileges and selfPrivileges attributes, which comprise the information, denoted as access control rules in this specification, that is evaluated against the parameters associated with the request message to obtain the access decision.

Figure 7.1.1-1 illustrates the relation between <accessControlPolicy> resource instances (ACP) and the instances of the protected resources, denoted Resource_1 to Resource_N.

# Figure 7.1.1-1: Relation between Resource Instances and Access Control Policies

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 7.1.3 	Format of privileges and selfprivileges Attributes

The privileges and selfPrivileges attributes exhibit the same data type format which is specified as follows.

Each privileges or selfPrivileges attribute comprises a set of access control rules. We denote in the following the set of access control rules as acrs and an individual access control rule in this set as acr. The access control rules in acrs are indexed with the letter k. The number of access control rules in the set is denoted with the letter K:

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 7.1.4 	Access Control Decision

The access decision is derived by comparing the parameters associated with a resource access request message as described in clause 7.1.2 with the access control rules included in the privileges or selfPrivileges attributes of all ACP sets assigned to the protected resource by means of the accessControlPolicyIDs, cf. Figure 7.1.1-1.

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

## 7.2	AE Impersonation Prevention

Since several AEs can behave maliciously and pretend to be another AE with their ID changed, Receiver CSE needs prevention mechanism for AE impersonation. This mechanism works at Registrar CSE since Registrar CSE is an entry point of M2M system.

When Receiver CSE receives a request, Receiver CSE shall perform as follows.

Figure 7.2-1: AE impersonation checking procedure

- Security association establishment is performed

- AE sends a request to Registrar CSE.

- Receiver CSE checks whether Receiver CSE is Registrar CSE (Registrar CSE finds ID associated in security association and find any <AE> resource which contains that ID in AE-ID attribute).

- If Receiver CSE is Registrar CSE, Receiver CSE checks the value in fr parameter is the same as the found ID in step 2. If the request is AE registration and fr parameter is empty string, this procedure is terminated.

- If the value is not the same, Receiver CSE sends response with impersonation error response code.

- Receiver CSE performs procedures specified in clause 8.2 [1].

### -----------------------End of change 4---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

Resource_1

List of IDs in accessControlPolicyIDs

attribute of Resource_1

Example:

ACP set = (ACP_1, ACP_2)

assigned to Resource_1

Each ACP includes one privileges and one selfPrivileges attribute.

privileges and selfPrivileges attributes include a set of access control rules (defined in Section 7.3)

Instances of

accessControlPolicy

resources (ACP)

ACP_4

ACP_3

ACP_2

ACP_1

...

Resource_2

Resource_3

Resource_N