| CHANGE REQUEST |
| --- |
| Group Name:* | SEC#15 @ TP#15 |
| Source:* | Philip Hawkes, Qualcomm, phawkes@qti.qualcomm.com, Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Format:* | Plenary |
| Date:* | 2015-01-21 |
| Contact:* | As above |
| Reason for Change/s:* | This CR addresses Qualcomm’s action item to address a comment by Altiux on TS-0003 in the candidate release. |
| CR against: | TS-0003 v0.9.0 |
| Clauses/Sub Clauses Affected* | 10.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Apply changes to TS-0003 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR addresses Qualcomm’s action item to address a comment by Altiux TS-0003 in the candidate release. The action was to “clarify if needed security options to be supported on TLS servers vs. TLS clients”

R02: Updated following discussion in SEC. Deleted comments.

R03: Editing following feedback from SEC.

### -----------------------Start of change 1-------------------------------------------

## 10.2	TLS and DTLS Details

### 10.2.1	TLS and DTLS Versions

Where TCP payloads are to be secured, TLS v1.2 [16] shall be used.

Where UDP payloads are to be secured, DTLS v1.2 [17] shall be used, noting that the DTLS v1.2 ciphersuites are identical to the TLS v1.2 ciphersuites.

All implementations shall support the Server Name Indication (SNI) to indicate their authority in the SNI HostName field as defined in Section 3 of RFC 6066 [44]. This is needed so that when a host that acts as a virtual server for multiple Authorities receives a new TLS or DTLS connection, it knows which keys to use for the TLS or DTLS session.

(D)TLS Clients on any Node and (D)TLS Servers on MNs shall support at least one of the TLS ciphersuites indicated in clause 10.2.2. “TLS and DTLS Ciphersuites for TLS-PSK-Based Security Frameworks” or 10.2.3 “TLS and DTLS Ciphersuites for Certificate-Based Security Frameworks”.

NOTE: (D)TLS Servers on MN need to support the TLS ciphersuites for those (D)TLS clients they are expected to interact with.

(D)TLS Servers on INs shall support all of the TLS ciphersuites indicated in clause 10.2.2. “TLS and DTLS Ciphersuites for TLS-PSK-Based Security Frameworks” and 10.2.3 “TLS and DTLS Ciphersuites for Certificate-Based Security Frameworks”.

### 10.2.2	TLS and DTLS Ciphersuites for TLS-PSK-Based Security Frameworks

The following Security Frameworks:

- Provisioned Symmetric Key Security Association Establishment Framework;

- MAF-Based Security Association Establishment Framework;

- Pre-Shared Key Remote Security Provisioning Framework;

- GBA-Based Remote Security Provisioning Framework;

shall use one of the key exchange algorithms defined in RFC 4279 [15].

TLS implementations in entities supporting these security frameworks shall implement at least the following TLS ciphersuite:

- TLS_PSK_WITH_AES_128_CBC_SHA256 (RFC 5487 [42]).

DTLS implementations supporting these security frameworks shall implement at least the following ciphersuites

- TLS_PSK_WITH_AES_128_CCM_8 (RFC 6655) [31].

### -----------------------End of change 1 ---------------------------------------------