| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#15 |
| Title:* | pCR Group Authentication Definition and Use Cases |
| Source:* | China Mobile |
| Contact: | Ziyao Cheng, China Mobile, chengziyao@chinamobile.com Minpeng Qi, China Mobile, qiminpeng@chinamobile.com Min Zuo, China Mobile, zuomin@chinamobile.com |
| Date:* | 2015-01-12 |
| Abstract:* | This contribution presents the pCR group authentication definition and use cases according to the comment on group authentication consideration. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0016 |
| Document(s) Impacted* | Security TR (TR-0012) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into an appropriate section of the Security TR-0012. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

==================<Start of Change (New Text 1)>=================

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in [i.2] and the following apply:

、

Editor Node: the definitions are subject to further refinement.

NOTE:	This may contain additional information.

==================<End of Change1>==========================

==================<Start of Change (New Text 2)>=================

#### 5.2.1.4	Normal flow

- DAP sends a message to indicate that there is a specific group of smart meters that need to communicate with the Utility Data Center / AMI Headend.

- Each smart meter in the group sends a request via the DAP in order to report to the Utility Data Center / AMI Headend.

- DAP needs to verify the smart meters identities to upload information before it forwards the request to the Utility Data Center/ AMI Headend.

- Utility Data Center/ AMI Headend verifies the identity of DAP, and performs mutual authentication with each smart meter in the group simultaneously.

==================<End of Change 2>==========================

==================<Start of Change (New Text 3)>=================

#### 5.2.2.4	Normal Flow

- The remote vehicle gateway sends a message to indicate that there is a specific group of vehicles that need to communicate with the vehicle service centre.

- Each vehicle in the group sends request to the remote vehicle gateway at the same time.

- The remote vehicle gateway verifies the vehicles and then sends request to the vehicle service centre, including vehicle identity list.

- The vehicle service centre verifies the remote vehicle gateway, and performs mutual authentication with each vehicle on the list simultaneously.

==================<End of Change 3>==========================