| CHANGE REQUEST |
| --- |
| Group Name:* | SEC#15 at TP#15 |
| Source:* | Philip Hawkes, Qualcomm, phawkes@qti.qualcomm.com, Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Mireille Pauliac, Gemalto, mireille.pauliac@gemalto.com |
| Format:* | Plenary |
| Date:* | 2015-01-21 |
| Contact:* | As above |
| Reason for Change/s:* | Add missing description of FQDN value for CSE in case of GBA RSPF. |
| CR against: Release* | Release 1 (January) |
| CR against: TS/TR* | TS-0003 v0.9.0 |
| Clauses/Sub Clauses* | 8.3.2.3, |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

The value of FQDN for CSE in case of GBA-based Remote Security Provisioning Framework.

### -----------------------Start of change 1-------------------------------------------

#### 8.3.2.3	GBA-Based Remote Security Provisioning  Framework

To share a long term Master Credential (Km) or Provisioned Secure Connection Key (Kpsa) between an Application Service/Middle Node and an Enrolment Target, the M2M Application Service/Middle Node shall perform a successful GBA bootstrapping and derive a NAF key (Ks_(ext/int)_NAF). This NAF key is the Master Credential (Km) or Provisioned Secure Connection Key (Kpsa).

Figure 8.3.2.3-1: 	The sequence of events when using the GBA-Based Remote Security Provisioning Framework.

NOTE:	The following font colours differentiate the general topic that the text relates to:
Black text contains Remote Security Provisioning -Framework-independent details.
Blue italic text highlights details specific to this particular Remote Security Provisioning Framework.
Purple italic text highlights technical actions that may include steps not specified by oneM2M.

Bootstrap Credential Configuration: The credentials configuration for Enrolee and M2M Enrolment Function (MEF) is described in 3GPP specification TS 33.220 [13]. The MEF plays the role of the BSF. The credentials used to perform mutual authentication between Enrolee and MEF are UNSP specific.

Bootstrap Instruction Configuration: the Enrolee, the MEF and the Enrolment Target shall be configured with the information needed for authorizing the remote provisioning.

  - The Enrolee shall be configured with the Enrolment Target Identity: identifying the Enrolment Target for which the Enrolee is to be provisioned.

  - The MEF shall be configured with the Enrolee-ID and the Enrolment Target Identity

  - The Enrolment Target Identity: Identifying the Enrolment Target for which the Enrolee (authenticated using the GBA) is to be provisioned

  - The Enrolee’s assigned CSE-ID or AE-ID (Enrolee-ID), The M2M Enrolment Function is to provide this entity identity for the Enrolee with the Km or Kpsa to the Enrolment Target, when requested by the Enrolment Target.

  - Enrolee’s GBA User Security Settings (GUSS) enables indicating if Enrolee is allowed to establish a NAF-specific key with the Enrolment Target or/and if the BSF can distribute a NAF specific key to the Enrolment Target.

### Bootstrap Enrolment Handshake:

### The Bootstrap Enrolment Handshake enables the establishment of a GBA bootstrapped key (Ks) shared between the Enrolee and the MEF with associated Bootstrapping Transaction Identifier ( B-TID) and key lifetime, by performing to the GBA Bootstrapping phase described in 3GPP TS 33.220 [13].

### If a bootstrapped key Ks is already shared between Enrolee and the MEF and still valid, then the Bootstrap Enrolment Handshake phase is not needed. The Enrolment Key Generation phase can take place with the existing GBA Bootstrapped key Ks.

### Enrolment Key Generation phase

### The Enrolment Key (Ke) shall be the GBA Bootstrapped key (Ks) established during the Bootstrap Enrolment Handshake.

### The Enrolment Key Identifier (Ke-ID) shall be the Bootstrapping Transaction Identifier ( B-TID) generated during the Bootstrap Enrolment Handshake.

### Integration to the Association Security Handshake:

- The Enrolee and the Enrolment Target shall establish the Master Credential (Km) or the Provisioned Secure Connection Key (Kpsa)  thanks to procedures described in 3GPP TS 33.220 [13] using the Enrolment Key (Ke) as GBA bootstrapped key Ks and the Enrolment Key Identifier (Ke-ID) as B-TID. The Enrolment Target plays the role of a NAF.

  - The Enrolee and the Enrolment Target shall establish NAF-specific key(s) as described in 3GPP TS 33.220 [13]. A key lifetime is associated to the NAF-specific keys. The Enrolment Target also receives the Enrolee’s User Security Settings (USS) from the MEF/BSF.

    - The FQDN of the NAF, used as input to generate the Ks_(int/ext)_NAF, shall be set as follows:

    - In the case where the Enrolment Target is an M2M Authentication Function, then the FQDN of the NAF is set to the FQDN of the M2M Authentication Function.

    - In the case where the Enrolment Target is a CSE, then the FQDN of the NAF is set to the public domain name representation of the CSE-ID as defined in TS-0001 [1].

    - In case of GBA_ME, NAF-specific key is Ks_NAF

    - In case of GBA_U, NAF-specific keys are Ks_int_NAF and Ks_ext_NAF.

  - The Master Credential (Km) ) or the Provisioned Secure Connection Key (Kpsa) shall be the NAF-specific key:

    - In case of GBA_ME, Km/Kpsa = Ks_NAF

    - In case of GBA_U, Km/Kpsa = Ks_int_NAF if HTTP Client application resides in the UICC. Otherwise, Km/Kpsa = Ks_ext_NAF.

  - The Enrolee and the Enrolment Target shall set the Master Credential Identifier (Km-Id) or  the Provisioned Secure Connection Key Identifier (Kpsa-Id)  to the value of KeId.

Enrolee and Enrolment Target shall perform (D)TLS-PSK handshake (RFC 4279 [15]) with the Master Credential (Km) or Provisioned Secure Connection Key (Kpsa) as Pre-Shared Key in compliance with clause 10.2.2 “TLS and DTLS Ciphersuites for TLS-PSK-Based Security Frameworks”. If UICC is used as Secure Environment supporting Remote Security Provisioning, GBA-U with Km/Kpsa = Ks_int_NAF shall be used for authentication and key exchange.

### -----------------------Start of change 1-------------------------------------------