| CHANGE REQUEST |
| --- |
| Meeting:* | SEC#16 at TP#16 |
| Source:* | Philip Hawkes, Qualcomm, phawkes@qti.qualcomm.com, Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2015-03-16 |
| Contact:* | As above |
| Reason for Change/s:* | Essential corrections for aligning the PSK-based SAEF with TS-0001 |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 v1.0.1 |
| Clauses/Sub Clauses* | 8.2.2.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR provides essential corrections for aligning the PSK-based SAEF with TS-0001. This CR is based on SEC-2015-0452R02 which was postponed at SEC#15.

R01: Changed to latest template. No change to content.

### -----------------------Start of change 1-------------------------------------------

#### 8.2.2.1	Provisioned Symmetric Key Security Association Establishment Frameworks

This clause describes the Provisioned Symmetric Key Security Association Establishment Framework.  This framework enables mutual authentication of two entities corresponding to either two CSEs or a CSE and an AE. The Credential for this framework is a long-term symmetric key that has been provisioned into the entities to be authenticated. This key is called a Provisioned Secure Connection Key and is denoted Kpsa. The provisioning of Kpsa could be a pre-provisioning or a remote provisioning thanks to Remote Security Provisioning Frameworks, as described in clause 8.3. The entities authenticate each other by verifying message authentication codes in the Security Handshake which were generated using the Provisioned Secure Connection Key.

NOTE:	Long term Provisioned Secure Connection Keys can pose a security risk if not adequately secured, and for this reason long term Provisioned Secure Connection Keys are recommended to be stored in Secure Environments.

Figure 8.2.2.1-1 illustrates the sequence of events when using the Provisioned Symmetric Key Security Association Establishment Framework.

NOTE:	The following font colours differentiate the general topic that the text relates to:
Blue italic text highlights details specific to this particular Security Association Establishment Framework.

Purple italic text highlights technical actions that may include steps not specified by oneM2M.

Red italic text highlights security-related properties.

Figure 8.2.2.1-1: The sequence of events when using the Provisioned Symmetric Key
Security Association Establishment Framework

Credential Configuration: The Provisioned Secure Connection Key (Kpsa) and the corresponding Provisioned Secure Connection Key Identifier, denoted KpsaId, are provisioned to both entities either with pre-provisioning or remote provisioning. The format of KpsaId is defined in clause 10.5 “KpsaId Format”. If Entity A is a CSE, then Entity A shall also be configured with its CSE-ID (not shown in the figure).

Association Configuration: Entity A is configured with Entity B identity (IdB). This identity is used to route the (D)TLS exchange.

Association Security Handshake: The entities perform a (D)TLS-PSK handshake [15] to establish a secure session.

- MAF Server Handshake: There is no MAF Server Handshake applied in the Provisioned Secure Connection Key Security Association Establishment Framework.

- The "psk_identity" parameter [15] is set to the value of the Provisioned Secure Connection Key Identifier KpsaId.

- The "psk" parameter [15] is set to the value of the Provisioned Secure Connection Key Kpsa.

- The (D)TLS cipher suite profile for the Provisioned Secure Connection Key Security Association Establishment Framework is specified in clause 10.2.2.

- Following successful authentication of Entity B, Entity A associates the security context with Id B (Entity B’s entity identifier) configured to Entity A during Association Configuration.

- Following successful authentication of Entity A, Entity B associates the security context with a CSE-ID or AE-ID :

  - If Entity B was already provided with the CSE-ID or AE-ID corresponding to KpsaId, then Entity B associates the security context with that CSE-ID or AE-ID.

  - Otherwise, Entity B associates the security context with the Credential-ID formed from KpsaId as described in clause 10.4 “Credential-ID Details”. Entity B then determines CSE-ID or AE-ID from the Credential-ID as described in clause 8.2.1 “Overview on Security Association Establishment Frameworks”.

### -----------------------End of change 1---------------------------------------------