| Input Contribution |
| --- |
| Meeting ID* | SEC#16 |
| Title:* | TR-00016 Resource Definitions for Distributed Authorization |
| Source:* | Wei Zhou, Datang, zhouwei@catt.cn Hui Xu, Datang, xuhui@catt.cn |
| Uploaded Date:* | 2015-03-16 |
| Document(s) Impacted* | SEC WI-0023, oneM2M-TR-0016 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TR-0016. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

1	Introduction

This contribution defines some resources for supporting distributed authorization.

2	Proposal

### 5.2.x	Proposal Z: Using resource-based approach to implement distributed authorization

#### 5.2.x.1	Introduction

This clause describes a solution for distributed authorization using new defined <accessControl> resource and its child resources over the Mcc and Mcc' reference points. The child resources of the <accessControl> resource are <policyDecisionPoint>, <policyRetrievalPoint> and <policyInformationPoint>. These child resources are virtual resources that are used to trigger PDP process, PRP process and PIP process defined in TS-0003 [2] respectively.

This clause also describes the management procedures for the <accessControl> resource and its child resources.

#### 5.2.x.2	Resources

##### 5.2.x.2.1	Resource Type accessControl

The <accessControl> resource represents the method for providing authorization related services. The <accessControl> resource contains three child resources, they are <policyDecisionPoint>, <policyRetrievalPoint> and <policyInformationPoint>. These child resources are virtual resources that provide authorization functions of PDP, PRP and PIP defined in oneM2M TS-0003 [2] respectively. The <accessControl> resource shall be located directly under <CSEBase>.

Figure 5.2.x.2.1-1: Structure of <accessControl> resource

The <accessControl> resource shall contain the child resources specified in table 5.2.x.2.1-1.

Table 5.2.x.2.1-1: Child resources of <accessControl> resource

| Child Resources of <accessControl> | Child Resource Type | Multiplicity | Description | <accessControlAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| [variable] | <policyDecisionPoint> | 1 | See clause 5.2.x.2.2 | none |
| [variable] | <policyRetrievalPoint> | 1 | See clause 5.2.x.2.3 | none |
| [variable] | <policyInformationPoint> | 1 | See clause 5.2.x.2.4 | none |

The <accessControl> resource shall contain the attributes specified in table 5.2.x.2.1-2.

Table 5.2.x.2.1-2: Attributes of <accessControl> resource

| Attributes of <statsConfig> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| resourceID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described. |
| accessControlPolicyIDs | 1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| creationTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| expirationTime | 1 | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |

##### 5.2.x.2.2	Resource Type policyDecisionPoint

The <policyDecisionPoint> resource is a virtual resource because it does not have a representation. It is the child resource of the <accessControl> resource. When a RETRIEVE Request addresses the <policyDecisionPoint> resource, a PDP process is triggered. The access control decision request shall be included in the Content parameter of the RETRIEVE Request,  and the access control decision response shall be included in the Content parameter of the RETRIEVE Response.

The <policyDecisionPoint> resource inherits access control policies that apply to the parent <accessControl> resource.

##### 5.2.x.2.3	Resource Type policyRetrievalPoint

The <policyRetrievalPoint> resource is a virtual resource because it does not have a representation. It is the child resource of the <accessControl> resource. When a RETRIEVE Request addresses the <policyRetrievalPoint> resource, a PRP process is triggered. The access control policy request shall be included in the Content parameter of the RETRIEVE Request,  and the access control policy response shall be included in the Content parameter of the RETRIEVE Response.

The <policyRetrievalPoint> resource inherits access control policies that apply to the parent <accessControl> resource.

##### 5.2.x.2.4	Resource Type policyInformationPoint

The <policyInformationPoint> resource is a virtual resource because it does not have a representation. It is the child resource of the <accessControl> resource. When a RETRIEVE Request addresses the <policyInformationPoint> resource, a PIP process is triggered. The access control attribute request shall be included in the Content parameter of the RETRIEVE Request,  and the access control attribute response shall be included in the Content parameter of the RETRIEVE Response.

The <policyInformationPoint> resource inherits access control policies that apply to the parent <accessControl> resource.