| Input Contribution |
| --- |
| Meeting ID* | SEC#16 |
| Title:* | TR-00016 Procedures on Parent Resource for Distributed Authorization |
| Source:* | Wei Zhou, Datang, zhouwei@catt.cn Hui Xu, Datang, xuhui@catt.cn |
| Uploaded Date:* | 2015-03-16 |
| Document(s) Impacted* | SEC WI-0023, oneM2M-TR-0016 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TR-0016. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

1	Introduction

This contribution describes the management procedures on the parent resource defined for distributed authorization.

2	Proposal

### 6.2.x	Proposal Z: Using resource-based approach to implement distributed authorization

#### 6.2.x.1	Introduction

#### 6.2.x.2	Resources

#### 6.2.x.3	Procedures

##### 6.2.x.3.1	Introduction

This clause describes the management procedures for the <authorization> resource and its virtual child resources. These virtual child resources are <policyDecisionPoint>, <policyRetrievalPoint> and <policyInformationPoint> that are used to trigger a PDP process, a PRP process and a PIP process defined in oneM2M TS-0003 [2] respectively. Only Retrieve operation shall be allowed on these virtual resources.

##### 6.2.x.3.2	Create <authorization>

This procedure shall be used for creating a <authorization> resource.

Table 6.2.x.3.2-1: <authorization> CREATE

| <authorization> CREATE |
| --- |
| Associated Reference Point | Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 of oneM2M TS-0001 [1] apply with the specific details for: To: the address of the <CSEBase> where the <authorization> resource is intended to be Created. Content: attributes of the <authorization> resource as defined in clause 6.2.x.2.1-2 |
| Processing at Originator before sending Request | According to clause 10.1.1.1 of oneM2M TS-0001 [1] |
| Processing at Receiver | According to clause 10.1.1.1 of oneM2M TS-0001 [1]with the following additions: Upon successful validation of the provided attributes, the Hosting CSE creates the <authorization> resource including its virtual child resources specified in table 6.2.x.2.1-1 If there is a PDP process shall be bound to the <policyDecisionPoint> virtual resource, then bind it to the <policyDecisionPoint> virtual resource, otherwise leave the binding void. The PDP process and the binding method are out of scope If there is a PRP process shall be bound to the <policyRetrievalPoint> virtual resource, then bind it to the <policyRetrievalPoint> virtual resource, otherwise leave the binding void. The PRP process and the binding method are out of scope If there is a PIP process shall be bound to the <policyInformationPoint> virtual resource, then bind it to the <policyInformationPoint> virtual resource, otherwise leave the binding void. The PIP process and the binding method are out of scope |
| Information in Response message | According to clause 10.1.1.1 of oneM2M TS-0001 [1] |
| Processing at Originator after receiving Response | According to clause 10.1.1.1 of oneM2M TS-0001 [1] |
| Exceptions | According to clause 10.1.1.1 of oneM2M TS-0001 [1] |

##### 6.2.x.3.3	Retrieve <authorization>

This procedure shall be used for retrieving the attributes of a <authorization> resource.

Table 6.2.x.3.3-1: <authorization> RETRIEVE

| <authorization> RETRIEVE |
| --- |
| Associated Reference Points | Mcc and Mcc' |
| Information in Request message | According to clause 10.1.2 of oneM2M TS-0001 [1] |
| Processing at Originator before sending Request | According to clause 10.1.2 of oneM2M TS-0001 [1] |
| Processing at Receiver | According to clause 10.1.2 of oneM2M TS-0001 [1] |
| Information in Response message | According to clause 10.1.2 of oneM2M TS-0001 [1] |
| Processing at Originator after receiving Response | According to clause 10.1.2 of oneM2M TS-0001 [1] |
| Exceptions | According to clause 10.1.2 of oneM2M TS-0001 [1] |

##### 6.2.x.3.4	Update <authorization>

This procedure shall be used for updating the attributes of a <authorization> resource.

Table 6.2.x.3.4-1: <authorization> UPDATE

| <statsConfig> UPDATE |
| --- |
| Associated Reference Points | Mcc and Mcc' |
| Information in Request message | According to clause 10.1.3 of oneM2M TS-0001 [1] |
| Processing at Originator before sending Request | According to clause 10.1.3 of oneM2M TS-0001 [1] |
| Processing at Receiver | According to clause 10.1.3 of oneM2M TS-0001 [1] |
| Information in Response message | According to clause 10.1.3 of oneM2M TS-0001 [1] |
| Processing at Originator after receiving Response | According to clause 10.1.3 of oneM2M TS-0001 [1] |
| Exceptions | According to clause 10.1.3 of oneM2M TS-0001 [1] |

##### 6.2.x.3.5	Delete <authorization>

This procedure shall be used for deleting a <authorization> resource.

Table 6.2.x.3.5-1: <authorization> DELETE

| <statsConfig> DELETE |
| --- |
| Associated Reference Points | Mcc and Mcc' |
| Information in Request message | According to clause 10.1.4 of oneM2M TS-0001 [1] |
| Processing at Originator before sending Request | According to clause 10.1.4 of oneM2M TS-0001 [1] |
| Processing at Receiver | According to clause 10.1.4 of oneM2M TS-0001 [1] |
| Information in Response message | According to clause 10.1.4 of oneM2M TS-0001 [1] |
| Processing at Originator after receiving Response | According to clause 10.1.4 of oneM2M TS-0001 [1] |
| Exceptions | According to clause 10.1.4 of oneM2M TS-0001 [1] |