| Input Contribution |
| --- |
| Meeting ID* | SEC#16 |
| Title:* | Use case and requirements for End-to-End authentication |
| Source:* | Vinod Choyi, Interdigital, vinod.choyi@interdigital.com Dale Seed, Interdigital, dale.seed@interdigital.com |
| Uploaded Date:* | 2015-03-17 |
| Document(s) Impacted* | WI-0016, TR-0012 oneM2M End-to-End Security and Group Authentication |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Accept proposed definition for TR-0012 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1-------------------------------------------

  - Use case of End-to-End Authentication

    - Description

In an oneM2M system, entities may require service layer messaging in order to communicate with another entity that may be multiple hops away. Messages may traverse multiple intermediate entities before the message reaches the final destination (receiver). An entity may require a high-level of assurance that a message originated from a particular end entity. Current hop-by-hop security mechanisms do not meet the requirement and therefore an end-to-end security mechanism shall be adopted.

    - Actors

The entities involved in the use case are shown in Figure 1 and described as follows:

M2M Application: It represents an application that uses sensor data to perform certain application-specific operations. The M2M Application is multiple hops away from a sensor and may be connected to the sensor by entities that may belong to different administrative domains.

M2M Server: It represents an infrastructure entity that is responsible for enabling an M2M application to obtain services provided by the M2M service provider.

M2M Gateway: It represents a gateway that is responsible for processing and / or forwarding messages that are sent from an M2M Application and from M2M Devices.

M2M Device: It represents a sensor application or a sensor device that is responsible for measuring sensor data and communicating the data to an application.

Figure 1: Entities involved in oneM2M messaging

    - Pre-Conditions

The M2M Application, M2M Gateway, M2M Server and the M2M Device are all provisioned with appropriate credentials that may be used for authentication, message integrity protection, data integrity protection and data confidentiality protection.

M2M Device register with the M2M Gateway in order that an M2M Application may be able to access the sensor data provided by M2M Device.

    - Normal Flow

Procedure for oneM2M messaging:

- An M2M Application would like to subscribe to sensor data that is provided by an M2M Device. In order to obtain the data, the M2M Application sends a request message to the M2M Gateway via the M2M Server.

- The M2M Server receives the message and forwards the message to the appropriate M2M Gateway.

- The M2M Gateway on receiving the message from the M2M Server, must be able to verify with a high-degree of assurance that the message originated from the M2M Application. In addition, the M2M Gateway may also verify the message has not been tampered or modified by any intermediate entities (e.g. M2M Server). In order to verify the authentication of the message, the M2M Gateway performs an end-to-end authentication of the M2M Application based on the appropriate credentials. If the M2M Gateway is able to positively verify the authentication, the message from the application is processed by the M2M Gateway.

    - Potential Requirements

- M2M system shall support establishment of end-to-end security using provisioned end-to-end security credentials.

- M2M system shall support the capability to perform end-to-end  authentication.

### -----------------------End of change 1------------------------------------------------