| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#17 |
| Title:* | Group Authentication Architecture |
| Source:* | China Mobile |
| Contact: | Ziyao Cheng, China Mobile, chengziyao@chinamobile.com Minpeng Qi, China Mobile, qiminpeng@chinamobile.com Min Zuo, China Mobile, zuomin@chinamobile.com |
| Date:* | 2015-05-19 |
| Abstract:* | This contribution presents the architecture of static group authentication for the security TR-0012. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0016 |
| Document(s) Impacted* | Security TR (TR-0012) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into an appropriate section of the Security TR-0012. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

==================<Start of Change (New Text 1)>=================

#### 2.1	Normative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[x]  	oneM2M TS-0001 "Functional Architecture "

==================<End of Change 1>========================

==================<Start of Change (New Text 2)>=================

#### 3.3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

ASN	Application Service Node

ADN	Application Dedicated Node

==================<End of Change 2>========================

==================<Start of Change (New Text 3)>=================

# 6Candidate Architecture

## 6.1	Overview

The Candidate Architectures illustrate as follows:

### 6.1.1	Architecture of Static Group Authentication

Figure: 6.1.1-1:  Illustration of Architecture for Static Group Authentication

#### 6.1.1.1	Entities

For the architecture of static group authentication in Figure 6.1.1-1, there are three architectural components:

- ASN/ADN[x]: an M2M device assigned to a group by the M2M server initially, each M2M device in a given group shall carry out mutual authentication with MN.

- MN[x]: an M2M gateway which shall perform mutual authentication with the IN on behalf of all ASNs/ADNs in a given group, it could serve for multiple groups.

- IN[x]: an M2M server shall verify the MN’s identity and establish the security association with each M2M device in a given group.

NOTE: When the authentication procedure begins, the M2M devices in a given group (e.g. ASN/ADN) will not be changed until the end of this communication session.

#### 6.1.1.2	Reference Points

There are two reference points in the Group Based Authentication Architecture:

- the Mca/Mcc reference point [x] between the ADN/ASN and the MN.

- the Mcc reference point [x] between the MN and the IN.

==================<End of Change 3>========================