| Input Contribution |
| --- |
| Meeting ID* | SEC 18 |
| Title:* | SE reference point |
| Source:* | Giesecke & Devrient, Claus [dot] Dietze [@] gi-de[dot]com |
| Uploaded Date:* | 2015-07-24 |
| Document(s) Impacted* | WI-0021 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussion and decision to include the content into TS-0016 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## 7.2	Mcs reference point

### 7.2.1	Secure Environment Identifier (M2M-SE-ID)

M2M nodes may contain multiple Secure Environments each associated with a corresponding Secure Environment Identifier (M2M-SE-ID). Each SE contains several M2M Security Services, i.e. sensitive functions and sensitive data. The M2M-SE-ID is assigned to each Secure Environment.

Table 7.2.1-1: Secure Environment Identifier

| Identifier | Assigned by | Assigned to | Assigned during | Lifetime | Uniqueness | Used during |
| --- | --- | --- | --- | --- | --- | --- |
| M2M Secure Environment Identifier | M2M SE Provider | Secure Environment | Pre- or remote Provisioning or during manufacturing | Life of the M2M Service Registration. | Global per SE and per class of SE | communication establishment with and selection of SE; |

M2M-SE-ID is structured as follows:

Type of SE followed by unique ID, where type of SE is defined as given in table 7.1.1-2 and the unique ID is defined as described in Table 7.1.1-1.

Table 7.2.1-2: Type of Secure Environment

| Class of SE | Type of Secure Environment | Coding |
| --- | --- | --- |
| Hardware | UICC | Tbd |
| Software | Security Library | Tbd |
| ... |  |  |

Editor’s note: further types and classes tbd

Editor’s note: relation between SE-ID and node-ID is FFS. Definition of M2M Service Registration to be added.

## 7.3	SE Discovery and Selection

### 7.3.1	getSecureEnvironment

#### 7.3.1.1	Description

This service provides a list of available Secure Environments within the present M2M node including the SE class and type.

#### 7.3.1.2	Pre-Conditions

Type and Class of SE has been assigned during pre-provisioning or remote provisioning.

#### 7.3.1.3	Signature – getSecureEnvironment

Table 7.3.1.3-1: getSecureEnvironment

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId / cseId | IN | NO | Application Entity or CSE ID requesting the list of SE-IDs |
| applicationId | IN | NO | Application Identifier (App-ID) for the AE |
| responseType | OUT | NO | Response types: List of available SEs incl. their M2M-SE-IDs and their provided security level SEs do not exist |

Editor’s note: separate access from local entity and remote entities and inclusion of CSEs are for further study.

### 7.3.2	getSEFunctions

#### 7.3.2.1	Description

This service provides a list of available sensitive functions provided by a given SE.

#### 7.3.2.2	Pre-Conditions

M2M-SE-ID is known to the calling entity (getSecureEnvironment).

#### 7.3.2.3	Signature – getSEFunctions

Table 7.3.2.3-1: getSEFunctions

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| seId | IN | NO | M2M-SE-Identifier |
| applicationId | IN | NO | Application Identifier (App-ID) for the AE |
| responseType | OUT | NO | Response types: List of available sensitive functions No sensitive function available (but SE exists) SEs do not exist |

### 7.4.1	selectSecureEnvironment

#### 7.4.1.1	Description

Selects a particular SE available within the present entity.

#### 7.4.1.2	Pre-Conditions

Not applicable.

#### 7.4.1.3	Signature – selectSecureEnvironment

Table 7.4.1.3-1: selectSecureEnvironment

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| seId | IN | conditional | M2M-SE-ID |
| secLevel | IN | conditional | Types: SE with highest available security level to be selected SE with a particular security level to be selected |
| responseType | OUT | NO | Response types: Security level of selected SE together with seId Security level or selected SE does not exist |
| Note: conditional is to be interpreted as mandatory if no other conditional parameter does exist. |

## 7.5	Secure Environment Management

## 7.6	Sensitive Data Storage

## 7.7	Sensitive Cryptographic Functions

## 7.8	Secure Connection Establishment

## 7.9	Authentication and Identification