| CHANGE REQUEST |
| --- |
| Meeting:* | SEC 18 |
| Source:* | Vinod Choyi, Interdigital, vinod.choyi@interdigital.com Yogendra Shah, InterDigital, yogendra.shah@interdigital.com |
| Date:* | 2015-07-12 |
| Contact:* | Same as above |
| Reason for Change/s:* | Definitions for End-to-End Data Security |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | X Active WI-0016 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0012 oneM2M End-to-End Security and Group Authentication |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality X New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO X This CR is a mirror CR? YES NO X if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

In an oneM2M system, entities may require service layer messaging in order to communicate with another entity that may be multiple hops away. Messages may traverse multiple intermediate entities before the message reaches the final destination (receiver). An entity (receiver) would like to ensure that the data has not been modified by unauthorized entities and to also verify that the authenticity of the data originator (e.g. data producer or data owner  or data hosting entity ), in addition, the originator would like to be assured that only authorized entities are able to read / process the data in a meaningful manner.

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in [i.2] and the following apply:

End-to-End Data Integrity Protection: Provides the ability for an entity (e.g. data / content owner or generator) to integrity protect data / content. The integrity protected data may be transported over multiple hops consisting of trusted or untrusted communication entities. An authorized consumer of the data shall be able to verify the integrity of data and also shall be able to verify the originator of the data. Such a protection mechanism would ensure that the data is integrity protected “at-rest” and “in-transit” when handled by intermediate nodes.

End-to-End Data Confidentiality Protection: Provides the ability for an entity (e.g. data / content owner or generator) to provide for confidentiality protection of data / content. The confidentiality protected data may be transported over multiple hops consisting of trusted or untrusted communication entities. Only authorized entities can decrypt the confidentiality protected data. Such a protection mechanism would ensure that the data is confidentiality protected “at-rest” and “in-transit” when handled by intermediate nodes.

Editor Node: the definitions are subject to further refinement.

NOTE:	This may contain additional information.

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?