| CHANGE REQUEST |
| --- |
| Meeting:* | SEC 18 |
| Source:* | Vinod Choyi, Interdigital, vinod.choyi@interdigital.com |
| Date:* | 2015-07-12 |
| Contact:* | Same as above |
| Reason for Change/s:* | Use case and requirements for providing End-to-End Data Integrity |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | X Active WI-0016 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0012 oneM2M End-to-End Security and Group Authentication |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality X New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO X This CR is a mirror CR? YES NO X if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

In an oneM2M system, entities may require service layer messaging in order to communicate data / content with another entity that may be multiple hops away. Messages that carry data / content may traverse multiple intermediate entities before the message reaches the final destination (receiver). An entity (receiver) would like to ensure that the data has not been modified by unauthorized entities and to also verify that the authenticity of the data originator (e.g. data producer or data owner  or data hosting entity ).

### -----------------------Start of change 1-------------------------------------------

## Use case of End-to-End Data Integrity

### 5.6.1	Description

In an oneM2M system, entities may require service layer messaging in order to communicate data / content with another entity that may be multiple hops away. Messages that carry data / content may traverse multiple intermediate entities before the message reaches the final destination (receiver). An entity (receiver) would like to ensure that the data has not been modified by unauthorized entities and to also verify that the authenticity of the data originator (e.g. data producer or data owner  or data hosting entity ).

### 5.6.2		Actors

The entities involved in the use case are shown in Figure 5.5.2-1 and described as follows:

M2M Application: An application that uses sensor data to perform certain application-specific operations. The M2M Application is multiple hops away from a sensor and may be connected to the sensor by entities that may belong to different administrative domains.

M2M Server: An infrastructure entity that is responsible for enabling an M2M application to obtain services provided by the M2M service provider.

M2M Gateway: A gateway that is responsible for processing and / or forwarding messages that contain sensor data to the M2M Application from M2M Devices. The M2M Gateway may host the data on behalf of the M2M device.

M2M Device: It represents a sensor application or a sensor device that is responsible for measuring sensor data and providing the data that may be hosted on the device or another entity (e.g. M2M Gateway) so that the data is made accessible to an M2M Application.

Trusted Third-Party (TTP): It represents an entity that can broker trust relationships between entities that may belong within the same administrative domain or outside. The TTP may also facilitate in providing credential registration as well as credential requisition services.

Figure 5.5.2-1: Entities involved in oneM2M messaging

### 5.6.3	Pre-Conditions

M2M Device registers with the M2M Gateway in order that an M2M Application may be able to access the sensor data provided by M2M Device and optionally hosted on the M2M Gateway or at the M2M Device.

M2M Device registers the credentials used for integrity protection with the M2M Gateway or with a Trusted Third-Party (TTP)

If an M2M Gateway is hosting the data, then it registers the credentials used for integrity with another M2M Gateway or TTP

An authorized M2M Application is provisioned with appropriate credentials that is used for verifying the integrity / authenticity of the data.

### Normal Flow

Procedure for oneM2M messaging:

- An M2M Device registers its sensor data with an M2M Gateway

- The M2M Gateway based on policies and security requirements determines that the data has to be protected for integrity / authenticity using cryptographic mechanisms and therefore may generate appropriate credentials, identifiable by a credential identifier and registers the credentials with a TTP. Alternatively, the M2M Gateway may request for appropriate credentials from the TTP, which is then used for protecting the data for integrity / authenticity.

- An M2M Application would like to subscribe to sensor data that is provided by an M2M Device. In order to obtain the data, the M2M Application sends a request message to the M2M Gateway via the M2M Server.

- The M2M Server receives the message and forwards the message to the appropriate M2M Gateway.

- The M2M Gateway on receiving the message from the M2M Server verifies if the M2M Application is authorized to send the request message.

- Upon verification, the M2M Gateway sends the integrity protected sensor data that is hosted on the M2M Gateway to the M2M Server.

- The M2M Server forwards the sensor data to the M2M Application.

- Based on the type of credentials (symmetric or assymetric) that has been used for integrity protection the M2M Application may or may not be able to verify the integrity / authenticity of the sensor data. If the M2M Application does not have the appropriate credentials, identified by the credential identifier, it requests for the credentials with the TTP.

- The TTP checks for the authorization of the M2M Application, if authorized, the TTP provisions the M2M Applciation with the appropriate credentials using the credential identifier.

- The M2M Application is able to verify the integrity / authenticity of the sensor data and processes it.

### 5.6.5	Potential Requirements

- M2M system shall enable mechanisms to support the establishment of end-to-end data integrity using end-to-end security credentials

- M2M system shall support the ability to request End-to-End data integrity credentials

- M2M system shall support the ability to register End-to-End data integrity credentials

- M2M system shall support the ability to generate and host End-to-End integrity protected data

- M2M system shall support the ability to process End-to-End integrity protected data

### -----------------------End of change 1 ---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?