| CHANGE REQUEST |
| --- |
| Meeting:* | SEC 18 |
| Source:* | Vinod Choyi, Interdigital, vinod.choyi@interdigital.com |
| Date:* | 2015-07-12 |
| Contact:* | Same as above |
| Reason for Change/s:* | Use case and requirements for providing End-to-End Data Integrity and Data Confidentiality R01 addresses comments brought up duing SEC session on combining the use cases / requirements for both integrity and confidentiality |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | X Active WI-0016 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0012 oneM2M End-to-End Security and Group Authentication |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality X New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO X This CR is a mirror CR? YES NO X if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

In an oneM2M system, entities may require service layer messaging in order to communicate data with another entity that may be multiple hops away. Messages that carry data may traverse multiple intermediate entities before the message reaches the final destination (receiver). An entity (receiver) would like to ensure that the data has not been modified by unauthorized entities and to also verify that the authenticity of the data originator (e.g. data producer or data owner  or data hosting entity ). In addition, the data originator (e.g. data producer or data owner or data hosting entity) would like to ensure that only authorized entities are able to view and process the data. The data originator may like to ensure that even the hosting entity and intermediate nodes are not able to view or process the data and also protect the data at rest.

### -----------------------Start of change 1-------------------------------------------

## Use case of End-to-End Data Integrity

### 5.6.1	Description

In an oneM2M system, entities may require service layer messaging in order to communicate data with another entity that may be multiple hops away. Messages that carry data may traverse multiple intermediate entities before the message reaches the final destination (receiver). An entity (receiver) would like to ensure that the data has not been modified by unauthorized entities and to also verify that the authenticity of the data originator (e.g. data producer or data owner  or data hosting entity ). In addition, an entity that generates, owns or hosts data would like to make sure that only authorized entities are able to view and process the data. The entity in some cases, would like to ensure that even a hosting entity is not able to view and process the data and also ensure that unauthorized intermediate entities are not able to view and process the data.

### 5.6.2		Actors

The entities involved in the use case are shown in Figure 5.5.2-1 and described as follows:

M2M Application: An application that uses sensor data to perform certain application-specific operations. The M2M Application is multiple hops away from a sensor and may be connected to the sensor by entities that may belong to different administrative domains.

M2M Server: An infrastructure entity that is responsible for enabling an M2M application to obtain services provided by the M2M service provider.

M2M Gateway: A gateway that is responsible for processing and / or forwarding messages that contain sensor data to the M2M Application from M2M Devices. The M2M Gateway may host the data on behalf of the M2M device.

M2M Device: It represents a sensor application or a sensor device that is responsible for measuring sensor data and providing the data that may be hosted on the device or another entity (e.g. M2M Gateway) so that the data is made accessible to an M2M Application.

Trusted Third-Party (TTP): It represents an entity that can broker trust relationships between entities that may belong within the same administrative domain or outside. The TTP may also facilitate in providing credential registration as well as credential requisition services.

Figure 5.5.2-1: Entities involved in oneM2M messaging

### 5.6.3	Pre-Conditions

M2M Device registers with the M2M Gateway in order that an M2M Application may be able to access the sensor data provided by M2M Device and optionally hosted on the M2M Gateway or at the M2M Device.

If the M2M Device is hosting the data, then it registers the appropriate end-to-end data integrity credentials used for integrity protection and appropriate end-to-end data confidentiality credentials used for confidentiality protection with the M2M Gateway or with a Trusted Third-Party (TTP).

If an M2M Gateway is hosting the data, then it registers the appropriate end-to-end data integrity credentials used for integrity protection and the appropriate end-to-end data confidentiality credentials used for confidentiality protection with another M2M Gateway or with a TTP

An authorized M2M Application is provisioned with appropriate end-to-end data integrity credentials that is used for verifying the integrity / authenticity of the data and appropriate end-to-end data confidentiality credentials for decrypting the confidentiality protected data.

### Normal Flow

Procedure for oneM2M messaging, where the M2M Gateway performs integrity protection and confidentiality protection on behalf of the M2M Device:

- An M2M Device registers its sensor data with an M2M Gateway

- The M2M Gateway based on policies and security requirements determines that the data has to be protected for integrity / authenticity and / or confidentiality using cryptographic mechanisms and therefore may generate appropriate credentials, identifiable by credential identifiers and registers the credentials with a TTP. Alternatively, the M2M Gateway may request for appropriate end-to-end data integrity credentials from the TTP, which is then used for protecting the data for integrity / authenticity and appropriate data confidentiality credentials for confidentiality protecting the data. The M2M Gateway hosts the integrity protected and / or confidentiality protected data.

- An M2M Application would like to subscribe to sensor data that is provided by an M2M Device. In order to obtain the data, the M2M Application sends a request message to the M2M Gateway via the M2M Server.

- The M2M Server receives the message and forwards the message to the appropriate M2M Gateway.

- The M2M Gateway on receiving the message from the M2M Server verifies if the M2M Application is authorized to send the request message.

- Upon verification, the M2M Gateway sends the integrity and confidentiality protected sensor data that is hosted on the M2M Gateway to the M2M Server.

- The M2M Server forwards the sensor data to the M2M Application.

- Based on the type of credentials (symmetric or assymetric) that has been used for integrity protection the M2M Application may or may not be able to verify the integrity / authenticity of the sensor data. If the M2M Application does not have the appropriate end-to-end data integrity credentials for verifying the integrity/authenticity of the data, identified by the credential identifier, it requests for the appropriate credentials with the TTP. Similarly, if the M2M Application does have the appropriate end-to-end data confidentiality credentials for decrypting the data, it requests for the appropriate credentials, identitfied by the credential identifier with the TTP.

- The TTP checks for the authorization of the M2M Application, if authorized, the TTP provisions the M2M Applciation with the appropriate end-to-end data integrity and end-to-end data confidentiality credentials based on  the credential identifiers.

- The M2M Application is able to verify the integrity / authenticity of the sensor data and processes it. The M2M Application is able to decrypt the sensor data.

### 5.6.5	Potential Requirements

- M2M system shall support the ability to provide and verify end-to-end data integrity and authenticity at-rest.

- M2M system shall support the ability to provide end-to-end data confidentiality at-rest

- M2M system shall ensure that the end-to-end data credentials are protected for confidentiality, integrity and against tampering.

- The M2M system shall ensure that the end-to-end data credentials are protected from exposure to intermediate entities

### -----------------------End of change 1 ---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?