| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#17 |
| Title:* | Group Authentication Solution |
| Source:* | China Mobile |
| Contact: | Ziyao Cheng, China Mobile, chengziyao@chinamobile.com Minpeng Qi, China Mobile, qiminpeng@chinamobile.com Min Zuo, China Mobile, zuomin@chinamobile.com |
| Date:* | 2015-07-23 |
| Abstract:* | This contribution presents the description of group authentication solution for the static group in the security TR-0012. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0016 |
| Document(s) Impacted* | Security TR (TR-0012) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into an appropriate section of the Security TR-0012. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

==================<Start of Change (New Text 1)>=================

#### 3.2	Symbols

For the purposes of the present document, the following symbols apply:

||	Concatenation

#### 3.3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

IdAx           	Identifier for Entity Ax

IdAy           	Identifier for Entity Ay

IdB                	Identifier for Entity B

IdC                   	Identifier for Entity C

Kpsa        	Provisioned Credential for M2M Security Association Establishment

KpsaId                	Provisioned Credential for M2M Security Association Establishment Identifier

Ks                     	M2M Group Secure Connection Key

KsId                  	M2M Group Secure Connection Key Identifier

Rand	Random Number Generated by the Infrastructure Node

MN	Middle Node

IN	Infrastructure Node

==================<End of Change 1>==========================

==================<Start of Change (New Text 2)>=================

#### 2.1	Normative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[]  	oneM2M TS-0003 "Security Solutions"

[2]	IETF RFC 4279 "Pre-Shared Key Ciphersuites for Transport Layer Security (TLS) "

[3]	"Unicode Standard Annex #15; Unicode Normalization Forms", Unicode 5.1.0, March 2008. http://www.unicode.org

[4] 	IETF RFC 2014 "HMAC: Keyed-Hashing for Message Authentication"

[5]	IETF RFC 3629 "UTF-8, a transformation format of ISO 10646"

==================<End of Change 2>==========================

# ==================<Start of Change (New Text 3)>=================8	Available Options

## 8.2   Group Authentication

### 8.2.1  Group Authentication Solution 1

Figure 8.1.2-1 illustrates the sequence of events when using the group authentication solution 1 for the static group which corresponding to Clause 6.1.1. In this description, "Entity Ax" or "Entity Ay" corresponds to either a CSE or AE in a group, "Entity B" corresponds to MN-CSE, and "Entity C" corresponds to IN-CSE.

Credential Configuration: The Provisioned Credential for M2M Security Association Establishment (Kpsaxm, Kpsaym, Kpsami, Kpsaxi, and Kpsayi) and the corresponding Provisioned Credential for M2M Security Association Establishment Identifier, denoted KpsaxmId, KpsaymId, KpsamiId, KpsaxiId, and KpsayiId are provisioned to both entities either with pre-provisioning or remote provisioning.

NOTE 1: The provisioning (by definition) uses mechanisms not specified by oneM2M. The remote provisioning is performed thanks to Security Bootstrap Frameworks described in clause 8.3 in TS0003 [1].

NOTE 2: Entity Ax, Entity Ay, Entity B, and Entity C shall be configured with the information needed for the authentication and identification during the Inner/Outer Group Authentication and Group Security Association Handshake. For instance, Entity Ax is configured with Entity B identity (IdB) associated with the Provisioned Credential for M2M Security Association Establishment identifier KpsaxmId to establish security context by using Kpsaxm. Entity Ax is to use this identity IdB for Entity B authenticating using the related arguments. This identity is also used to route the (D)TLS exchange.

Inner Group Authentication:

- Each Entity Ax (or Ay) in a group and the Entity B perform a (D)TLS-PSK handshake [2] to establish a secure session:

Take Entity Ax as example:

  - The "psk_identity" parameter [2] is set to the value of the Provisioned Credential for M2M Security Association Establishment identifier KpsaxmId between the Entity Ax and the Entity B.

  - The "psk" parameter [2] is set to the value of the Provisioned Credential for M2M Security Association Establishment Kpsaxm between the Entity Ax and the Entity B.

- The Entity Ax and the Entity B authenticate each other by verifying Message Integrity Codes (MIC) which was generated using the symmetric key (Kpsaxm) to make mutual authentication.

NOTE 3: Each Entity in a group shall perform inner group authentication with the Entity B.

NOTE 4: This is just an example to use (D)TLS-PSK here, it is not limited to (D)TLS-PSK only.

Outer Group Authentication: Due to the successful Inner Group Authentication, Entity B could be on behalf of all entities in the group to make mutual authentication with the Entity C.

- The Entity B and Entity C perform a (D)TLS-PSK handshake [2] to establish a secure session:

  - The "psk_identity" parameter [2] is set to the value of the Provisioned Credential for M2M Security Association Establishment identifier KpsamiId between the Entity B and the Entity C.

  - The "psk" parameter [2] is set to the value of the Provisioned Credential for M2M Security Association Establishment Kpsami between the Entity B and the Entity C.

- The Entity B and Entity C authenticate each other by verifying Message Integrity Codes (MIC) which was generated using the symmetric key (Kpsami) to make mutual authentication. After that, each Entity in the group has carried out the authentication with the help of the Entity B.

- The Entity C generates the M2M Group Secure Connection Key for each Entity in the group. Especially, in the IN’s database, there is a mapping between the identifier of MN (e.g. IdB) and each Entity’s identifier (e.g. IdAx) in the group. For instance, Entity C generates Ksx for Entity Ax from the Provisioned Credential (Kpsaxi) between the Ax and C, a random number (Rand) and the identifier of Ax (IdAx). Moreover, Entity C sets the Group Secure Connection Key Identifier (KsxId) equal to KpsaxiId, and stores the M2M Group Secure Connection Key (Ksx) and the related Identifier (KsxId).

NOTE 5: The derivation of the M2M Group Secure Connection Key, e.g. Ksx := HMAC-SHA-256(Kpsaxi, “oneM2M Group Secure Connection Key derivation” ||  Enrolee-Ax-ID || Rand), where Kpsaxi is the value of the Provisioned Credential between the Enrolee Ax and the IN; Rand is a random number generated by the Entity C; Enrolee Ax’s CSE-ID or AE-ID (Enrolee-Ai-ID), which shall be encoded to an octet string according to UTF-8 encoding rules as specified in IETF RFC 3629 [5] and apply Normalization Form KC (NFKC) as specified in [3]; HMAC-SHA-256 is defined in RFC 2014 [4].

Group Security Association Handshake: The Group Security Association Handshake enables the establishment of the M2M Group Secure Connection Key (e.g. Ksx) and the associated Key Identifier (e.g. KsxId) shared between each Entity Ax (or Ay) in the group and the Entity C.

Take Entity Ax as example:

- Entity C sends the random number (Rand) to Entity B.

- Entity B forwards the Rand to the Entity Ax.

- Entity Ax generates the M2M Group Secure Connection Key (Ksx) from the Provisioned Credential (Kpsaxi) between the Entity Ax and the Entity C, the random number (Rand) and the identifier of Ai (IdA), sets the Group Secure Connection Key Identifier (KsxId) is KpsaxiId, and stores the M2M Group Secure Connection Key (Ksx) and the related Identifier (KsxId). After that, Entity Ax sends the Service Request Message to Entity B.

- Entity B forwards the Service Request Message to Entity C.

NOTE 6: The Service Request Message is sent by the entity in a given group when the entity requires the IN to provide the services.

- Upon the Service Request Message, Entity B forwards this message to IN.

NOTE 7: After each Entity in a group (e.g. Ax) sets up security association with IN using the same key (e.g. Ksx), each Entity could be seen as authenticated when the security association works, since the mutual authentication between each Entity (e.g. Ax) and the IN is fulfilled through the proof of possessing the M2M Group Secure Connection Key (e.g. Ksx).

Figure: 8.1.2-1: The sequence of events When using Group Authentication Solution 1

==================<End of Change 3>========================