| Input Contribution |
| --- |
| Meeting ID* | SEC#18 |
| Title:* | SEC-2015-0565-TR-0019_Access_Token_Use_Case_for_Dynamic_Authorization |
| Source:* | Wei Zhou, Datang, zhouwei@catt.cn Hui Xu, Datang, xuhui@catt.cn Peng Wang, China Unicom, wangpeng@chinaunicom.cn |
| Uploaded Date:* | 2015-07-20 |
| Document(s) Impacted* | SEC WI-0019, oneM2M-TR-0019 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TR-0016. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

1	Introduction

This contribution provides a use case about dynamic authorization and corresponding requirements for TR-0019.

2	Proposal

## 5.x	Use Case for Access Token in Dynamic Authorization

### 5.x.1	Description

In a oneM2M System the Platform, Gateways and Devices interact each other in the way of many-to-many, furthermore many of these relations may be dynamic and temporary. So the access control mechanism used by the M2M System shall be flexible and efficient.

The use case in the following sections shows using dynamically issued access tokens that carry authorization information to simplify the access control management. In this use case the mobile phone of a tourist is issued with access tokens in which there are access privileges to the resources of  M2M Gateways/Devices. The tourist then can use these access tokens to access various M2M Gateways or Devices in the hotel or attractions, such as accessing his/her room, operating electric devices in the room, accessing the VIP area, using the facilities in fitness center, renting bicycle, or using some tourist facilities in the attractions. If using the traditional way, i.e. the privileges are placed in the local stored access control policies, all the access control policies in the gateways or devices related to this tourist shall be  updated. As there are so many tourists coming and going, the workload of modifying and uploading access control policies will be very large if it's not impossible.

### 5.x.2	Actors

The entities involved in this use case are shown in the Figure 5.x.2-1 and described as follows:

M2M Platform: It represents an infrastructure entity that interacts with M2M Gateways/Devices and M2M Application for providing common functionalities. In this use case the M2M Platform provides communication path between two M2M Gateways/Devices that do not have registration relation.

Token Issuer: It represents a M2M Gateway that is responsible for issuing access tokens to other M2M Gateways/Devices.

Mobile Phone: It represents a M2M Device held by a tourist. Access tokens are issued to the mobile phone, and the tourist uses it to interact with other M2M Gateways/Devices.

M2M Gateway: It is responsible for caching and forwarding the messages exchanging between the M2M Platform and target M2M Devices. It also acts as a control center that stores various information related to the M2M Devices that have registered to it.

M2M Device: It represents various M2M devices such as lock of door, fitness equipment, lock of the bicycle, smart TV, facility for tourists at attractions and so on.

Figure 5.x.2-1: Using token to carry authorization information

### 5.x.3	Pre-conditions

The issuer (M2M Gateway 1) of access tokens is provisioned with security credentials that are used for providing integrity and confidentiality protection for access tokens.

Other M2M Gateways are provisioned with security credentials that are used for verifying received access tokens.

### 5.x.4	Normal Flow

The procedure of issuing and using access tokens is:

- A tourist registers his/her mobile phone as a M2M Device with the M2M Gateway 1 at the hotel reception. The M2M Gateway 1 also plays the role of token issuer.

- The token issuer issues one or multiple access tokens to the mobile phone according to the services booked by the tourist. Inside the tokens there are some authorization information describing what privileges are assigned to the mobile phone (M2M Device).

The tourist then can use these access tokens to access various M2M Gateways or Devices in the hotel through his/her mobile phone, such as accessing his/her room, operating electric devices in the room, accessing the VIP area, using the facilities in fitness center, renting bicycle, or using some tourist facilities in the attractions.

- When the tourist arrives some sites such as door of room, the mobile phone may detect a M2M Gateway or a M2M Device with which the mobile can contact. The mobile phone then establishes security association with the detected device via the M2M Gateway 1 and M2M Platform. After that a resource access request with appropriate access tokens are sent to the M2M Gateway/Device.

- The M2M Gateway/Device verifies the access tokens sent by the mobile phone, extracts the privileges from the token, and evaluates the access request with the privileges. If it is permitted, the M2M Gateway/Device executes the requested operation on the target resource.

### 5.x.5	Potential requirements

- The M2M entity shall be able to issue access tokens that describe what privileges are assigned to the holder of access tokens for accessing the resources in the local or other M2M entities.

- The M2M System shall provide authentication, integrity and confidentiality protection for access tokens.

- The M2M System shall be able to revoke the access tokens that are not yet expired.