| Input Contribution |
| --- |
| Meeting ID* | SEC#18 |
| Title:* | TR-0019 A Proposal of Token Issuance Resource Definition Part |
| Source:* | Wei Zhou, Datang, zhouwei@catt.cn Hui Xu, Datang, xuhui@catt.cn |
| Uploaded Date:* | 2015-07-20 |
| Document(s) Impacted* | SEC WI-0019, oneM2M-TR-0019 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TR-0019. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

1	Introduction

This contribution provides a solution about access token issuance and use in oneM2M Dynamic Authorization System.

2	Proposal

## 8.x	Proposal N: A Solution of Access Token Issuance and Use

### 8.x.1	Access Token Issuance Architecture

### 8.x.2	General Procedure of Token Issuance and Use

### 8.x.3	Resource Definitions for Token Issuance

#### 8.x.3.1	Resource Type accessTokens

The <accessTokens> resource represents the method for providing the services related to access token issuance. The <accessTokens> resource shall be located directly under <CSEBase>.

Figure 8.x.3.1-1: Structure of <accessTokens> resource

The <accessTokens> resource shall contain the child resources specified in table 8.x.3.1-1.

Table 8.x.3.1-1: Child resources of <accessTokens> resource

| Child Resources of <authorization> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <accessTokenIssuing> | 1 | See clause 8.x.3.2 |
| [variable] | <accessToken> | 0..n | See clause 8.x.3.3 |

The <accessTokens> resource shall contain the attributes specified in table 8.x.3.1-2

Table 8.x.3.1-2: Attributes of <accessTokens> resource

| Attributes of <statsConfig> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| resourceID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described. |
| authorizationPolicyIDs | 1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| creationTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| expirationTime | 1 | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |

#### 8.x.3.2	Resource Type accessTokenIssuing

The <accessTokenIssuing> resource is a virtual resource because it does not have a representation. It is the child resource of the <accessTokens> resource. When a CREATE Request addresses the <accessTokens> resource, an access token issuance process is triggered. The access token request shall be included in the Content parameter of the CREATE Request,  and the access token response shall be included in the Content parameter of the CREATE Response.

The <accessTokenIssuing> resource inherits access control policies that apply to the parent <accessTokens> resource.

#### 8.x.3.3	Resource Type accessToken

The <accessToken> resource represents M2M Access Token information that is created by an access token insurance process. The <accessToken> resource is the child resource of the <accessTokens> resource.

Figure 8.x.3.1-1: Structure of <accessTokens> resource

The  <accessToken> resource shall contain the attributes specified in table 8.x.3.3-1.

Table 8.x.3.3-1: Attributes of <accessToken> resource

| Attributes of <statsConfig> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| resourceID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described. |
| resourceName | 1 | WO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described. |
| parentID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described. |
| creationTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| expirationTime | 1 | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| labels | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [1] where this common attribute is described |
| issuer | 1 | RO | This attribute contains the identifier of the token issuer. |
| holder | 1 | RO | This attribute contains the identifier of the token holder. |
| token | 1 | RO | This attribute contains the access token itself. |